大葉大學九十二學年度第一學期總複習

| 課目名稱 | 授課老師 | 系級 | 學號 | 姓名 | 成績 |
| --- | --- | --- | --- | --- | --- |
| 積體電路設計導論 Introduction to IC Design | 黃宗柱 T.-C. Huang | 資工研一、大四 |  |  |  |

- True or False：

(	)	1.	The static power dissipation does not matter with frequency.

(	)	2.	IC test is usually unable to change the yield.

(	)	3.	P-MOS transistors are good switches for low-voltage.

(	)	4.	The body effect and the stack effect describe the same thing.

(	)	5.	Usually, the stick diagram describes the position rather than the thickness.

(	)	6.	For all primitives, the Euler paths can be implemented by two non-interlaced diffusion lines.

(	)	7.	Channel routing algorithms for PCB are implanted from those from VLSI.

(	)	8.	The sheet resistance of silicide is greater than that of polysilicon.

(	)	9.	Chip sizes can fit the Moore’s Law.

(	)	10.	To prevent from the breakdown, the diffusion density tends to be doped heavier.

(	)	11.	To prevent from the drain breakdown, the gate-drain spacing should be longer.

(	)	12.	Usually, implantation for active region can be faster than diffusion.

(	)	13.	Active region is the intersection of Gpolysilicon and diffusion region.

(	)	14.	The DRCs usually take the conservative limitation.

(	)	15.	The LVS algorithms usually take the schematic symbol as comparative objects.

(	)	16.	In SPICE simulation, .AC DEC 10 1K 1G takes loger than .TRAN 1p 1m.

(	)	17.	For matched layout, the matched pair of transistors are usually drawn symmetrically.

(	)	18.	To prevent from the thermo-radial errors, some devices are laid as centroid.

(	)	19.	Cross couple matched layout is usually used to reduce the shifting and gradient errors.

(	)	20.	The sheet resistance of a 10um x 10um poly is 100 times that of a 1um x 1um poly.

(	)	21.	Guard rings can effectively reduce the latch-up effect due to noise.

(	)	22.	To prevent from the latch-up effect, the well-contacts should be closer to each active region.

(	)	23.	The SOI process can effectively reduce the static power dissipation for CMOS circuits.

(	)	24.	Micron rules in scaling can be easily calculated out by hand.

(	)	25.	Reverse engineering is illegal.

(	)	26.	The transistor in saturation usually acts as a dynamic resistor so that the saturation region is also called VCR region.

(	)	27.	Usually, the depletion mode nMOS has a positive threshold voltage, but the enhancement negative.

(	)	28.	A bulk-biased MOS looks like a channel JFET.

(	)	29.	H-tree routes can reduce the clock jitters.

(	)	30.	Usually, layout includes floorplanning, partitioning, placement and routing.

- Multiple Choice：

(	)	1.	The P:N transistor-size for a pseudo-nMOS equal-noise-margin inverter is about  1:2  2:1  1:6  6:1.

(	)	2.	The yields of chips with areas 1:2:3 are Y1, Y2, and Y3 with the rest conditions controlled,  Y1<Y2<Y3  Y1+Y2 > 2Y3  Y1=Y2=Y3  Y1+Y2 = 2Y3.

(	)	3.	The corners of the transfer function of an inverter are at (2V, 4.8V) and (3V, 0.4V). The low-level noise margin is about  2.8  1.8  2.6  1.6 V.

(	)	4.	To observe the bode-plot of a linear circuit with Req=15K, C1=1nF, C2=100pF, which analysis is proper?  .TRAN 1ps 1us  .DC Vs 1 5  .AC DEC 10 0.1G  .AC DEC 10K 1G.

(	)	5.	The sheet resistances of metal, diffusion, silicide and n-well are Rm, Rd, Rs, Rn.  Rm<Rd<Rs<Rn  Rm>Rd>Rs>Rn  Rm>Rn>Rd>Rs  Rm<Rs<Rd<Rn.

(	)	6.	The transfer function of the circuit XOR(NOR(A,A),NAND(A,A)) looks like    _─_ └┐┌┘  -_- .

(	)	7.	A CMOS inverter connected its output to its input may oscillate have an intermediate voltage  latch a value  have a high-Z output.

(	)	8.	According to the minimum interlace algorithm, the standard Eular-path layout of aoi2222 has at least  0  1  2  3 interlace(s).

(	)	9.	The delay time of a unit-size CMOS inverter will be  > tr+tf  < (tr+tf)/2  >(tr+tf)/2  <(tr+tf)/3.

(	)	10.	Which method must not solve the clock skew problem?  inserting buffer  using H-tree  reverse clocking to data stream  improving the clock generator.

(	)	11.	Which is not a complete logic set? {and, or, not} {and, not} {and, or} {nor}.

(	)	12.	An nMOS transistor is a good switch for passing high voltage  good switch for passing low voltage  bad switch for passing V(0)  bad switch for passing small signal.

(	)	13.	Which cannot be a layout description? EDIF GDS II Netlist .

(	)	14.	Which is not a complete logic set? {and, or, not} {and, not} {and, or} {nor}.

(	)	15.	Which of the following can have the highest resolution? poly-resistance poly-capacitance MOS capacitance MOS resistance.

(	)	16.	Delay time is usually defined as that form 0.9Vdd input to 0.1Vdd output 0.1Vdd input to 0.9Vdd output 0.5Vdd input to 0.5Vdd output  (rise time + fall time)/2.

(	)	17.	In nm process, which power dissipation will dominate? dynamic load short-circuit static.

(	)	18.	Which can implement any function to a primitive? CMOS Domino SFPL CVSL.

(	)	19.	In single-cell high-speed logics, which is usually preferred? NAND4 NOR4 NAND10 NOR10.

(	)	20.	To fit the stage ratio and H-tree, the fanout of the clock tree is usually 3 4 10 30.

(	)	21.	The diffusion resistance from an i/o pad is used to prevent from thinox puncture peak current drain breakdown latch-up.

(	)	22.	The diode clamper in i/o pads is used to prevent from ESD noise latch-up bird’s beak.

(	)	23.	Additional power pads are usually used to prevent from damage risk noise cross talk latch-up.

(	)	24.Which logic can save power and have strong drivability?BJT Domino BiCMOS CCMOS.

(	)	25.	Which layer is grown first?FOX Thinox LOCOS Passivation.

- Questions：

- Draw the stick diagram of a matched layout of a differential pair (M1←<Cross coupled>→M2, M3←<mirror>→M4, M5<M=2>).

- Draw the stick diagram of a Boolean function F=AB+C in Eular-path and diffusion-line approach.

- Draw a n-type domino gate, ao22 and explain the operations at low- and high- clock levels.

- Explain the following terms: bus contention, transparent output, bird’s beak, LOCOS, THINOX, FOX, SFPL, C2MOS, metastability, passivation, latch-up effect, body effect, stack effect, ESD, SEM, Etching, implant, diffusion, twin-well, drain breakdown, pad-limited, core-limited, butting, feed-through, doubly guard rings, CCD, JEDEC, Reverse Engineering, CMP, DRC, LVS, BSIM.

- Draw a block diagram of an SRAM with an SA and row- and column-addresses multiplexed.

- Use the bit-size of a DRAM module to illustrate the Moore’s Law.

- Draw a Y-chart with at least 3 levels and give the typical EDA flow.

- Give the typical flow for tape-in of a full custom chip to the CIC.

- List the MOE consortiums in VLSI field and give a conference/symposium name in 2003.

- Describe the interface for single-clock different-domain circuits.

- Describe the basic concept of content-associate memory (CAM).

- Describe the scopes of Level-1, Level-2 models of SPICE and First-order Equations.

- Describe the basic concept of fast-page mode (FPM) DRAM.

- Give a test bench for ESD and classify to 3 or 4 classes.

- Draw a typical storage hierarchy pyramid and put down some typical devices with suitable byte-sizes.

- Pick out unreasonable constraints in the following timing diagram and explain.

- Draw a Huffman model with notations C(clock), D(DFF I/P), Q(DFF O/P) and put down the relation to cycle time(Tc) considering skew(tSK) and jitter (tJT).

- Illustrate at least 3 approaches to reduce the skew problem.

- Draw the diagram of the typical PLL.

- Give an as-simple-as-possible example to illustrate the clock-gating failure.

- Choose a proper (equal input margin) Wp/Wn of the output inverter for a 3-bit address decoder shown as below. and assume VDD=3.3V, |Vtp|=Vtn=0.45V, n/p=2.6, Ln=Lp.

- Laid out a NOR-type RS latch on the following SOG. Remember that you can use a turned-off transistor to split the diffusion lines.

# Text boxes

2004/1/12 13:20-15:00