國立彰化師範大學電子系九十三學年第一學期期中考考卷

課目：數位IC設計 日期：2004/11/16(Tue.)  時間：1:00~2:50pm  地點：31303  老師：黃宗柱

學號：______________             姓名：_______________   得分：___________________

- TRUE OR FALSE (Mark T or F, 10%):

( F	)	1.	For matched layout, the matched pair of transistors are usually mirrored symmetrically.

( T	)	2.	Cross couple matched layout is usually used to reduce the shifting and gradient errors.

( F	)	3.	The sheet resistance of a 10um x 10um poly is 100 times that of a 1um x 1um poly.

( T	)	4.	Usually, layout includes floorplanning, partitioning, placement and routing.

( T	)	5.	Leakage will trend to dominate power dissipation in the coming nano-meter technology era.

- MULTIPLE CHOICE (Choose the best one, 15%):

( D	)	1.	As a TTL(0.4V, 2.8V)-CMOS(0.2V, 4.8V) interface, the noise margin is about (A) 4.6 (B) 2.3 (C) 2.4 (D) 1.2 V.

( D	)	2.	The transfer function of the circuit XNOR(NOR(A,A),NAND(A,A)) looks like (A) _─_ (B)└┐(C)┌┘ (D) -_- .

( C	)	3.	Which is not a complete logic set? (A) {and, or, not} (B) {and, not} C{and, or} D{nor}.

( B	)	4.	Which can have the highest resolution? (A) poly-resistance (B) poly-capacitance (C) MOS capacitance (D) MOS resistance.

( A	)	5.	The diode clamper in I/O pads is used to prevent from (A) ESD (B) noise (C) latch-up (D) bird’s beak.

- QUESTIONS (75%):  NOTE: The following is just for reference.

    - Laid out a function A>B on the following SOG. Remember that you can use a turned-off transistor to split the diffusion lines. (Ans= corrected)

    - Write a SPICE code to draw the Bode plot of a CMOS inverter including default models. Define the rest question and parameters by yourself.

*BODE PLOT OF AN INVERTER

.MODEL		NCH	NMOS

.MODEL		PCH	PMOS

MP	OUT	IN	VDD	VDD	PCH	W=2U	L=0.35U

MN	OUT	IN	0	0	NCH	W=1U	L=0.35U

VDD	VDD	0	3

VIN	IN	0	AC	1

.AC	DEC	101	1K	1T

.OPTION	POST

.END

    - Write a Verilog code including a synchronously resettable DFF in behavioral model and a 4-bit Johnson counter in structural view using the DFFs.

module DFF(Rst, Clk, D, Q);

input 		Rst, Clk, D;

output 	Q;

reg		Q

always@(Clk) if(Rst) Q=0; else Q=D;

endmodule

module JohnsonCounter(Rst, Clk, Q);

input Rst, Clk;

output [3:0] Q;

DFF	D0(Rst, Clk, Q[1], Q[0]);

DFF	D1(Rst, Clk, Q[2], Q[1]);

DFF	D2(Rst, Clk, Q[3], Q[2]);

DFF	D3(Rst, Clk, QN0, Q[3]);

not	G1(QN0, Q[0]);

endmodule

    - Describe at least 4 methods to relax the skew problem.

      - Using Phase Lock Loop;

      - Inserting Buffers along the wires;

      - Laid out as an H-tree;

      - Clocking against the data-stream order (in contra-direction).

    - Draw the stick diagram of the primitive CMOS gate with function .