## Slide 1
Hardware Description Language
-- Logic Design using Verilog
Tsung-Chu Huang
Dept. of Electronic Eng.
National Changhua University of Ed.
Email: tch@cc.ncue.edu.tw
2022/09/22

## Slide 2
Quick Tutorial
Select 3 Verilog-Compilers for tutorial.
  SynaptiCAD’s Verilogger Pro
  Candence’s VerilogXL or NCSim
  ModelSim
  Altera’s Quartus II
Exercise and experience:
  Hierarchy design orientation
  Design styles and views
  Testfixture (Testbench) Construction
Video Lectures
  Please browse from the links attached in the syllabus at website
  http://testlab.ncue.edu.tw/tch/lecture/HDL2015/syllabus.htm

## Slide 3: Hierarchy, Tree and Nest Blocks
Top, Root
S
U
V
W
T

## Slide 4: Testbench or Testfixture
Synthesizable Hardware
Top
S
U
V
W
T
initial block
as signal generator
and logic analyzer
$display
$monitor
waveform
like a scope
or logic analyzer

## Slide 5
Hierarchy Design Orientation
Bottom-up
Top-down
Long-term library construction
Easy modularization
Shorten design phase
Should be modularized carefully
Ideal EDA Flow
Middle-out
Ends-In
Hybrid (Greedy) : Human thinking

## Slide 6
Example: 4-Bit Adder
Can designed as a primitive cell optimized to SOP (or POS) forms using McKlusky method (or K-Map)
Implicant | A3 | A2 | A1 | A0 | B3 | B2 | B1 | B0 | Ci | Co | S3 | S2 | S1 | S0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
4 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
5 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
6 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
7 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
 |  |  |  |  |  | : |  |  |  |  |  |  |  | 
 |  |  |  |  |  | : |  |  |  |  |  |  |  | 
 |  |  |  |  |  | : |  |  |  |  |  |  |  | 
498 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1
499 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0
500 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
501 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
502 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
503 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0
504 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1
505 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
506 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1
507 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0
508 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
509 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
510 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
511 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0
Time Complexity: Incredibly exponentially increasing!

## Slide 7
AND
Can be found in physical library
XOR
Can be found in physical library
Half Adder
Half Adder
Top-down Analysis
4-Bit Adder
Full Adder
Full Adder
Full Adder
Full Adder
Behavioral View
{Co, S} = A + B
Structure View
Behavioral View
{Co,S}=A+B+Ci
Structure View
Behavioral View
{C,S}=A+B
AND
Can be found in physical library

## Slide 8
Bottom-up Synthesis
4-Bit Adder
AND
Can be found in physical library
VLSI Layout → Physical View

## Slide 9
Bottom-up Synthesis
4-Bit Adder
AND
Can be found in physical library
Physical View
Standard Cell
Symbol View

## Slide 10
Bottom-up Synthesis
4-Bit Adder
Schematics

## Slide 11
Bottom-up Synthesis
4-Bit Adder
Schematics
Half Adder

## Slide 12
Bottom-up Synthesis
4-Bit Adder
Half Adder
Symbol View

## Slide 13
Bottom-up Synthesis
4-Bit Adder
Half Adder
Half Adder

## Slide 14
Bottom-up Synthesis
4-Bit Adder
Half Adder
Half Adder
Full Adder

## Slide 15
Bottom-up Synthesis
4-Bit Adder
Full Adder
Full Adder
Full Adder
Full Adder

## Slide 16
Flattened Synthesis
For Some example
NAND
NAND
NOT
AOI
NOT
XOR
NOR
NAND
NAND
NAND
NOT
AOI
NOT
XOR
NOR
NAND
NAND
NAND
NOT
AOI
NOT
XOR
NOR
NAND
Physical View

## Slide 17: Ideal EDA Flow along Y-Chart
Behavioral
Structural
Physical
modularization
partitioning
library
synthesize
sim
ver

## Slide 18
VLSI Design Tools Supported by TSRI (CIC)
Syntheses & Analyses
Layout Editor
Laker, Virtuoso
Circuit Simulator
SPICE, Spectre
Logic Simulator
VHDL, Verilog
Synthesizer
Design Compiler
STA
PrimeTime/Power
Schematic
Composer
Debugger
Debussy
Physical Extract
Calibre
Physical Verify
Dracula, Calibre
FPGA Synthesis
ISE, Quartus
DFT
SynTest, Mentor
Place & Route
SE, Apollo, Astro

## Slide 19
VLSI Design Tools Supported by TSRI (CIC)
Front-end & Back-end
Layout Editor
Laker, Virtuoso
Circuit Simulator
SPICE, Spectre
Logic Simulator
VHDL, Verilog
Synthesizer
Design Compiler
STA
PrimeTime/Power
Schematic
Composer
Debugger
Debussy
Physical Extract
Calibre
Physical Verify
Dracula, Calibre
FPGA Synthesis
ISE, Quartus
DFT
SynTest, Mentor
Place & Route
SE, Apollo, Astro

## Slide 20
VLSI Design Tools Supported by TSRI (CIC)
Levels
Layout Editor
Laker, Virtuoso
Circuit Simulator
SPICE, Spectre
Logic Simulator
VHDL, Verilog
Synthesizer
Design Compiler
STA
PrimeTime/Power
Schematic
Composer
Debugger
Debussy
Physical Extract
Calibre
Physical Verify
Dracula, Calibre
FPGA Synthesis
ISE, Quartus
DFT
SynTest, Mentor
Place & Route
SE, Apollo, Astro

## Slide 21
VLSI Design Tools Supported by TSRI (CIC)
Views
Layout Editor
Laker, Virtuoso
Circuit Simulator
SPICE, Spectre
Logic Simulator
VHDL, Verilog
Synthesizer
Design Compiler
STA
PrimeTime/Power
Schematic
Composer
Debugger
Debussy
Physical Extract
Calibre
Physical Verify
Dracula, Calibre
FPGA Synthesis
ISE, Quartus
DFT
SynTest, Mentor
Place & Route
SE, Apollo, Astro
P
B
S

## Slide 22: Lab02 Flip-Flops
Latches and Flip-Flops
Gate-Level and Behavioral Models
Implement blocking ( = ) by latches and non-blocking ( <= ) by FFs in Quartus II.
Simulated Clock Generator
reg Clk;
initial Clk = 0;
always #half_period Clk = !Clk;
Problem 1: How to Convert btw DFF, JK-FF, RS-FF, and TFF?
Problem 2: Complete all possible combinations for this lab.