## Slide 1
Hardware Description Language
-- Logic Design using Verilog
Tsung-Chu Huang
Dept. of Electronic Eng.
National Changhua University of Ed.
Email: tch@cc.ncue.edu.tw
2022/10/06

## Slide 2
Outline
RTL or Behavioral
Two Major Phases of HDL
Applicative Tools Related to HDL
ASM-Based Synthesis using an Example

## Slide 3
Which is Better – RTL or Behavior
Rethink using Binary Counter and Gray Counter
Q5 Q4 Q3 Q2 Q1 Q0
Low Power Channel
Regular structure or regular behavior?
module Gray(Clk, Q);
input Clk;
output [n-1:0] Q;
wire [n-1:0] Qb;
binary_counter (Clk, Qb);
xor_array (Q, Qb);
endmodule
module Binary(Clk, Q);
input Clk;
output [n-1:0] Q;
wire [n-1:0] Qb;
always@(posedge Clk)
Q=Q+1;
endmodule

## Slide 4
Two Major Phases
Simulation
  Usually simulated along time axis (initial)
  With stimuli
Synthesis
  Continuously exists
      Gate-Level (Structural View)
      RTL ( assign L = f(R); )
  Always Procedural (Behavioral Model)

## Slide 5
Sequential Circuits
Huffman Model: Combinational Circuits with a set of DFFs
  Combinational Network is a DAG (Directed Acyclic Graph)
  1-Cycle FSM with additional Reset cycle.
  Can be expanded to an iterative logic array (ILA) that is a combinational circuit, i.e. trivial 0-cycle FSM.
  Long critical paths can be spitted by inserted DFFs.
Seq. Ckt
Datapath
ASM
Huffman Model
Pure FSM
Critical-Path Split
Pipelined Datapath
ILA
Combinational Circuits

## Slide 6
Considering Subtractors
module Sub(A, B, Bi, D, Bo);
input A[n-1:0], B[n-1:0], Bi;
output D[n-1:0], Bo;
reg D[n-1:0], Bo;
assign {Bo, Bi}=A-B-Bi;
endmodule
–
Bin
Bout
B
A
D
Boolean Function Based Design: Too Complex
Half-Subtractor→Full-Subtractor→n-bit Subtractor
Parallel Design
Modified from Adder:
  S = A + B if Sub==0
  S =A - B = A + (-B) = A + (~B+1) if Sub==1
  D = S = A + (Sub ? ~B : B) + Sub

## Slide 7
6-Bit Parallel Multiplier
2 3 4
1 2 3
X )
7 0 2
4 6 8
2 3 4
2 8 7 8 2
1 0 1 1 = B
1 1 0 1 = A
X )
1 0 1 1
0 0 0 0
1 0 0 0 1 1 1 1
1 0 1 1
1 0 1 1
1 →
0 →
1 →
1 →
Product P=BxA

## Slide 8
module MULij(Ai, Bj, Ci, Co, Pi, Po);
input Ai, Bj, Ci;
output Co, Pij;
and (AB, Ai, Bj);
FullAdder (Pi, Ci, AB, Co, Po);
endmodule
Multiplier Cell
+
Bj
Ai
Ci(j-1)
Cij
Pij

## Slide 9
6-Bit Parallel Multiplier
i
j
k=i-j
k=1
k=2
i=0
i=1
j=0
j=1
i=2
j=2
A[0]
A[1]
A[5]
B[0]
B[1]
B[2]
P[11]
P[10]
P[9]
P[5]
P[4]
P[6]
P[7]
P[8]
P[0]
P[1]
P[2]
P[3]
B[3]
B[4]
B[5]
Row0 
Row1 
Row2 

## Slide 10
Coding by C2V in V95
#include <stdio.h>
#include <stdlib.h>
main()
{
int i, j, N=6;
for(i=0; i<N; i++) {
for(j=0; j<N; j++) {
printf("MCell M%d(A[%d], B[%d], ", i*N+j, i, j);
if(j==0) printf("0, "); else printf("C[%d], ", i*N+j-1);
printf("C[%d], ", i*N+j);
if(i==0) printf("0, ");
else if(j==N-1) printf("C[%d], ", (i-1)*N+j);
else printf("S[%d], ", (i-1)*N+j+1);
printf("S[%d]);\n", i*N+j);
}
}
}
MCell M0(A[0], B[0], 0, C[0], 0, S[0]);
MCell M1(A[0], B[1], C[0], C[1], 0, S[1]);
MCell M2(A[0], B[2], C[1], C[2], 0, S[2]);
MCell M3(A[0], B[3], C[2], C[3], 0, S[3]);
MCell M4(A[0], B[4], C[3], C[4], 0, S[4]);
MCell M5(A[0], B[5], C[4], C[5], 0, S[5]);
MCell M6(A[1], B[0], 0, C[6], S[1], S[6]);
MCell M7(A[1], B[1], C[6], C[7], S[2], S[7]);
MCell M8(A[1], B[2], C[7], C[8], S[3], S[8]);
MCell M9(A[1], B[3], C[8], C[9], S[4], S[9]);
MCell M10(A[1], B[4], C[9], C[10], S[5], S[10]);
MCell M11(A[1], B[5], C[10], C[11], C[5], S[11]);
MCell M12(A[2], B[0], 0, C[12], S[7], S[12]);
MCell M13(A[2], B[1], C[12], C[13], S[8], S[13]);
MCell M14(A[2], B[2], C[13], C[14], S[9], S[14]);
MCell M15(A[2], B[3], C[14], C[15], S[10], S[15]);
MCell M16(A[2], B[4], C[15], C[16], S[11], S[16]);
MCell M17(A[2], B[5], C[16], C[17], C[11], S[17]);
MCell M18(A[3], B[0], 0, C[18], S[13], S[18]);
MCell M19(A[3], B[1], C[18], C[19], S[14], S[19]);
MCell M20(A[3], B[2], C[19], C[20], S[15], S[20]);
MCell M21(A[3], B[3], C[20], C[21], S[16], S[21]);
MCell M22(A[3], B[4], C[21], C[22], S[17], S[22]);
MCell M23(A[3], B[5], C[22], C[23], C[17], S[23]);
MCell M24(A[4], B[0], 0, C[24], S[19], S[24]);
MCell M25(A[4], B[1], C[24], C[25], S[20], S[25]);
MCell M26(A[4], B[2], C[25], C[26], S[21], S[26]);
MCell M27(A[4], B[3], C[26], C[27], S[22], S[27]);
MCell M28(A[4], B[4], C[27], C[28], S[23], S[28]);
MCell M29(A[4], B[5], C[28], C[29], C[23], S[29]);
MCell M30(A[5], B[0], 0, C[30], S[25], S[30]);
MCell M31(A[5], B[1], C[30], C[31], S[26], S[31]);
MCell M32(A[5], B[2], C[31], C[32], S[27], S[32]);
MCell M33(A[5], B[3], C[32], C[33], S[28], S[33]);
MCell M34(A[5], B[4], C[33], C[34], S[29], S[34]);
MCell M35(A[5], B[5], C[34], C[35], C[29], S[35]);

## Slide 11
Enhancement in IEEE 1364-2001 V2K
Design management—Verilog configurations
Scalable models—Verilog generate
Constant functions
Indexed vector part selects
Multidimensional arrays (reg [7:0] a[1:4][0:255];)
Bit and part selects within arrays
Signed arithmetic extensions (eg. reg signed [15:0] x; >>>)
Power operator ** (xor ^)
Re-entrant tasks and recursive functions
Combinational logic sensitivity token (always@*)
Comma-separated sensitivity lists
Automatic width extension beyond 32 bits
Enhanced file I/O
In-line parameter passing by name
Combined port and data type declarations
ANSI-style input and output declarations
reg declaration initial assignments

## Slide 12
8 Blocks in Verilog
Block | Outlook | Property | for-loop | index
statements | begin [:name] end | grouping |  | 
module | module #(para) ID (ports); endmodule | parallel |  | 
always | always@(events) statements; | procedural | concurrent | integer
initial | initial statements; | serial | sequential | Integer
task | task ID; endtask | procedural | sequential | integer
function | function ID; endfunction | procedural | sequential | sequential
generate | generate endgenerate |  | by time 0 | genvar
specify | specify endspecify |  |  | 

## Slide 13
“Block” in Verilog
A rectangle region
  Hierarchical blocks
  Specific blocks
      module / endmodule
      always
      generate
      Initial
      specify / endspecify
      function / endfunction
      Task / endtask
To block is to stop something moving
  Blocking Assignment
  In “x = y; z = x;” write(x) will block read(x).
  Non-blocking Assignment
  In “x <= y; z <= x;” write(x) won’t block read(x).
begin
begin
end
begin
end
end

## Slide 14
“for” in Verilog
integer i;
initial begin
for(i=1; i<10; i=i+1) begin
X = i[7:0];
#10;
end
$stop;
end
genvar i;
(generate)
for(i=1; i<10; i=i+1) begin:NAME
MODULE G1(X[i], Y[i+1]);
assign OUT[i] = IN[i-1]+A;
end
(endgenerate)
integer i;
always@(posedge Clk) begin
for(i=1; i<10; i=i+1) begin
R[i] <= R[i-1];
end
R[9] <= R[0];
end
Time
Space

## Slide 15
Parametered/Generate Verilog-2K

## Slide 16
Coding by V2K
genvar i, j;
for(i=0; i<N; i=i+1) begin : Row
for(j=0; j<N; j=j+1) begin : Col
MCell Cell( A[i], B[j], Ci[i][j], Co[i][j], Si[i][j], So[i][j]);
end
end
endmodule

## Slide 17
Big-Data Verification
`timescale 1ns/10ps
module Test_MUL;
parameter N = 8;
reg [N-1:0] A, B;
wire [2*N-1:0] P;
MUL U1(A, B, P);
integer i, j, ok;
initial begin
$monitor($time, ",", A, ",", B, ",", P);
ok=1;
for(i=0; i < 1<<N ; i=i+1)
for(j=0; j < 1<<N ; j=j+1)
begin
A=i; B=j;
#10;
if(P != i*j) ok=0;
end
$display("Varification: %s.", ok ? "Ok" : "Failed");
$stop;
end
endmodule
VSIM 3> run
# 0, 0, 0, 0
:
:
# 655340,255,254,64770
# 655350,255,255,65025
# Varification: Ok.
# Break in Module Test_MUL at D:/work/MulArray/Test_MUL.v line 20
VSIM 4> |

## Slide 18
Layout View: 6-Bit Parallel Multiplier

## Slide 19
N-bit Shifter
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
Shift_Left1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
Shift_Left2
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
Shift_Left3
1
0
1
Constant Shifter
Shift Register

## Slide 20
Algorithmic State Machine
A special design style of general finite state machines.
It can be designed by mapping from the flow-chart.
It can be synthesized manually.
High area overhead and low performance due multiplexer stack.
  Describe your system in pseudo code;
  Draw the flow-chart;
  Map the flow-chart to ASM chart;
  Map the ASM chart to the HDL or circuit.

## Slide 21: Pseudo Code
A high-level, almost-executable description
Used for leader’s instruction, explanation of algorithms, etc.
Pascal-like or C-like codes with some comprehensive English is preferable.
Example:

## Slide 22: Basic Flowchart Elements
Flow and Direction:
Decision:
condition
Y
N
Process:
process
Terminals:
begin
end
(Card) Input:
Specific Outputs:
card in
tapeout
report
display

## Slide 23: Sequence Control if-then-else
if (
} else {
Y
) {
C
Y
Y
N
}
Condition
N
N

## Slide 24: Sequence Control switch
c
2
1
N
3
if (expr==const1) {P1}
else if (expr==const2) {P2}
else if (expr==const3) {P3}
else if (expr==const4) {P4}
else {Pdefault}
switch (expr) {
case const1: {P1} break;
case const2: {P2} break;
case const3: {P3} break;
case cosnt4: {P4} break;
...
default: {Pdefault}
}

## Slide 25: Sequence Control For-loop
for(i=1;i<=9;i++) {
}
for (
I
;
;
N
) {
P
}
C
Initialization
Condition
Process
Next
Y
N
for(j=1;j<=9;j++)
printf(“%dX%d=%2d\t”,i,j,i*j);
printf(“\n”);

## Slide 26: Sequence Control Do-While-Loop and While-Do-Loop
do {
} ;
P
} while(
C
Y
Condition
Process
N
while (
} ;
P
) {
C
Y
Process
Condition
N

## Slide 27
Map Flowchart to ASM Chart
Split Processes in flowchart into States that each state can be executed in 1 clock cycle.
Note that a WR-dependent process should be split into two states.
a = b + c;
x = a * d;
(write first then read)
a = b + c;
State1:
x = a * d;
State2:
x = a + d;
a = b * c;
(read first then write)
x = a + d;
a = b * c;
State1:

## Slide 28
Map Decision to Demultiplexer
If the condition is a 1-bit variable, directly map the decision to a demultiplexer that is a combinational gate (i.e., it takes a delay less than the clock cycle).
C
N
Y
C
0
1
The clock state of a decision is belong to the last process, therefore the last process should be split into 2 states if there is a WR-dependency.
C
N
Y
C = A & B;
C
0
1
(Dummy)
C = A & B;

## Slide 29
Map Decision with Expression to Diamond
If the condition is an expression instead of a direct input, map the decision to a a diamond.
A diamond is composed of a demultiplexer and an extra process.
C=f( )
N
Y
C
0
1
f( )
0
1
f( )
0 1
C
f( )
When the dealy of combinational circuit f( ) is too large, it is better to split it to two states with a demultiplexer.
C
0
1
(Dummy)
C = f( );

## Slide 30: Example 8-bit Multiplier
Clk
Rst
N
X
Y
A
C
B

## Slide 31: For Instance
N ← N + 1
begin
end
N←0; A←0; B←Y; C←0
B[0]
No
Yes
{C,A}←A + X
N=0
No
Yes
{C,A,B}←{C,A,B}>>1
0
0
0
0
0
0
0
0
1
0
1
0
0
1
0
1
0
0
0
0
N
B
1
0
0
1
0
1
1
1
X=151
1
0
1
0
0
1
0
1
Y=165
1
0
0
1
0
1
1
1
1
0
1
0
0
1
0
1
0
0
0
0
0
1
0
0
1
0
1
1
1
1
0
1
0
0
1
0
0
0
0
1
0
1
0
0
1
0
1
1
1
1
0
1
0
0
1
0
0
0
0
1
0
0
1
0
0
1
0
1
1
1
1
0
1
0
0
1
0
0
1
0
1
0
1
1
1
1
0
0
1
1
1
0
1
0
0
1
0
0
1
0
0
1
0
1
1
1
1
0
0
1
1
1
0
1
0
0
0
0
1
1
0
1
0
1
1
1
1
0
0
1
1
1
0
1
0
0
0
0
1
1
0
0
1
0
1
1
1
1
0
0
1
1
1
0
1
0
0
1
0
0
0
0
1
0
1
1
1
1
0
0
1
1
1
0
1
0
0
1
0
0
0
0
0
1
0
1
1
1
1
0
0
1
1
1
0
1
0
1
0
1
1
0
1
0
1
1
1
0
1
0
0
1
1
1
0
1
0
1
0
1
0
1
0
1
0
1
1
1
0
1
0
0
1
1
1
0
0
1
1
0
0
1
0
1
0
1
1
1
0
1
0
0
1
1
1
0
0
1
1
0
0
0
1
0
1
0
1
1
1
0
1
0
0
1
1
1
0
1
1
1
1
1
0
0
0
0
1
0
1
0
1
0
0
1
1
1
0
1
1
1
0
1
1
0
0
0
0
1
0
1
0
1
0
0
1
1
0
0
0
0
→
+
→
→
+
→
→
→
+
→
→
+
P=151X165=24915

## Slide 32: Example of Verification using C
#include <stdio.h>
main()
{
unsigned char X, Y, C, A, B, N, Verified;
int i, P, Q, Acc, S;
Verified = 1;
for(i=0;i<(1<<16);i++){
X=i/(1<<8);
Y=i%(1<<8);
P=X*Y; // Golden Circuit
// Algorithm Started Here
N=0; A=0; B=Y; C=0; // Initialization
do {
// Accumulate
if(B%2) {Acc = A + C*256 + X; A=Acc%256; C=(Acc>>8)%2;}
// Shift CAB
S = C*65536 + A*256 + B; S = S >> 1; B=S%256; A=(S>>8)%256; C=(S>>16)%2;
N++;
} while(N!=8);
Q=(A<<8)+B;
if(Q!=P) {
Verified=0;
printf("Error when X=%d, Y=%d, Q=%d\n", X, Y, Q);
break;
}
}
if(Verified) printf("The circuit is exhaustively functionally verified.\n");
}

## Slide 33: Example: Verified using Assembly Language
BEGIN: MOV N, #States
CLR A
CLR C
MOV B, X
LOOP: JE SHIFT
ADC Y
SHIFT: SHR CAB
DEC N
JNZ LOOP
END
C and Assembly codes can be the fast logic simulator.

## Slide 34: Example: 8-bit Multiplier
N ← N + 1
begin
end
N←0; A←0; B←Y; C←0
B[0]
No
Yes
{C,A}←A + X
N=0
No
Yes
{C,A,B}←{C,A,B}>>1
Dummy
begin
end
N←0; A←0; B←Y; C←0
B[0]
0
1
{C,A}←A + X
{C,A,B}←{C,A,B}>>1; N←N+1
dummy
1
0
N=0
Initial:
Accumulate:
Shift:
Dummy2:
ASM Chart

## Slide 35: Map ASM Elements to Sequencer
State
D
Q
CLR
State
end
D
Q
CLR
begin
D
Q
PRE
0 1
C
C
1
0
0
1
f( )
f( )
0 1
C

## Slide 36: Map to State Sequencer
dummy
begin
end
N←0; A←0; B←Y; C←0
B[0]
0
1
{C,A}←A + X
{C,A,B}←{C,A,B}>>1; N ← N + 1
dummy
1
0
N=0
Accumulate:
Shift:
ASM Chart
D
Q
PRE
0 1
D
Q
CLR
D
Q
CLR
D
Q
CLR
D
Q
CLR
D
Q
CLR
0 1
D
Q
CLR
Initial:
Initial
Accumulate
Shift

## Slide 37: Map to ALU
dummy
begin
end
N←0; A←0; B←Y; C←0
B[0]
0
1
{C,A}←A + X
{C,A,B}←{C,A,B}>>1; N ← N + 1
dummy
1
0
N=0
Accumulate:
Shift:
ASM Chart
Initial:
C
A
B
N
0 1
Accumulate
1 0
Accumulate
0 1
Shift
0 1
Shift
0 1
Shift
0 1
Shift
+
1
+
0 1
Initial
0
0 1
Initial
0
0 1
Initial
0
0 1
Initial

## Slide 38
D
Q
PRE
0 1
D
Q
CLR
D
Q
CLR
D
Q
CLR
D
Q
CLR
D
Q
CLR
0 1
D
Q
CLR
Initial
Accumulate
=
0
Control
Ready
P
C
A
B
N
0 1
Accumulate
1 0
Accumulate
0 1
Shift
0 1
Shift
0 1
Shift
0 1
+
1
+
0 1
Initial
0
0 1
Initial
0
0 1
Initial
0
0 1
Initial
Y
X
Shift
Rst
Clk

## Slide 39: Remapped to Coding Gate-Level Model for Sequencer
module Sequencer(Rst, Clk, B, E, Initial, Accumulate, Shift, Ready);
input Rst, Clk, B, E;
output Initial, Accumulate, Shift, Ready;
  DFFp (Clk, Rst, 0, Q1)
  DFFc (Clk, Rst, Q1, Initial);
  DFFc (Clk, Rst, initial, Q2);
  or (A, Q2, E0);
  mux (B, A, B1, B0);
  DFFc (Clk, Rst, B1, Accumulate);
  or (Q3, B0, Accumulate)
  DFFc (Clk, Rst, Q3, Shift);
  DFFc (Clk, Rst, Shift, Q4);
  mux (E, Q4, E1, E0);
  or (Q5, Ready, E1);
  DFFc (Clk, Rst, Q5, Ready);
endmodule

## Slide 40: Remapped to Coding Minimized Counter-Based State Diagram
Init
Acc
Init
Shift
N
PowerOn or SysRst

## Slide 41: Counter-Based FSM Coding 2-State-Cycle 2n-Bit Sequential Multiplier
module MUL(Rst, Clk, X, Y, P, Ready);
  Parameter n=3;
  input Rst, Clk;
  input [2^n-1:0] X, Y;
  output [2*2^n-1:0] P;
  output Ready;
  reg [n-1:0] N
  reg C;
  reg [2*2^n-1:0] P;
  reg [1:0] State;
  parameter Init=2’b00, Acc=2’b01, Shift=2’b10, Ready=2’b11;
  always@(posedge Clk)
  if(Rst) begin N=0; State=Acc; C=0; P=Y; end
  else case(State)
  Acc: P=P+X;
  Shift: begin
  N=N+1; P={C, P[15:1]}; C=0;
  State=N?Acc:Ready;
  end
  Ready: State=Ready;
  endcase
endmodule

## Slide 42: Counter-Based FSM Coding 1-State-Cycle 2n-Bit Sequential Multiplier
module MUL(Rst, Clk, X, Y, P, Ready);
  input Clk, Rst;
  output Ready;
  input [7:0] A, B;
  output [15:0] P;
  reg [15:0] P;
  reg [2:0] N;
  reg Ready;
  wire [8:0] S;
  wire [16:0] Q;;
  assign S = P[0]?(P[15:8]+A):P[15:8];
  assign Q = {S, P[7:0]};
  always@(posedge Clk)
  if(Rst) begin N=0; P[15:8]=0; P[7:0]=B; Ready=0; end else if(!Ready) begin
  P = Q >> 1;
  if(N==7) Ready = 1; else N = N + 1; end
endmodule

## Slide 43
N-Bit Multiplier
Execution Time
Area Cost
Parallel Multiplier (Combinatinal Circuit)
N-bit Sequential
Partially Parallel
assign P = A * B;

## Slide 44: Example: Greatest Common Divisor
Actually you have known the algorithm!
So, just catch the regularities from observation.
gcd( 91, 35 ) =
70
= gcd( 21, 35 )
= gcd( 35, 21 )
21
= gcd( 14, 21 )
= gcd( 21, 14 )
14
= gcd( 7, 14 )
= gcd( 14, 7 )
14
0
7

## Slide 45: Example: Greatest Common Divisor
Then you can write a function in C.
unsigned int GCD(unsigned int A, insigned int B)
{
unsigned int C;
if(A<B) SWAP(A, B);
while(B>0) {
C = A % B;
A = B;
B = C;
}
return(A);
}
void SWAP(unsigned int A, unsigned int B)
{
unsigned int C;
C = A;
A = B;
B = C;
}
Can be implemented in 1 cycle in hardware!
/ % can be simulated
in ModelSim (V2K).
Need not be implemented
in some synthesizers.

## Slide 46: From C Straightforward to Verilog Example: GCD
module GCD(Clk, Rst, A, B, D, Ready);
input Clk, Rst;
input [31:0] A, B;
output [31:0] D;
output Ready;
parameter Init=0, Mod=1, Out=2;
reg [1:0] PS, NS;
always@(posedge Clk)
if(Rst) begin NS=Init; PS=Init; Ready=0; end
else begin PS = NS;
wire [31:0] X, Y;
always@* case(PS)
Init: begin
X = (A<B) ? B : A; Y = (A<B) ? A : B; NS = Mod;
end
Mod: begin X <= Y; Y <= X % Y; NS = Y ? Mod : Out; end
Out: begin D = X; NS = Out; Ready=1; end
endcase
endmodule

## Slide 47: From C Straightforward to Verilog Example: Bubble Sorter
int Sort(int M[], N)
{
int a, n;
for(n=N-1;n>0;n--)
for(a=0;a<n;a++)
Swap(M[a], M[a+1]);
return(0);
}
Module M(Clk, WE, A, D);
inout [31:0] D;
input [11:0] A;
input Clk, WE;
reg [31:0] M [0:4095];
always@(posedge Clk)
if(WE) M[A]=D;
else D=M[A];
endmodule
WE
Sorter
M
Clk
Start
Ready
A
D
B<D
B=D
A=A+1
WE=0
N=4095
A=0
WE=0
B<D: B=D;
A=A+1; WE=0;
If(A=N-1) N=N-1
B>=D: A=A-1;
WE=1;
Ready=1
N=0
D=B;
A=A+1; WE=1
If(A=N-1)
N=N-1
Init
Go
R
C
W
Ok

## Slide 48: From C Straightforward to Verilog Example: Bubble Sorter
module Sorter(Clk, Init, WE, A, D, Ready);
input Clk, Init;
inout [31:0] D;
output WE, Ready;
output [11:0] A;
reg [2:0] S;
parameter Ok=0, Go=1, R=2, C=3, W=4;
reg [11:0] A;
reg [31:0] B, D;
reg [11:0] N;
reg Ok;
  always@(posedge Clk)
  if(Init) begin N=4095; S=Go; end
  else case(S)
  Go: begin A=0; WE=0; S=R1; end
  R: begin B=D; A=A+1; S=C; end
  C: if(B>D) begin A=A-1; WE=1; S=W; end
  else begin B=D; A=A+1; WE=0;
  if(A>=N-1) if(N>1) begin N=N-1; S=C; end
  else S=Ok;
  else S=Go;
  end
  W: begin D=B; A=A+1; WE=1;
  if(A>=N-1) begin if(N>1) begin N=N-1; S=Go; end
  else S=Ok;
  end
  end
  Ok: Ready=1;
  endcase
endmodule

## Slide 49: From C Straightforward to Verilog Example: Prime Numbers
void prime()
{
unsigned int M[100], N=0, i, j, yes;
M[N++]=2;
for(i=3; i<9999; i+=2) {
j=0;
yes=1;
while(M[j]*M[j]<i) if(i%M[j++]) {yes=0; break;}
if(yes) M[N++]=i;
}
}

## Slide 50: Exercises and Rethinks
List prime numbers < 9999.
Calculate the area of a triangle with edges A, B, and C.
Quick Sort in Hardware. (How about parallel sorter?)
Sequentially Fourier transform. (How about FFT?)
Memory Controller (Why not SW?)
Traffic Light Controller (Why not HW?)
Elevator Controller (Why not HW?)
FIR/IIR Filters (Why not FSM?  Datapath)
PLC (programmable logic controller) (Why not HW?)
JTAG TAPC (test access port controller) (Why not SW?)

## Slide 51: Lab04 Counters
Binary Counters with/without properties:
  Loadable: data, LOAD-control
  Resettable: Rst-control
  Up/Down Counting
  Stride/Step/Increment
  Start/End
  Recount/Stop at end
  Synchronous/Asynchronous for each control
  Johnson, Ring Counters, LFSR Counters
  Snake
Problem 1. Complete all the combinations in this lab.