## Slide 1
Hardware Description Language
-- Logic Design using Verilog
Tsung-Chu Huang
Dept. of Electronic Eng.
National Changhua University of Ed.
Email: tch@cc.ncue.edu.tw
2022/10/13

## Slide 2
Huffman Model for a Finite State Machine
Single Clock, Synchronous, DFF-based
Q
D
Q
D
Q
D
Q
D
Combinational
Circuit
PI:
Primary Inputs
PPI:
Pseudo PI
PO:
Primary Outputs
PPO:
Pseudo PO
Clk
M
L
N
M
X
Z
Q
y
D
Y
NS: Next State
PS: Present State

## Slide 3: Common Finite State Machines
Sequence Detectors:
General Counters:
  Binary Counters:
  Ring Counters:
  Johnson Counters:
  Linear Feedback Shift Registers:
Timed Buttons:
  Debouncer:
  Morse Codes:
Controllers:
  Memory/CPU Controllers:
  TAPC (Test Access Port Controller, JTAG, IEEE1149.1):

## Slide 4
Classification of FSM’s
Mealy Machine: The outputs are dependent on both the state and the input.
Moore Machine: The outputs are dependent on only the present state.
Combinational
Circuit

## Slide 5
State Diagram
Example of Mealy Machine: A Lock with Password 1011
Waiting for
1011
Waiting for
011
1/0
1/0
Waiting for
11
0/0
0/0
Waiting for
1
1/0
0/0
1/1
0/0
00
01
11
10

## Slide 6
State Table & Flow Table
Q |  | X | D |  | Z
Q1 | Q0 | X0 | D1 | D0 | Z0
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 1
K-map or
McKlusky Method:
Q
D
0
Q
D
1
X
Z
Transition Table

## Slide 7
Typical Verilog Description
Example of Mealy Machine: A Lock with Password 1101
module Lock(Clk, X, Z)
input Clk, X;
output Z;
reg Z;
parameter W1011=2’b00, W011=2’b01, W11=2’b10, W1=2’b11;
reg [1:0] Present_State, Next_State;
always@(posedge Clk)
Present_State = Next_State;
always@(X or Present_State) begin
Next_State = Present_State;
case(Present_State)
W1011 : Next_State = X ? W011 : W1011;
W011 : Next_State = X ? W011 : W11;
W11 : Next_State = X ? W1 : W1011;
W1 : Next_State = X ? W011 : W11;
default: Next_State = W011;
endcase
case(Present_State)
W1 : Z = X ? 1 : 0;
default: Z = 0;
endcase
end // always
endmodule

## Slide 8
State Diagram
Example of Moore Machine: Recent Ones
S0
0
S1
1
S2
1
S3
2
0
1
0
0
1
0
1
1

## Slide 9
State Diagram
Example of Moore Machine: Recent Ones

## Slide 10
Typical Verilog Description
Example of Mealy Machine: A Lock with Password 1101
module Recent1s(Clk, X, Z)
input Clk, X;
output [1:0] Z;
reg [1:0] Z;
reg [1:0] Present_State, Next_State;
always@(posedge Clk)
Present_State = Next_State;
always@(X or Present_State) begin
Next_State = Present_State;
case(Present_State)
0 : Next_State = X ? 1 : 0;
1 : Next_State = X ? 2 : 1;
2 : Next_State = X ? 1 : 0;
3 : Next_State = X ? 2 : 1;
default: Next_State = 0;
endcase
end // always
assign Z = Present_State[1] + Present_State[0];
endmodule
Moore decoder from present state to output

## Slide 11
JTAG, IEEE1149.1 and Boundary Scan
Reason to Introduce this Example
  JTAG is often used in the FPGA flow for HDL practice
  It is a good example for FSM
  a common knowledge for seniors in electronic eng.
JTAG
  JTAG (Joint Test Action Group)
  IEEE 1149.1 – compatible boundary scan access port for printed circuit board-level continuity and diagnostic testing of the device in which all digital input, output, and input/output pins are tested.

## Slide 12
Hierarchical Board-level Test and Transmission
Pull them up to test?

## Slide 13
Boundary Scan
Basic Concept
TDI
TDO

## Slide 14
Boundary Scan
Background
Joint Test Action Group (JTAG) Boundary Scan Standard, 1988
IEEE P1149.1 Testability Bus Standard (Proposal), 1989
Basic Structure:
  TAP (Test Access Port) Controller
  Registers: IR (Instruction Register) and BR (Bypass Register)
  Extra Pins:
      TMS (Test Mode Singal)
      TCK (Test Clock)
      TDI (Test Data Input)
      TDO (Test Data Output)

## Slide 15
Boundary Scan
Chip Architecture for BS1149.1
Application Circuit
TDI
TDO
IR
TAPC
TMS
TCK
BR
probably with scan chains

## Slide 16
A Basic Boundary Scan Cell
IN
0
1
D
Q
D
Q
0
1
OUT
SCAN_OUT
SCAN_IN
Shift
Clock
Update
Mode
0
Normal mode
1
1
Scan mode
0
Capture mode
Update mode
Can update PIs (capture POs) simultaneously for detecting delay response.
Can be used both as input and output boundary scan cells.

## Slide 17
Basic Test Access Controller
A Synchronous Finite State Machine with 2X8 States
TestReset
Start/Iddle
1
0
0
Meta-state for
Data Operations
11
Meta-state for
Instruction Operations
1
11111

## Slide 18
State Diagram of TAPC
1
0
0
TestReset
Start/Iddle
1
SelectIR
CaptureIR
ShiftIR
Exit1IR
PauseIR
Exit2IR
UpdateIR
0
0
1
0
1
1
1
1
0
1
0
1
SelectDR
CaptureDR
ShiftDR
Exit1DR
PauseDR
Exit2DR
UpdateDR
0
0
1
0
1
1
0
1
0
0
1
1
0
1
0
0

## Slide 19
Boundary Scan
Exercise with TI BS1.0
Exercise and trace some examples using TI Scan Educator 1.0 (downloaded from TI or my web).
Write the basic TMS sequence for applying a pattern and detecting the result to a circuit under test (CUT) originally with 4 pins.
Hint: Initialization, Scanning in 4 bits, Update, Capture, Scanning out 4 bits, Update.
Homework #2: Design a Boundary Scan Control according to the above state diagram using Verilog (due in 2 Weeks)
You can trace it by comparing to TI Scan Educator 1.0

## Slide 20
Counter/Timer Based State Machine
Counters in General Sense
Binary Counter
  Ripple Counter: Toggle FFs triggered by Input.
  Parallel counter takes much space while FSM design takes much time.
Gray Counter
  Minimum transition count for low power, low noise application
Shifting Counter
  Incomplete coding.
  Almost zero propagation time in Huffman model of sequential circuits → Fastest
  Examples:
    Ring Counter
      1-hot code for some direct or fast application
    Johnson Counter
      Fastest and with 2N states
    LFSR (Random) Counter
      Random number generation, random test and compression
      Decoder required for use as counter.

## Slide 21
Counter/Timer Based State Machine
Combination of Counter and FSM
Counter
Data
Load
Reset
Up/Down
Clock
Q
Si
Sj
Triggered by some state
Initialized by some state
Sk
Decoder
Or
Comparator
Decode to some inputs of FSM
S2
S4
S3
S1
Sn

## Slide 22
Transferring Multiple-Cycles States
Using a Shared Resettable Counter and Comparators
delay
n cycles
Si
Si+n+1
Ii /Oi
/Oi+n
Si
Si+n+1
Si+n
Si+1
Ii /Oi
/Oi+n
Si
c++
Sc
Si+n+1
c==n /Oi+n
c<n
Ii+n /Oi+n,c=0
< n

## Slide 23
Example
Basic Traffic Lights
Problem Formulation
  Normal Procedure: 15 sec green → 5 sec yellow → 60 sec red.
  If the button pressed
    Green: the rest time < 10, extend it to 10 sec.
    Yellow or red: shorten the next period of the red light to 15 sec.
  Assumed 1KHz Clock is supported.
  An RC-delay with an enough time constant used as Power-On state. The lights may be at any state just prior to power-on. At the moment of Power-On, initialize the counter and give 60 sec red light for safe.
Power-On
Button
Clock

## Slide 24: Lab05 Button-Press Timer
Design a 4Hz frequency divider
Draw the 3-state state diagram.
Show the button press time on the 7Seg LEDs
Separate the duration into 2 or 3 periods and show the results on the green LEDs.
Problem 1. Design a sequence detector for receiving 1011.
Problem 2. Can you design the Morse Codes by yourself now?