## Slide 1: FSM-Based Design for Hex-decimal Morse Code in DE0/Cyclone III
Tsung-Chu Huang
2022/10/20
NCUE

## Slide 2: Outline
Introduction to Morse Codes
Experiment:
  Frequency Divider:
    Sampling Debounce: tB~0.1ms < T=1/f < tK~0.1s
    Timer: short di < 0.25s < long da < 1.2 s
  IU: 4-Bit Morse Code-like
  OU: 4-Digit Scroll-Left Hexidecimal LEDs
State Diagram
  3-State FSM: easily understood
  8-State FSM: flexible for extension
Coding and Demonstration

## Slide 3: Standard Morse Codes
Properties:
  applied for 160 years
  1~5 bits, variant
  Huffman-code-like, efficient (the more frequent the shorter)
  Di:Da:NextChar ~ 1:3:5 or 7

## Slide 4: 4 7-Seg LEDs as OU
R22 J3-2
P21 J3-1
Hexidecimal [15:0] reg H
Scroll left for possible extension
Buttons 0-2: RstN, EntN, KeyIn
Scroll-left register H records current digits
P21, R22 for later extension

## Slide 5: Debouncer for Buttons or Keys
Single-Pole Double Throws (1P2T, 單刀雙投)
  Floating Transitions
Single-Pole Single-Throws (1P1T)
  Possible Single Floating Transitions
  Possible Both Bi-stable Bouncing
(1) Latching
tK
tB
VDD
VOUT
(2) Schmitt
Trigger
(1) Latching
1-shot
(3) Masking
(4) FSM
Sync.
Async.
(5) Sampling

## Slide 6: Frequency Divider and Timer
Debounce & Timer: select f = 100Hz
Timer: 7 bits are enough (0~127), Unit: 10ms
1:3:5  short-time threshold ~ 25 units
Overtime: stop incrementing
reg [18:0] FD;
always@(posedge Clk50MHz) FD = FD + 1;
assign Clk100Hz = FD[18];
reg [6:0] T;
always@(posedge Clk100Hz)
T = (PS == ClearState) ?
0 :
(T==127) ? 127 : T+1 );

## Slide 7: Typical FSM Template
reg [1:0] PS, NS;
always@(*)
case(PS)
endcase
always@(posedge Clk100Hz)
if (!RstN) begin
end
else begin
end
Combinational
Circuits
always@(*)
assign wires =
Gate g1( , , );
PS
other
reg
S1: NS = … ;
S2: NS = … ;
H = 0; …
PS = NS;
Other reg = … ;

## Slide 8: 3-State FSM for b-bit KeyIn
Take short time (Di) or long time (Da) as 0/1
Constant bit count, eg. 4-bit hexidecimal (16) Morse-like Codes
b records for the current bit count
Code Digit X records previous bits
Scroll-left register H records current digits

## Slide 9: Coding Step by Step : FSM Template
always@(*) case(PS)
HIGH: NS = KeyN ? HIGH : LOW;
LOW : NS = KeyN ? RISE : LOW;
RISE: NS = HIGH;
endcase
always@(posedge Clk100Hz)
if(!RstN) begin PS = S1; H=0; X=0; b=0; end
else begin PS = NS;
case(PS)
HIGH: T=0;
LOW : T= (T==e) ? T : T+1'b1;
RISE: if(T<L) if(b==3) begin b=0; H = {H[11:0], X, B}; end
else begin b = b+1; X = {X[1:0], B}; end
else H = {4'b0, H[15:4]};
endcase
end

## Slide 10: Coding Step by Step : Observation
always@(*) case(PS)
HIGH: NS = KeyN ? HIGH : LOW;
LOW : NS = KeyN ? RISE : LOW;
RISE: NS = HIGH;
endcase
always@(posedge Clk100Hz)
if(!RstN) begin PS = S1; H=0; X=0; b=0; end
else begin PS = NS;
case(PS)
HIGH: T=0;
LOW : T= (T==e) ? T : T+1'b1;
RISE: if(T<L) if(b==3) begin b=0; H = {H[11:0], X, B}; end
else begin b = b+1; X = {X[1:0], B}; end
else H = {4'b0, H[15:4]};
endcase
end

## Slide 11: Coding Step by Step : Implied State
always@(*) case(PS)
HIGH: NS = KeyN ? HIGH : LOW;
LOW : NS = KeyN ? RISE : LOW;
RISE: NS = HIGH;
endcase
always@(posedge Clk100Hz)
if(!RstN) begin PS = HIGH; H=0; X=0; b=0; end
else begin PS = NS;
case(PS)
HIGH: T=0;
LOW : T= (T==e) ? T : T+1'b1;
RISE: if(T<L) if(b==3) begin b=0; H = {H[11:0], X, B}; end
else begin b = b+1; X = {X[1:0], B}; end
else H = {4'b0, H[15:4]};
endcase
end
HIGH
T=0
RST

## Slide 12: Coding Step by Step : INIT & IDLE
always@(*) case(PS)
HIGH: NS = KeyN ? HIGH : LOW;
LOW : NS = KeyN ? RISE : LOW;
RISE: NS = HIGH;
endcase
always@(posedge Clk100Hz)
if(!RstN) begin H=0; X=0; b=0; PS = HIGH; end
else begin PS = NS;
case(PS)
HIGH: T=0;
LOW : T= (T==e) ? T : T+1'b1;
RISE: if(T<L) if(b==3) begin b=0; H = {H[11:0], X, B}; end
else begin b = b+1; X = {X[1:0], B}; end
else H = {4'b0, H[15:4]};
endcase
end
HIGH
T=0

## Slide 13: Coding Step by Step : Timing
always@(*) case(PS)
HIGH: NS = KeyN ? HIGH : LOW;
LOW : NS = KeyN ? RISE : LOW;
RISE: NS = HIGH;
endcase
always@(posedge Clk100Hz)
if(!RstN) begin H=0; X=0; b=0; PS = HIGH; end
else begin PS = NS;
case(PS)
HIGH: T=0;
LOW : T= (T==e) ? T : T+1'b1;
RISE: if(T<L) if(b==3) begin b=0; H = {H[11:0], X, B}; end
else begin b = b+1; X = {X[1:0], B}; end
else H = {4'b0, H[15:4]};
endcase
end
HIGH
T=0
LOW
T++

## Slide 14: Coding Step by Step : Process
always@(*) case(PS)
HIGH: NS = KeyN ? HIGH : LOW;
LOW : NS = KeyN ? RISE : LOW;
RISE: NS = HIGH;
endcase
always@(posedge Clk100Hz)
if(!RstN) begin H=0; X=0; b=0; PS = HIGH; end
else begin PS = NS;
case(PS)
HIGH: T=0;
LOW : T= E ? T : T+1'b1;
RISE: if(E) H = {4'b0, H[15:4]};
else if (b==3) begin b=0; H = {H[11:0], X, B}; end
else begin b = b+1; X = {X[1:0], B}; end
endcase
end
HIGH
T=0
LOW
T++
RISE
HXBb
assign B = (T>s);
assign E = (T==e);

## Slide 15
always@(posedge Clk)
Present_State  Next_State;
Combinational Circuits
// Look-Up-Table-Style
always@*
case (input)
case1: value= ;
case2: value= ;
endcase
// Combinational Netlist
GATE1 g1(…);
GATE2 g2(…);
Module1 u1(…);
Module2 u2(…);
// RTL Style with formulation
assign F = Arithmetic/Logic-representation ;
Synchronous Finite State Machine Design

## Slide 16
FALL
HIGH
LOW
RISE
Basic 4 Meta States of a Button
I = 1
I = 0
T1
T1=0
T2=0
T2

## Slide 17
Then you can separate to macro states:
T1
Timing
Timing
Clock Reset
Clock Reset
Operation1
Symbol4
Symbol3
Timing
Operation1
Symbol4
Symbol3

## Slide 18
RISE
T ?
HEAD
T=0
HIGH
T=T+1
FALL
T ?
TAIL
T = 0
LOW
T=T+1
K = 1
K = 0
K = 1
K = 0
always@(posedge Clk)
EOL/EOW/?
0/1/?

## Slide 19: Synchronous Design
Synchronous Design:
  Single-Clock FSM
  Be careful of
    Glitches of Frequency-Divider and Clock-Generator
    Glitches of NS-Logic
    Error between Button and Clock
Asynchronous Design:
Note: Event-Dependencies
  ↑Key asynchronously resets High-Timer TH
  ↓Key asynchronously resets Low-Timer TL
  Prevent from Timers’ overflows.  Stop counting.

## Slide 20: Lab07 Hexadecimal Morse Codes
Practice:
  Design a 3-state hexadecimal Morse Codes
  Extend to a fixed-length word
  Extend with backspace functions
Problems:
Note: Event-Dependencies
  ↑Key asynchronously resets High-Timer TH
  ↓Key asynchronously resets Low-Timer TL
  Prevent from Timers’ overflows.  Stop counting.