## Slide 1: UART Transmitter and Receiver
Tsung-Chu Huang
NCUE
2022/10/27

## Slide 2: Outline
Review of 4-bit Morse Codes and Display
Introduction to RS232 & PS/2 Connectors
Introduction to basic UART
Block Diagrams
Counter Extraction from Macro-States
  Transmitter Tx
  Receiver Rx
Coding
Demonstration

## Slide 3: Reviewing 4-Bit Morse Code
always@(*) case(PS)
HIGH: NS = KeyN ? HIGH : LOW;
LOW : NS = KeyN ? RISE : LOW;
RISE: NS = HIGH;
endcase
always@(posedge Clk100Hz)
if(!RstN) begin H=0; X=0; b=0; PS = HIGH; end
else begin PS = NS;
case(PS)
HIGH: T=0;
LOW : T= E ? T : T+1'b1;
RISE: if(E) H = {4'b0, H[15:4]};
else if (b==3) begin b=0; H = {H[11:0], X, B}; end
else begin b = b+1; X = {X[1:0], B}; end
endcase
end
HIGH
T=0
LOW
T++
RISE
HXBb
assign B = (T>s);
assign E = (T==e);

## Slide 4: Simple Channel via PS/2
R22 J3-2
P21 J3-1
Hexidecimal [15:0] reg H
Scroll left for possible extension
Buttons 0-2: RstN, EntN, KeyIn
Scroll-left register H records current digits
P21, R22 for later extension
Convenient for stripped wires instead of Dupone lines.

## Slide 5: UART, RS232 & PS/2
RS232 is a set of standards including the electrical properties and data properties.
PS/2 is an extension of serial port SPI with 2 set of UARTs.
UART
RS232
PS/2
Connectors
Vcc
Cable
etc.
Connectors
Vcc
Cable
Synchronous
Or Async.
etc.

## Slide 6: Spec in this Experiment
8 Data Bits + Start/Stop Bits
Baud Rate: 9.6kbps (bit per second)
System Clock: Clk50MHz
D0
D1
D2
D3
D4
D5
D6
D7
Start
Stop
Rx
Tx
Rx
Tx
R22
P21
P21
R22

## Slide 7: IU-Tx/Rx-OU Block Diagram
Send
Tx
Data
Enter
Data
SysClk1
Clk50MHz
SampleClk
RstN
RstN
KeyN
IN
Ready
Ready
Rx
EN
Data
Data
SysClk2
Clk50MHz
EN

## Slide 8: Tx State Diagram
D0
D1
D2
D3
D4
D5
D6
D7
Start
Stop
b= 0
1
3
5
7
9
2
4
6
8
10
Idle
Start
b=0
R←H
Shift
t=0
b++
Shift
Elapse
t++
t=T
Reset
EntN
b=10
!EntN
case(b)
0: Out=0
9: Out=1
others: shift (Out, R)

## Slide 9: Rx State Diagram
Idle
Start
b=0
E=0
t=0
E=!E
Shift
Eb++
Elapse
t++
t=T/2
Rest
1
0
if(E) case(b)
0: (push)
9: (flash, pop)
others: shift (R, In)
D0
D1
D2
D3
D4
D5
D6
D7
Start
Stop
b= 0
1
3
5
7
9
2
4
6
8
10

## Slide 10: Another Rx State Diagram
D0
D1
D2
D3
D4
D5
D6
D7
Start
Stop
b= 0
1
3
5
7
9
2
4
6
8
0
Rest
START
ZERO
SAMPLE
Idle0
Idle1
HALF
PERIOD
READY
1
1
0
T=0
T==H
b=0
b++
T++
T++
T==P
b==8

## Slide 11: Baud Rate and Half-Period Frequency
Baud rate = 9.6kbps  ,
If , modulo count M = /
M = 2604.167 ~ 2,604  count from 0 to 2602 + 1 state for setting
Skew allowance = 1/(2*Length) x 100% ~
reg [12:0] T;
always@(posedge Clk50MHz)
case(PS)
START : b=0;
RESET : begin T=0; (processing;) end
ELAPSE: T = T + 1;
endcase
always@(*)
case(PS) ...
S2 : NS = b==10 ? IDLE : ELAPSE;
ELAPSE: NS = T==(M-2) ? NEXT : ELAPSE;
endcase

## Slide 12: UART Transmitter and Receiver (Corrected & Updated)
Tsung-Chu Huang
NCUE
2018/11/30

## Slide 13: Another Rx State Diagram
D0
D1
D2
D3
D4
D5
D6
D7
Start
Stop
b= 0
1
3
5
7
9
2
4
6
8
0
Rest
START
ZERO
SAMPLE
Idle0
Idle1
HALF
PERIOD
READY
1
1
0
T=0
T==H
b=0
b++
T++
T++
T==P
b==8

## Slide 14: Blocking/Nonblocking Syntheses
// Blocking
always@(posedge Clk)
begin
A = B;
B = A;
end
FF
D1
Q2
D3
Q4
Clk
Latch
D1
D2
Q1
Q2
D3
D4
Q3
Q4
Clk
// Nonblocking
always@(posedge Clk)
begin
A <= B;
B <= A;
end

## Slide 15: Reviewing 4-Bit Morse Code
always@(*) case(PS)
HIGH: NS = KeyN ? HIGH : LOW;
LOW : NS = KeyN ? RISE : LOW;
RISE: NS = HIGH;
endcase
always@(posedge Clk100Hz)
if(!RstN) begin H=0; X=0; b=0; PS = HIGH; end
else begin PS = NS;
case(PS)
HIGH: T=0;
LOW : T= E ? T : T+1'b1;
RISE: if(E) H = {4'b0, H[15:4]};
else if (b==3) begin b=0; H = {H[11:0], X, B}; end
else begin b = b+1; X = {X[1:0], B}; end
endcase
end
HIGH
T=0
LOW
T++
RISE
HXBb
assign B = (T>s);
assign E = (T==e);

## Slide 16: Baud Rate and Half-Period Frequency
Baud rate = 9.6kbps  ,
If , modulo count M = /
M = 2604.167 ~ 2,604  count from 0 to 2602 + 1 state for setting
Skew allowance = 1/(2*Length) x 100% ~
reg [12:0] T;
always@(posedge Clk50MHz)
case(PS)
START : b <= 0;
RESET : begin T<=0; (processing;) end
ELAPSE: T <= T + 1;
endcase
always@(*)
case(PS) ...
S2 : NS = b==10 ? IDLE : ELAPSE;
ELAPSE: NS = T==(M-2) ? NEXT : ELAPSE;
endcase