## Slide 1: HDL Scripting in Python with case study on CORDIC and VGA display by Cyclone III
Tsung-Chu Huang
IC-TestLab NCUE, Taiwan
2022/11/24

## Slide 2: Outline
Scripting
Case Study: CORDIC
  generate/endgenerate Block
  Fixed-Point and Floating-Point Calculation
    Overflow and Sign-Extension Traps
OU: VGA Display
  Display Interface
    Equation-Satisfied Coordinate Patterns
    2-port (w/r) Memory Mapping
MU:
    W/R basics
Coding & Demonstration

## Slide 3: Scripting/Shell
Scripts:
    Simple Command Rows Integrating Programs to System
OS
APP Programs Utilities
Shell Scripts
Package/OS | Scripts | Interpreter
DOS | Some_batch.BAT | OS Shell
UNIX/Linux | sh, csh, tcsh, bsh | OS Shell
MS Office | VBA | Office
Cross OS | perl | Perl package
Cross OS | python | python pkg
Cross OS | General Language | Compiler
Cadence CAD | SKILL | CAD pkg
Other CAD | tcl | CAD pkg

## Slide 4: Straight-Translation Synthesis
Simple synthesizer without decision & optimization
  Define/modify parameters
  fprintf(fp, "module Circuit(Clk, In, Out, %d);", Param);
  system("vsim Circuit.v –do some.tcl");
Useful Scripting
matlab
c
python
Verilog
SPICE
tcl
batch

## Slide 5: Case Study: CORDIC
Although similar math proposed by Briggs in 1624
COordinate Rotation DIgital Computer (Volder, 1956)
General CORDIC Conditions:
=Tx

## Slide 6: Case Study: CORDIC
h
h
Select
such that
; ; s = +1;

## Slide 7: General Superfunctions for CORDIC
No. | Functions
1 | 
2 | 
3 | 
No. | Functions
1 | 
2 | 
3 | 
Currently-Found Superfunctions:
Inverse functions can be also solved.
Can you expand a non-superfunction to a superfunction such that ?

## Slide 8: Fixed-Point and Sign Extension
Fixed-Point Operations
  Let <i, m> as a fixed-point format with i-bit integer and m-bit mantissa.
IEEE1364-1995
  Take care of 2’s complement operations by yourself.
  reg [6:0] a=7’b1101010 ; // <3.4>=-1.375
  reg [9:0] b = { 3{a[6]}, a} ;
  Try to transfer to the maximum-length wires/reg before operations.
IEEE 1364-2001
  Declare 2’s-complement as reg signed [6:0] a=-22;
  Take care of the point position by yourself.

## Slide 9: Floating-Point Operations
IEEE 754:
  Fraction (分數)is the rest deducted the integer part of a real number.
  Mantissa (尾數)is the tail cut off integer bit of a number 1.M
  Exponent is an offset-integer with base-2 exponent E=E' -
  Extended widths for operations and normalized for final formats.
Custom FP operations: extra position integer p
  Derive the maximum positive M and minimum negative m and expected resolution with b-bits of fraction
   width of p =
m-bit mantissa M (m=23 for 32-bit or 52 for 64-bit)
e-bit exponent E’
s

## Slide 10: Parallel CORDIC.v
parameter N, W, Kn= …;
parameter a[0:N]= …; // Look-Up Table
module CORDIC(theta, cos, sin);
input [W-1:0] theta;
output [W-1:0] cos, sin;
wire [W-1:0] x[0:N], y[0:N], z[0:N]; //<2.W-2>
assign z[0] = theta;
assign x[0]=Kn;
assign y[0]=0;
genvar i;
for(i=0; i<N; i=i+1) begin : Stage
AddSub U1(!z[i][W-1], x[i+1], x[i], y[i]>>i);
U2(z[i][W-1], y[i+1], x[i]>>i, y[i]);
U3(!z[i][W-1], z[i+1], z[i], z[i]);
end
assign cos = x[N];
assign sin = y[N];
endmodule
module AddSub(A, X, Y, S);
… assign S = X + A ? Y : ~Y + 1; endmodule

## Slide 11: Pipeline CORDIC.v
parameter N, W, Kn= …;
parameter a[0:N]= …; // Look-Up Table
module CORDIC(Clk, theta, cos, sin);
input Clk;
input [W-1:0] theta;
output [W-1:0] cos, sin;
wire [W-1:0] x[0:N], y[0:N], z[0:N]; //<2.W-2>
assign z[0] = theta;
assign x[0]=Kn;
assign y[0]=0;
genvar i;
for(i=0; i<N; i=i+1) begin : Stage
AddSub U1(Clk, !z[i][W-1], x[i+1], x[i], y[i]>>i);
U2(Clk, z[i][W-1], y[i+1], x[i]>>i, y[i]);
U3(Clk, !z[i][W-1], z[i+1], z[i], z[i]);
end
assign cos = x[N];
assign sin = y[N];
endmodule
module AddSub(Clk, A, X, Y, S);
… always@(posedge Clk) S = X + A ? Y : ~Y + 1; endmodule

## Slide 12: Serial CORDIC.v
parameter N, W, Kn= …;
parameter a[0:N]= …; // Look-Up Table
module CORDIC(Clk, Rst, theta, cos, sin, Rdy);
input Clk; output Rdy;
input [W-1:0] theta;
output [W-1:0] cos, sin;
wire [W-1:0] x[0:N], y[0:N], z[0:N]; //<2.W-2>
reg i;
reg [W-1:0] Rx, Ry, Rz;
AddSub U1(Clk, !z[i][W-1], x[i+1], x[i], y[i]>>i);
U2(Clk, z[i][W-1], y[i+1], x[i]>>i, y[i]);
U3(Clk, !z[i][W-1], z[i+1], z[i], z[i]);
always@(posedge Clk) if(Rst) begin x[0]=Kn; y[0]=0; z[0] = theta;
i=0; Rdy = 0; end
else if(i==32) Rdy = 1;
else begin i=i+1; Rx = x[i]; Ry = y[i]; Rz = z[i]; end
assign cos = x[N]; assign sin = y[N];
endmodule
module AddSub(A, X, Y, S);
… S = X + A ? Y : ~Y + 1; endmodule

## Slide 13: Why Scripting
Why Scripting
  No commands for iterating in App.
  Irregularly duplicating.
  Parameter calculating outside of APP.
  Variety of designs.
  Many iterations for timing/power closure and experiments.
How Scripting
  Try small designs in APP.
  Draft the scripts for design and TCL.
  Plan what you need.
  Increase the options in scripts.

## Slide 14: Simulation Environments
Tools Installation in Windows
  ModelSim (command-line: vsim)
  Python/numpy/matplotlib
  Note: Add paths to system variables
Scripting Flow
ModelSim
Python
def CORDIC
… … … …
Script.py
module CORDIC(
… … … …
Design.v
vlog Design.v
… … … …
vsim.tcl
# data
# 1.234 701
… … … …
Transcript
Comparison:
… … … …
Report
initial begin
… … … …
Testbench.v
Rapid
Prototyping

## Slide 15: Rapid Prototyping Environments
Facility & Tools Installation
  Quartus II Synthesizer with DE0/EP3C
  VGA Display (also as a case for OU study)
Verification Flow

## Slide 16: VGA Display Principle

## Slide 17: Horizontal and Vertical Synchronization

## Slide 18: Cycles in a Frame in 60Hz
Then the pixels in a h scan:
48 + 640 + 15 + 96
Then the controller is responsible to
  Generate vsync and hsync clocks
  Sending data after behind vertical sync.
VGA
640 pixels,
480 Lines
525 Lines
33
10

## Slide 19: DE0 Template: DE0_Default
CORDIC_Test
VGA_Ctrl
VGA_Clk
VGA_OSD_RAM
IMG_RAM
DE0_CORDIC
CORDIC