## Slide 1
Hardware Description Language
-- Logic Design using Verilog
Tsung-Chu Huang
Dept. of Electronic Eng.
National Changhua University of Ed.
Email: tch@cc.ncue.edu.tw
2022/09/15

## Slide 2: Reference Book
Reference Book Mark Gordon Arnold. Verilog Digital Computer Design: Algorithms into HardwareI, ISBN: 0136392539, Prentice Hall PTR, 1999.
Lecture Site https://dlearn.ncue.edu.tw
Website http://testlab.ncue.edu.tw/tch [lecture]
Tools ModelSim-Altera, Quartus II, EP3C16K
Average duration: 2W 9:05-12:00, 15W 8:30am-12:00 - possible 1 leave for conference
Evaluation HW+Quiz 5% x 4 Practice Test 20% x 2 Paper Exam 20% x 2 Bonus Project 20% x 1 (optional)

## Slide 3: Terasic Altera DE0 Cyclone III Design Kit
Device: SoPC (System-on-a-Programmable-Chip) EP3C16F484C6N
Design Kit (software) Quartus II 9.0~13.1 Web Edition (free) DE0 DVD9 design kit: https://drive.google.com/drive/folders/141If6V7_K0ndAU6K5cDORBqskcYo-uen?usp=sharing [ETC/DE0] Install by next week!
eNgineering sample
speed
#pins = 22x22
Flip-chip package
#LEs =16k
Cyclone III
EPROM  Flash
Intel® Quartus® II Web Edition Design Software Version 13.1 for Windows https://www.intel.com/content/www/us/en/software-kit/666221/intel-quartus-ii-web-edition-design-software-version-13-1-for-windows.html

## Slide 4: Syllabus
Mn | Topics | W | Lec. | Content | Lab | Content
1st | Verilog Language ModelSim I/O | 1 | 01 | Overview | 01 | N-bit Adder
 |  | 2 | 02 | View, Level, Hierarchy | 02 | FFs, Cnt, fDiv
 |  | 3 | 03 | Type, Op, 4Mdl,8Blks | 03 | 7Seg, BCD_Timer
 |  | 4 | 04 | ASM, Serial Multipliers | 04 | Scroll Snake
2nd | Quartus II Design Flow CU | 5 | 05 | Exam, FSM | 05 | Button-press time
 |  | 6 | 06 | Morse Codes | 06 | Morse Codes
 |  | 7 | 07 | UART | 07 | UART
 |  | 8 | 08 | Setup-Hold Timing | 08 | Multiplication timing closure
3rd | EDA Scripting ALU, MU | 9 | 09 | Exam, Fixed-Point | 09 | Practice
 |  | 10 | 10 | Booth Multipliers, IEEE754 | 10 | Booth EDA Scripts
 |  | 11 | 11 | CORDIC, ROM | 11 | CORDIC EDA Scripts
 |  | 13 | 12 | ROM &RAM | 12 | Memory Controller
4th | CPU design in Verilog | 14 | 13 | Intro CPU Design, SAP3x5 | 13 | SAP3x5
 |  | 15 | 14 | SAP444 | 14 | SAP444
 |  | 16 | 15 | Introduction to MIPS | 15 | Tiny MIPS
 |  | 17 | 16 | SPIM and Implementation | 16 | SPIM Assembly
 |  | 18 | - | Bonus Proj. | Exam | Practice
W3, 7, 11, 16 8:30am quiz; W5, 14 paper exam; W9, 18 practice exam

## Slide 5
Hardware-Descriptive Language
硬體描述語言
軟硬有別：Speed, Power, (Chip) Area, Cost, EZ
軟硬不分：軟硬體在一定前提下可以互換
軟硬共設計：考慮前提決定軟硬架構比例最佳化
This Course:
  Logic Design硬體基礎 (電子二)
  描述硬體的軟體
  設計CPU、指令及其組合語言
  設計組合語言軟體
  由C語言演算法轉換成Verilog硬體有限狀態機
  (甄戰 !!!)

## Slide 6
Overview on HDL
Introduction to General HDL including NETLIST
Competition btw VHDL and Verilog
HDL Tools
Application of VLSI HDL
Y-Chart: Level and Views
Modeling
Quick Tutorial using 1 or 2 Tools
  Gate-Level
  Behavioral Mode
Preparation for Next Course

## Slide 7
Usual Applications of HDLs
Logic Simulation and Verification
Synthesis for FPGA/SoPC Prototyping
Synthesis for Cell-base VLSI Design
Soft Intellectual Property (IP) Design
Modeling Low or Equal Level Circuit

## Slide 8
HDL in General Sense
Schematic/Graph
Text Language
Gate-Level Above
Transistor-Level
module adder(A, B, C, S);
input [31:0] A, B;
output [31:0] S;
output C;
…
ends
VDD V 0 3V
M1 Z IN 0 0 NCH
M2 Z IN V V PCH
R1 A IN 15
C1 Z 0 1P
VIN A 0 PWL(0 0 1N 3V)
VDD
A
IN
Z
NETLIST
HDL
SCHEMATICS

## Slide 9
Major HDLs in Common Sense
Academic
Industry
VHDL
Verilog
VHDL
Verilog
VHDL
(1980)
Verilog
(1990)
SystemVerilog
(2000)
Gate Level
Transistor Level
RTL
System Level
SystemC
(2000)
HLS
C++
(2010)
SPICE
(1970)
Verilog-A
Analog
Mixed-Signal
Digital
} format
engine {

## Slide 10
History of Major HDLs
Year | VHDL | Verilog | SystemC
1971 |  | Paul Huang (黃炎松), NCTU-E59 | 
1981 | US Defense, Spec of ASIC |  | 
1982 |  | Paul founding Cadnece | 
1983 |  | Prabhu Goel, Automated Integrated Design Systems | 
1984 |  | Phil Moorby, renamed to “Gateway Design Automation” | 
1987 | IEEE S1076 |  | 
1990 |  | purchased by Cadence →Verilog XL | 
1990 |  | Open Verilog International (OVI) →Accellera | 
1992 |  | IEEE Grouping | 
1995 |  | IEEE S1364 | 
2001 |  | IEEE S1364-2001:Scalability | 
2005 |  | IEEE S1364-AMS, 1800 System-Verilog | 
2008 | IEEE S1076-2008 |  | 
2011 |  |  | IEEE S1666

## Slide 11
List of HDL Simulators
VerilogXL, LeapForm, LDV, NCV /Cadence
ModelSim /Mentor (Download ModelSim-Altera Starter Edition)
VSS /Synopsys
Vantage /ViewLogic
Silos /SimuCAD
Verilogger Pro /SynaptiCAD (http://www.syncad.com)
ActiveHDL /Aldec
VeriBest /VeriBest
VeriWell /VeriWell
Debussy /SpringSoft
VCS /Chronologic
FrontLine /FrontLine
Silos /SimuCAD
HDL Entry in FPGA Co., e.g., Max/Quartus(Altera), ISE(Xilinx)
IEEE Standard 1364-2001

## Slide 12
Preparation for Next Courses
Install Intel-Altera Quartus II 13.1 including Cyclone III and ModelSim from https://www.intel.com/content/www/us/en/software-kit/666221/intel-quartus-ii-web-edition-design-software-version-13-1-for-windows.html
Try a Verilog Online.
Exercise Schematics Tools by Yourself (E.g., OrCAD/Schematic may be the most popular and basic tool)
This course will start from 8:30am every Thursday.
Scores:
  Quiz or Practice: 8:30am Week 3, 7, 11, 15. 5% per quiz
  Paper Exam: Week 5, 13. 20% per exam
  Practice Exam: Week 9, 18. 20% per exam
  Bonus Project: “Tiny MIPS on Cyclone III”, demo by SPIM. 20%

## Slide 13: Levels & Views
Circuit-Level
Physics-Level
Transistor-Level
Logic-Level
Register-Level
System-Level
Board-Level
Behavioral-View
Structural-View
Physical-View
Functional-View

## Slide 14: Y-Chart
Gajski transferred the level-view table into a sphere chart:

## Slide 15: SoC EDA
Behavioral
Structural
Physical
modularization
partitioning
library
synthesize
sim
ver

## Slide 16: Usual Levels & Views
Logic-Level
Register-Level
System-Level
Behavioral-View
Structural-View
Physical-View
“Behavioral Mode”
“RTL Mode”
“Gate-Level”

## Slide 17
Program
||
Algorithm
+
Data Structure
Internal & External Models

## Slide 18: Structural & Functional Models

## Slide 19
Structural Models
Recursive Definition
Symbol View: A system or circuit can be represented by a symbol with its function.
A Structural View of a system (or circuit) is a representation or model that consists nodes for subsystems (or subcircuits) and elements (or components) represented by some symbol view, and arcs for their input/output relations.
Usually hierarchical.
The bottom-level boxes (components) are called primitive elements, which functional model is assumed to be known such as and, nand, or, nor, not, etc.

## Slide 20
Structural Modeling at Logic Level
External Representation
Structural Properties
Hardware Descriptive Languages
Internal Representation
Example: A Simple Verilog Parser in C Language.

## Slide 21
External Representation
Text or schematic for human.
  Connectivity specifies I/O, components with signals.
Text or Language:
  HDL: VHDL, Verilog, C, etc.
  Netlist: SPICE, gat, tdl, etc.
Schematics:
  Cadence Schedmatics
  OrCAD Schedmatics, ..etc.

## Slide 22
Structural Properties in Logic Level
Branches/Fanout
Stem
Fanout-free
Reconvergent Fanout
Gate Type
Inversion
Inversion Parity
Level of a Gate in Circuit

## Slide 23
Structural Properties in Logic Level
Example
G2
G1
G3
G4
G5
G6
G7

## Slide 24
Structural Properties in Logic Level
Example: s27 in ISCAS89 benchmark
0
1
2
3
14
12
8
16
15
13
11
17
9
10
5
6
7

## Slide 25
Internal Representation
Example: My Simple Verilog Parser
Top
module
module
module
module
module
module
Instance
Instance
Instance
Instance
Port List
Pin List
Port List
Pin List
Net
List

## Slide 26
Structure-Oriented Design Methodology
Top-Down Design
Bottom-Up
Middle-Out
Ends-In
Hybrid (Greedy)
Top
A
B
C
D
E

## Slide 27
Functional Modeling at Logic Level
Truth Table & Primitive Cubes.
State Table & Flow Table.
Binary Decision Diagrams.
Programs as Functional Models.

## Slide 28
Truth Table & Primitive Cubes
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
A | B | C | F
X | 1 | 0 | 0
1 | 1 | X | 0
X | 0 | X | 1
0 | 1 | 1 | 1

## Slide 29
Huffman Model for a Finite State Machine
Single Clock, Synchronous, DFF-based
Q
D
Q
D
Q
D
Q
D
Combinational
Circuit
PI:
Primary Inputs
PPI:
Pseudo PI
PO:
Primary Outputs
PPO:
Pseudo PO
Clk
M
L
N
M
X
Z
Q
y
D
Y
NS: Next State
PS: Present State

## Slide 30
State Diagram
(Sequence Detector) Example: A Lock with Password 1011
Waiting for
1011
Waiting for
011
1/0
1/0
Waiting for
11
0/0
0/0
Waiting for
1
1/0
0/0
1/1
0/0
00
01
11
10

## Slide 31
State Table & Flow Table
Q |  | X | D |  | Z
Q1 | Q0 | X0 | D1 | D0 | Z0
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 1
K-map or
McKlusky Method:
Q
D
0
Q
D
1
X
Z

## Slide 32
Binary Decision Diagrams
A Binary Decision Diagram (BDD) is a graph model of the function of a circuit.
B
A
B
C
0
1
C
0
1
1
0
1
0
0
1
1
0
B
C
A
0
1
F
Reduced Ordered BDD

## Slide 33
Programs as Functional Models
Assembly-Like:
  LDA A
  AND B
  INV
  OR C
  STA F
C-Like:
  main(F, A, B, C)
  { int F, A, B, C;
  F = ~ ( A && B ) || C;
  }
C-Code is the direct and fast simulator.
        C=A+B;
        A=R1*R2;
        B=~B;

## Slide 34
Functional Modeling at Register Level
Basic RTL Constructs
Timing Modeling in RTLs
Internal RTL Models (See Internal structural model)

## Slide 35
Basic RTL Constructs
RTL (Register-Transfer Language in Register-Transfer Level)
  PC←PC+1; A←A+B+C
  PC←PC+1; if C=1 PC←#FA07
  R3←A – R4; A←0
C or Verilog-like Language:
  module Adder(Co, Sum, A, B, Ci);
  Input [15:0] A, B;
  Input Ci;
  output Co;
  output [15:0] Sum;
  assign {Co, Sum} = A + B + Ci;
  endmodule

## Slide 36
Timing Modeling in RTLs
Verilog-like Code:
  Sum = #20 A+B;
  initial
  begin
  A=1; B=0;
  #10 B=1; A=0;
  #40 B=0;
  #10 $stop;
  end

## Slide 37
Tool Installation
No. | Envir. | Verilog | Link or Installation
1 | Online | CodingGround | https://www.tutorialspoint.com/compile_verilog_online.php
2 | Online | JDoodle | https://www.jdoodle.com/execute-verilog-online/
3 | Windows | SynaptiCAD (old) | http://testlab.ncue.edu.tw/tch/download/download.htm
4 | Windows | SynaptiCAD | https://www.syncad.com/syn_down.htm
5 | Windows | ModelSim-Altera | https://www.intel.com/content/www/us/en/software-kit/666221/intel-quartus-ii-web-edition-design-software-version-13-1-for-windows.html
6 | Linux | ModelSim | Usually for cell-based design, ask Administrator
7 | Linux | VerilogXL | Usually for cell-based design, ask Administrator
8 | Linux | VNC | Usually for cell-based design, ask Administrator

## Slide 38
Main Tools for this Course
Intel-Altera Quartus II 9.0~13.1
  Cyclon III
  ModelSim-Altera

## Slide 39: Outlooks of Verilog Files
1 design can have 1 files.
1 file can have modules.
Outlook of a module
module #(parameters) Name (ports);
endmodule
parameter/port declaration;
reg/wire/integer declaration;
gate netlist;
hierarchical instances;
blocks (always, initial, …)
parallel statements

## Slide 40: A library is a forest
File System
Module Forest
Top
module1
Top
module2
Top
module3
module
module
module
module
module
module
gate
gate
gate
gate
gate
gate
V2K Quick Reference: https://sutherland-hdl.com/pdfs/verilog_2001_ref_guide.pdf

## Slide 41: Terminology “Block” in Verilog
Verb: stopping the movement.  non-blocking assignment
Noun: a cuboid or a rectangle area:
  Statements: “begin (: name) … end”  grouping
  Module: “module … endmodule”  parallel statements
  Sequential: “initial (begin … end)”  sequential statements from t = 0
  Procedural: “always (begin … end)”  activated at time 0 then always “always @ (events) … “  triggled upon the events
  Generate: “generate … endgenerate”  create at time 0
  Case: “case … endcase”  switching
  Specification: “specify … endspecify”
  Function: “function … endfunction”
  Task: “task … endtask”
  UDP (user defined primitive): primitive … table … endtable endprimitive
  Configuration: config … endconfig  version and library control
  For-loops: for begin (: name) … end
  Repeat: repeat (times) begin … end

## Slide 42
Lab01 Adder