## Slide 1
Hardware Description Language
-- Logic Design using Verilog
Tsung-Chu Huang
Dept. of Electronic Eng.
National Changhua University of Ed.
Email: tch@cc.ncue.edu.tw
2022/09/29

## Slide 2
Simplified VLSI Design Flow
OK
idea
module cpu(ports)
inout ports;
:
// RTL Coding
:
endmodule
OK
Y
Y
Rapid Prototyping
Prototyping Chip

## Slide 3
Outline
Data Types and Operators in Verilog
Organic Elements in Structure View
  Module/Instance
  Ports/Nets Mapping
Four Models of HDL
  Switch/Gate/RTL/Behavioral
Two Usual Phases of HDLs
  Simulation: Event Driven
  Synthesis: Continuous/Procedural

## Slide 4
Special Letters used in Verilog
`
Left single quote
'
right single quote
#,
number sign
@,
at sign
$,
dollar sign

## Slide 5
Data Types in Verilog
Switch-Level:
Logic-Level:
  1’b0
  1’b1
  1’bz (floating, high impedance),
  1’bx (unknown)
Signal Intention of Switch | 
Input | Output
supply | pull
strong | pull
pull | weak
weak | medium
large | medium
medium | small
small | small
high | high
Constants:
  8’b01011100 8-bit Binary
  8’o377 8-bit Octal
  8’d255 8-bit Decimal
  8’haf 8-bit Hexadecimal
  ‘ha0b9 unsized hex
  255 unsized decimal
13’ h1A2F
radix
#bits

## Slide 6
Operations in Verilog
Similar to C Language
  Unary: assign a = ~b; // bitwise not
  Binary: assign a = b & c; // bitwise and
  such as: +, -, *, /, |, ^, <<, >>,
  Ternary: assign d = c ? a : b; // if 1, d=a; else d=b
Synthesizable Operators:
  Most ALU and logic operation designs are developed in library.
  In RTL model, the designs are “assigned” according to data flow.
Unsynthesizable Statements and Operators:
  Statements dependent to time or times, e.g., initial, repeat
  Switch-level
  Operators used in compiling/simulation only, e.g., ===
  Operators with no design/method in current library, e.g., / % (in some tool)

## Slide 7
Operations in Verilog
Type | Symbol | Operation
Arithmetic | * | Multiply
 | / | Divide
 | + | Add
 | - | Subtract
 | % | Modulus
 | + | Unary plus
 | - | Unary minus
Logical | ! | Logical negation
 | && | Logical and
 | ¦¦ | Logical or
Relational | > | Greater than
 | < | Less than
 | >= | Greater than or equal
 | <= | Less than or equal
Equality | == | Equality
 | != | inequality
Reduction | & | Bitwise negation
 | ~& | nand
 | ¦ | or
 | ~¦ | nor
 | ^ | xor
 | ^~ ~^ | xnor
Shift | >> | Right shift
 | << | Left shift
Concatenation | { } | Concatenation
Conditional | ?: | conditional

## Slide 8
Module and Instance
module MODULE1( … );
:
:
endmodule
module MODULE2( … );
:
:
endmodule
module MODULE3( … );
:
:
endmodule
A module is an object that
is defined as a template.
module top( … );
:
:
MODULE1 Instance1(…);
MODULE1 Instance2(…);
MODULE2 Instance3(…);
MODULE1 Instance4(…);
MODULE2 Instance5(…);
:
:
endmodule
Testbench or
Top-Module to Be Implemented:
Instances are duplicated elements in the parent module of its associated module.

## Slide 9
Port-Net Mapping
module M1(Clk, A, B);
input Clk;
inout A;
output B;
:
:
endmodule
Port (Pin) – Internal View
Net (Wire) – External View
Clk
A
B
Instance1
of M1
Wire1
Node2
Net3
They may have the same or different names.
Port Mapping in Instantiation:
  Port-Associated Mapping:
  e.g., M1 Instance1(.A(Node2), .Clk(Wire1), .B(Net3));
  Ordered Mapping:
  e.g., M1 Instance2(Wire1, Node2, Net3);
Parameter-Port Declaring and Instantiation:
  Declaration:
  e.g., module M1 #(parameter N=16)(Port1, Port2);
  Instantiation:
  e.g., M1 #(8) Instance1 (Net1, Net2);

## Slide 10
Passing a parameter
Instantiation
  Ordered mapping: ADD #(4, 8) U1 (X, Y, Sum);
  Port-associated mapping: ADD #(.M(4), .N(8)) U1(.A(X), .B(Y), .S(Sum));
Module Declaration
  Traditional: module ADD(A, B, S); parameter M=2, N=3; input [M-1:0] A; input [N-1:0] B; : endmodule
  default values should / cannot given for some compilers.
  ANSI Style: module ADD #( parameter M=2, parameter N=3) ( input [M-1:0] A, input [N-1:0] B, output [N:0] S); : endmodule

## Slide 11
Digital IC Design Automation
Switch Level Syntheses
  Physical Design Automation for Various Logic Structures.
  Primitive Logic Gates: Eular-Path Guided CMOS Layout
Gate Level Syntheses
  K-Map → McKlusky & Quintus Method: 2-Level Optimized
  Breyton’s ESSPRESSO: Multiple-Level Efficient
RTL Model Syntheses
  Data-Flow Graph Theory
  Macro Instancing from Library (Database and Rule-base)
Behavioral Model Syntheses
  Finite State Machine (FSM)
  Algorithmic State Machine (ASM) (Mapped from Flowchart)
  Rule-Base or Artificial Intellectual Techniques

## Slide 12
4 Models (Levels) of Verilog
module multiplexer(A, B, C, F);
input A, B, C;
output F;
tranif1 (F, A, C);
pmos (F,B,C);
endmodule
Switch Level Model
module SR_latch(S, R, P, Q);
input S, R;
output P, Q;
nor g1(Q, R, P);
nor g2(P, S, Q);
endmodule
Gate Level Model
(Structural Model)
module adder(A, B, Ci, Co, S);
input [31:0] A, B;
input Ci;
output Co;
output [31:0] S;
assign {Co, S}=A+B+Ci;
endmodule
operator
Register Transfer Level
(Data-Flow Model)
module counter(Clk, Q);
input Clk;
output [15:0] Q;
reg [15:0] Q;
always@(posedge Clk)
Q=Q+1;
endmodule
operator
(Behavioral Model)
(Procedural Model)
(Register-Transfer Model)

## Slide 13
Some Examples of Gate Level Design
module posedge_detector(in, out);
input in;
Output out;
not #5 (c, b), (b, a), (a, in);
nand #10 (out, in, a);
endmodule
Example 1:
Example 2: Hazard (Glitch) Elimination
0
1
1
0
1
1
0
0
AB
C
00
01
11
10
0
1
assign F=(A&B)|(~A&C);
A
B
C
F
assign F=(A&B)|(~A&C)|B&C;

## Slide 14
RTL Assignment from Library
The basic synthesis method is
  To parse an arithmetic-logic expression into a tree
  Matching parameters and checking the port-net consistencies
  Calling the instance from macro-block libraries and connecting.
A
B
C
E.g., assign A=B + ~C;
=
A
+
B
~
C
+

## Slide 15
Examples of RTL Design
module comparator(A, B, GT, EQ, LT);
parameter SIZE=16;
input [SIZE-1:0] A, B;
output GT, EQ, LT;
assign GT=(A>B);
assign EQ=(A==B);
assign LT=(A<B);
endmodule
Comp
> = <
3 to 8 decoder
1-hot code
module decode3to8(in, out);
parameter SIZE=3;
input [SIZE-1:0] in;
output [1<<SIZE-1] out;
assign out=1’b1<<in;
endmodule
1
0
A
B
module multiplexer(F, C, A, B);
input A, B, C;
output F;
assign F=C?A:B;
endmodule

## Slide 16
Bus Splitting and Concatenating
assign C={A,B};
assign {D, E}=C;
A[3:0]
B[3:0]
C[7:0]
D[1:0]
E[5:0]
assign A=C[7:4];
assign B=C[3:0];
assign D=C[7:6];
assign E=C[5:0];
assign data = 2{4'b0001, 2{3‘b011}};
0001-001-001-0001-001-001
00010010010001001001

## Slide 17
What’s Behavior
Event!
Another Event!

## Slide 18
always block / Procedural
RTL / Behavioral
initial block / Simulation only
Continuous
Basis
Non-ordered
Switch Model
Gate Model
RTL Model
Context Sequence and Timing
context
time
0
initial block / Simulation only
initial block / Simulation only
always block / Procedural
RTL / Behavioral
Compiler/system blocks
task/function/specify …
Synthesizable: Continuous and Procedural Blocks

## Slide 19
always block / Procedural
RTL / Behavioral
Continuous
Basis
Non-ordered
Switch Model
Gate Model
RTL Model
Basic Synthesis
always block / Procedural
RTL / Behavioral
Combinational
Sequential

## Slide 20
Basic Synthesis
Combinational Circuit
Continuously Exists
assign Z = f(X,Q)
assign D = g(X,Q)
X
Z
D
Q
event
Procedural behaviors
always@(event) Q←D;

## Slide 21
Events in Verilog
Inputs
Inout
Driving Events
Driven Events
Primitive Event of a Signal:
  Positive edge: posedge variable
  Negative edge: negedge variable
  Changing to another state (such as 1’bz)
Compound Events :
  Any event of a signal: variable
  Using or
  Example: always@(posedge Clk or negedge In)
Sensitivity List

## Slide 22
Time
Inputs
Inout
Simulated Circuit Time
Simulation CPU Time
Circuit Time >> CPU Time for Small Low-Speed Design
CPU Time >> Circuit Time for Large High-Speed Design

## Slide 23
Time Wheel
Internal Queue Structure for Event-Driven Simulation
Event
Circuit time
Cause & Effect
Event
Circuit time
Cause & Effect
Event
Circuit time
Cause & Effect
Event
Circuit time
Cause & Effect
Event
Circuit time
Cause & Effect
Event
Circuit time
Cause & Effect
Event
Circuit time
Cause & Effect
Event
Circuit time
Cause & Effect
Event
Circuit time
Cause & Effect
Event
Circuit time
Cause & Effect

## Slide 24
L-value and reg
Left Value:
  The variable left to the assignment of an expression in C or Verilog
Register:
  Register circuit usually denotes the flipflop array, such as counters.
  reg in behavioral mode may not necessarily be a register
  reg keeps the variable data while elapsing in simulation phase
  Declare reg for all left values in behavioral model blocks.
  reg can also define memory arrays during simulation phase.
module M1(in, out);
:
Output [7:0] out;
reg [7:0] out; // behavioral Lvalue
reg [7:0] Memory[1023:0]; //1KB
always@(Events) begin
:
out = right_expression;
:
end
endmodule

## Slide 25
8 Blocks in Verilog
Block | Outlook | Property | for-loop | index
statements | begin [:name] end | grouping |  | 
module | module #(para) ID (ports); endmodule | parallel |  | 
always | always@(events) statements; | procedural | concurrent | integer
initial | initial statements; | serial | sequential | Integer
task | task ID; endtask | procedural | sequential | integer
function | function ID; endfunction | procedural | sequential | sequential
generate | generate endgenerate |  | by time 0 | genvar
specify | specify endspecify |  |  | 

## Slide 26
Directives in Verilog
`back-quote and $dollar-sign Directives
Preprocessor
  Macro Substitutions: `define sym string
  Include Construct: `include file
  Conditional Process: `ifdef sym <Code> `endif
Simulation Directives: (Ignored by HDL Compiler)
  `timescale unit / precision
  `resetall
System Functions: (Prefixed by $)
  $display, $write: write a message to the display
  $monitor: monitoring every event
  $time: return the circuit simulation time
  $stop, $continue
  $finish

## Slide 27
Example
`include ”parts.v”
`timescale 1ns/1ps
`define high 7:4
`define Sum {C, S}
module xyz(input, output);
:
parameter five = 4’b0101;
:
Assign `Sum = Bus[`high] + five;
:
Endmodule
module testbench;
initial begin
:
$monitor($time, ”Sum=%b, Adr=%H”, Sum, A);
:
#10 $stop;
end
endmodule

## Slide 28
Command Line and Monitor
module cnt(Clk, Rst, Q);
input Clk, Rst;
output [31:0] Q;
reg [31:0] Q;
always@(posedge Clk or posedge Rst)
if(Rst) Q=0;
else Q=Q+1;
endmodule
module test;
reg Clk, Rst;
wire [31:0] Q;
cnt u1(Clk, Rst, Q);
always Clk = #10 ~Clk;
initial begin
Clk=0;
$display("------------Time---- Clk-------Q-");
$monitor("%5d %b %h", $time, Clk, Q);
Rst=1;
#15 Rst=0;
#320 $stop;
end
endmodule
------------Time---- Clk-------Q-
0 0 00000000
10 1 00000000
20 0 00000000
30 1 00000001
:
320 0 0000000f
330: 1 00000010
Stop at simulation time 335000

## Slide 29
Assignments
Continuous Assignments =
  → Simulation: Evaluate RHS and change Lvalue at 1 step when any event occurs.
  → Synthesis: Draw a wire from the RHS to the Lvalue.
Procedural Assignments
  Blocking Assignments =
    “Blocking” means to be locked at the dependency.
    Simulation: Evaluate RHS and change Lvalue at 1 step when any event occurs.
    Synthesis: Cannot be synthesized if any data dependency.
  Non-blocking Assignments <=
    Simulation: Evaluate RHS at the first phase then change Lvalue at the second phase.
    Synthesis: Cannot be synthesized if any data dependency;
    There won’t be dependency if all are non-blocking.

## Slide 30
Function and Task
Compilation Directives
  The same as function/procedure in PASCAL
  and non-void/void functions in C.
Advantage:
  Fast, convenient and easy to maintain the source code.
  Convenient for reading.
  Repetition and duplication

## Slide 31
Example of Function
module xyz(Clk, X, Y);
:
always(posedge Clk)
begin
:
X <= Reverse(Y);
:
end
:
endmodule
function [7:0] Reverse(In); // functionname is a reg
input [7:0] In;
swap(Reverse[7], Reverse[0]);
swap(Reverse[6], Reverse[1]);
swap(Reverse[5], Reverse[2]);
swap(Reverse[4], Reverse[3]);
Endfunction
task swap(A, B);
input A, B;
reg A, B;
A <= B;
B <= A;
endtask

## Slide 32
Blocking and Non-blocking Assignments
Blocking Assignments
always@(posedge Clk)
begin
X = Y + 1;
Y = X << 1;
end
Assume X==3 and Y==6 at first,
the simulator evaluates Y+1==7
and gives 7 to X; then it evaluates X<<1 == 14 and gives 14 to Y.
always@(posedge Clk)
begin
Y = X << 1; X = Y + 1;
end
Assume X==3 and Y==6 at first,
the simulator evaluates X<<1==6
and gives 6 to Y; then it evaluates Y+1 == 7 and gives 7 to Y.
Non-blocking Assignments
always@(posedge Clk)
begin
X <= Y + 1;
Y <= X << 1;
end
Assume X==3 and Y==6 at first,
the simulator evaluates X’==Y+1==7 and Y’==X<<1==6,
then it gives values:
X←X’==7 and Y←Y’==6;
always@(posedge Clk)
begin
Y <= X << 1; X <= Y + 1;
end
The simulation results will be the same as the above and it can be synthesized.

## Slide 33
begin
F1<=F2;
F2<=F1;
end
begin
F1=F2;
F2=F1;
end
Blocking and Non-blocking Assignments
Blocking Assignments
Non-blocking Assignments
Dual latches
FF
D
Q
Q’
D
Q
Dual latches
FF
D
Q
Q’
D
Q
F1
F2
F1
F2

## Slide 34
z
Switch-Case
case, casex, casez
case (expression)
constant1: statement1;
:
constantj: statementj;
:
default: statementd;
endcase
0, 1
x
?
casez(c)
8’b01z?11??: statement1;
:
8’b1100????: statementj;
:
default: statementd;
endcase
casex(c)
4’b00xx: statement1;
:
4’b0xxx: statementj;
:
default: statementd;
endcase

## Slide 35
Example: Flipflops
Positive-Edge Triggered D-Flipflop:
module DFF(Clk, D, Q);
input Clk, D;
output Q;
reg Q;
always@(posedge Clk)
Q=D;
endmodule
Resettable DFF:
(Asynchronous)
module DFF(Rst,Clk, D, Q);
input Rst, Clk, D;
output Q;
reg Q;
always@(posedge Clk or posedge Rst)
if(Rst) Q=1’b0;
else Q=D;
endmodule
Resettable DFF:
(Synchronous)
module DFF(Rst,Clk, D, Q);
input Rst, Clk, D;
output Q;
reg Q;
always@(posedge Clk)
if(Rst) Q=1’b0;
else Q=D;
endmodule
Rst
Clk
Q
Q
Rst
Clk

## Slide 36
Example: Counters
Basic Up-Counting Counter:
module CNT(Clk, Q);
input Clk;
output [7:0] Q;
reg [7:0] Q;
always@(posedge Clk)
Q=Q+1;
endmodule
Resettable Counter:
(Asynchronous)
module CNT(Rst,Clk, Q);
input Rst, Clk;
output [15:0] Q;
reg [15:0] Q;
always@(posedge Clk or posedge Rst)
if(Rst) Q=15’b0;
else Q=Q+1;
endmodule
Resettable Counter:
(Synchronous)
module CNT(Rst,Clk, Q);
input Rst, Clk;
output [31:0] Q;
reg [31:0] Q;
always@(posedge Clk)
if(Rst) Q=31’b0;
else Q=Q+1;
endmodule
Rst
Clk
Q
Q
Rst
Clk

## Slide 37
Example: Counters
Basic Down-Counting Counter:
Module CNT(Clk, Q);
input Clk;
output [7:0] Q;
reg [7:0] Q;
always@(posedge Clk)
Q=Q-1;
endmodule
Loadable Counter:
module CNT(Load, Clk, D, Q);
input Load, Clk, D;
output [15:0] Q;
reg [15:0] Q;
always@(posedge Clk)
if(Load) Q=D;
else Q=Q+1;
endmodule
Modulo Counter:
module CNT(Rst,Clk, Q);
input Rst, Clk;
output [7:0] Q;
reg [7:0] Q;
always@(posedge Clk)
if(Rst) Q=7’b0;
else if(Q==99) Q=7’b0; //%100
else Q=Q+1;
endmodule

## Slide 38: Lab03 7SEG Decoder & Freq Dividers
Boolean Logic
7-Segment LED Decoder
Frequency Dividers
Running Lamps
(Snake – a FPGA contest problem)
Problem 1. Review Karnaugh-Map (https://en.wikipedia.org/wiki/Karnaugh_map)
Problem 2. Quine–McCluskey Algorithm (https://en.wikipedia.org/wiki/Quine%E2%80%93McCluskey_algorithm)
Problem 3. Study Espresso Algorithm (https://en.wikipedia.org/wiki/Espresso_heuristic_logic_minimizer) by exercise the Logic Friday.