## Slide 1: Notes and Examples for Verilog Design
Tsung-Chu Huang
Nat’l Changhua Univ. of Edu.
2022/11/10

## Slide 2: 1.1 IC/FPGA Contest
Web: http://campusweb.yuntech.edu.tw/~icdesign/index.html
Dates
  Pretest: 8:30am-8:30pm, Wed. 2010/3/24
  Finals: Thu. 8:30am-8:30pm, 2010/4/29
Tools
  Design/Simulation: Quartus II, ModelSim 6.3
  Auxiliary: Word, Excel
  Others: paper notes
Training
  Prior to Pretest: 8:30am-3:30pm, Sat. 3/6, 3/13, 3/20
    ModelSim, Basic Design, Excises, Past/Mock Exams
  Post to Pretest: 8:30am-3:30pm, Sat. 4/17, 4/24
    FPGA Programming, Improvement and Report

## Slide 3: 2 Basics
ModelSim
Some Basic Useful Skills and Tools
Basic Elements, Modules and Design Styles

## Slide 4: 2.2 Some Basic Useful Skills and Tools
Basic Descriptions
Flipflops
Counters, LFSR, Johnson Counters
Decoders and ROM
Register Array and Memory
Finite State Machine
Some Basic Useful Skills and Tools

## Slide 5: 2.2 Basic Elements, Modules and Design Styles
Basic Descriptions
Flipflops
Counters
Decoders and ROM
Registers and Memory
Finite State Machine

## Slide 6: 2.2.1 Basic Descriptions
// non-arithmetic Decoder, ROM table
reg output;
always@(inputs)
case(inputs)
0’bxxxx: output = 0’bxxxx;
default:
endcase
// arithmetic combinational circuits
wire outputs;
assign output = f(inputs);
// Flip-flop Array
Reg States;
always@(posedge Clk)
if (Rst) States = InitialStates;
else States = NextStates;
// gate-level gates/modules
gate1 g1(output, inputs);
module1 u1(outputs, inputs);

## Slide 7: 2.2.2 Flipflops
// Synchronous Resettable DFF
module DFF(Rst, Clk, D, Q);
input Rst, Clk, D;
output Q;
always@(posedge Clk)
if (Rst) Q=0;
else Q=D;
endmodule
// Asynchronous Resettable DFF
module DFF(Rst, Clk, D, Q);
input Rst, Clk, D;
output Q;
always@(posedge Clk or posedge Rst)
if (Rst) Q=0;
else Q=D;
endmodule
// Synchronous Resettable DFF
module DFF(RstN, Clk, D, Q);
input Rst, Clk, D;
output Q;
always@(posedge Clk)
if (Rst) Q=D;
else Q=0;
endmodule
// Asynchronous Resettable DFF
module DFF(RstN, Clk, D, Q);
input Rst, Clk, D;
output Q;
always@(posedge Clk or posedge Rst)
if (Rst) Q=D;
else Q=0;
endmodule
// Synchronous Resettable DFF
module DFF(PRE, Clk, D, Q);
input Rst, Clk, D;
output Q;
always@(posedge Clk)
if (PRE) Q=1;
else Q=D;
endmodule
// Synchronous Resettable DFF
module DFF(PreN, Clk, D, Q);
input Rst, Clk, D;
output Q;
always@(posedge Clk)
if (PreN)Q=D;
else Q=1;
endmodule

## Slide 8: 2.2.3 Binary Counters
// Synchronous Resettable Up-Counter
module DFF(Rst, Clk, Q);
input Rst, Clk;
output [15:0] Q;
always@(posedge Clk)
if (Rst) Q=0;
else Q=Q+1;
endmodule
// Asynchronous Resettable Down-Cnt
module DFF(Rst, Clk, Q);
input Rst, Clk;
output [15:0] Q;
always@(posedge Clk and posedge Rst)
if (Rst) Q=0;
else Q=Q-1;
endmodule
// Synchronous Loadable Counter
module DFF(Load, Clk, D, Q);
input Rst, Clk;
input [15:0] D;
output [15:0] Q;
always@(posedge Clk)
if (Load) Q=D;
else Q=Q+1;
endmodule
// Modulo Counter from 3 to 100
module DFF(Rst, Clk, Q);
input Rst, Clk;
output [6:0] Q;
always@(posedge Clk)
if (Rst) Q=3;
else if (Q==100) Q=3;
else Q=Q+1;
endmodule
// Synchronous Resetable Enable Loadable Counter
module DFF(Rst, EN, Load, Clk, D, Q);
input Rst, Clk;
input [15:0] D;
output [15:0] Q;
always@(posedge Clk)
if (Rst) Q = 0;
else if (EN)
if (Load) Q = D;
else Q=Q+1;
endmodule

## Slide 9: 2.2.3 Linear Feedback Shift Registers (LFSR)
// LFSR
`define Seed = 5’b10101
module LFSR(Rst, Clk, Q);
input Rst, Clk;
output [4:0] Q;
always@(posedge Clk)
if (Rst) Q = `Seed;
else begin
Q[3:0]<= Q[4:1];
Q[4] <= Q[4] ^ Q[0];
end
endmodule

## Slide 10: 2.2.4 Decoders and ROM
Encoder/Decoders
  (Full) Address Decoder
  (Full) Address Encoder
  One-hot Code
  Thermal(-meter) Code
  Berger Code
  Hamming Code
  Seven-Segment Code
  ASCII Code
  BCD Code
  Gray (Grey) code
  Borden code
  m/n code
  Huffman code
  Johnson (counter) code

## Slide 11: 2.2.5 Register Arrays and Memory
// LFSR
`define Seed = 5’b10101
module LFSR(Rst, Clk, Q);
input Rst, Clk;
output [4:0] Q;
always@(posedge Clk)
if (Rst) Q = `Seed;
else begin
Q[3:0]<= Q[4:1];
Q[4] <= Q[4] ^ Q[0];
end
endmodule

## Slide 12: 3 Notes
Blocking and Non-blocking
Rules

## Slide 13: Sequence Control if-then-else
if (
} else {
Y
) {
C
Y
Y
N
}
Condition
N
N

## Slide 14: Sequence Control For-loop
for(i=1;i<=9;i++) {
}
for (
I
;
;
N
) {
P
}
C
Initialization
Condition
Process
Next
Y
N
for(j=1;j<=9;j++)
printf(“%dX%d=%2d\t”,i,j,i*j);
printf(“\n”);

## Slide 15: Sequence Control Do-While-Loop and While-Do-Loop
do {
} ;
P
} while(
C
Y
Condition
Process
N
while (
} ;
P
) {
C
Y
Process
Condition
N

## Slide 16: 4 Examples
Introduction
Basics
Notes
Examples

## Slide 17: RTL Code of ALU
// RTL code of Adders
module Adder(A, B, Ci, Co, S);
input [15:0] A, B;
i8nput Ci;
output Co;
output [15:0] S;
  assign {Co, S} = A + B + Ci;
endmodule
// RTL code of Multipliers
module Mul(A, B, P);
input [15:0] A, B;
output [31:0] P;
  assign P = A * B;
endmodule
// RTL code of Adder/subtractor
module ALU(ADD, A, B, Ci, Co, S);
input [15:0] A, B;
i8nput Ci;
output Co;
output [15:0] S;
  assign {Co, S} =
  ADD ? (A + B + Ci)
  : (A – B – Ci);
endmodule
// RTL code of 2m Divider
module Div(A, m, Q);
input [15:0] A;
Input [3:0] m;
  assign Q = Q >> m;
endmodule
// Multiplier and Accumulator
module A(Rst, Clk, X, A);
input Rst;
input [15:0] X;
output [31:0] P;
  always@(posedge Clk)
  if(Rst) A=0;
  else A = A + A[15:0]*X;
endmodule

## Slide 18: Decoders
// BCD to 7-Seg Decoder
module BCD7Seg(HEX, LED);
input [3:0] HEX;
output [7:0] LED;
always@(HEX) // Sensitivity List
case(HEX) //hgfedcba
0:LED= 8'b00111111;
1:LED= 8'b00000110;
2:LED= 8'b01011011;
3:LED= 8'b01001111;
4:LED= 8'b01100110;
5:LED= 8'b01101101;
6:LED= 8'b01111101;
7:LED= 8'b00000111;
8:LED= 8'b01111111;
9:LED= 8'b01101111;
10:LED= 8'b01011111;
11:LED= 8'b01111100;
12:LED= 8'b01011000;
13:LED= 8'b01011110;
14:LED= 8'b01111001;
15:LED= 8'b01110001;
default:
LED= 8'b10000000;
endcase
endmodule

## Slide 19: Finite State Machine
// Simple Finite State
module Lock(Clk, X, Z)
input Clk, X;
output Z;
reg Z;
parameter W1011=2’b00, W011=2’b01, W11=2’b10, W1=2’b11;
reg [1:0] Present_State, Next_State;
// Transitions of Sequential Circuits with Event Clk
always@(posedge Clk)
Present_State = Next_State;
// Combination Circuits with Input/Sensitivity List
always@(X or Present_State) begin
Next_State = Present_State;
case(Present_State)
W1011 : Next_State = X ? W011 : W1011;
W011 : Next_State = X ? W011 : W11;
W11 : Next_State = X ? W1 : W1011;
W1 : Next_State = X ? W011 : W11;
default: Next_State = W011;
endcase
case(Present_State)
W1 : Z = X ? 1 : 0;
default: Z = 0;
endcase
end // always
endmodule

## Slide 20: Memory
// RAM Generated by MegaWizard/Quartus II
module ram8x32 (address, we, data, q);
input [4:0] address;
Input we;
input [7:0] data;
output [7:0] q;
wire [7:0] sub_wire0;
wire [7:0] q = sub_wire0[7:0];
lpm_ram_dq lpm_ram_dq_component(address, data, we, sub_wire0);
Defparam
lpm_ram_dq_component.lpm_width = 8,
lpm_ram_dq_component.lpm_widthad = 5,
lpm_ram_dq_component.lpm_indata = "UNREGISTERED",
lpm_ram_dq_component.lpm_address_control = "UNREGISTERED",
lpm_ram_dq_component.lpm_outdata = "UNREGISTERED",
lpm_ram_dq_component.lpm_file = "C:/demo/SAP3X5/Program1.mif",
lpm_ram_dq_component.lpm_hint = "USE_EAB=ON";
endmodule
// RAM for Advanced Compiler eg. ModelSim or VerilogXL
module RAM8x32 (AD, WE, D, Q);
  input [4:0] AD;
  Input WE;
  input [7:0] D;
  output [7:0] Q;
  Reg [7:0] RAM[4:0];
endmodule

## Slide 21: Divided-by-10 Divider
Given a long binary number from a DIP switch, display the decimal number on the 7-segment LEDs.
Assumptions:
The DIP switch is changed one by one.
Note that the binary number is so long that the transformation cannot be implemented by a decoder.
A divided-by-10 divider is suggested.

## Slide 22: One-Shot RESET
D
Q
CLR
D
Q
CLR
D
Q
CLR
D
Q
CLR
Q
D
Q
D

## Slide 23: QRS÷T=Q…R
1
1
0
1
1
1
0
1
1
1
0
1
0
1
1
1
1
1
1
1
0
1
0
1
0
1
1
1
0
1
0
1
0
1
1
1
0
1
0
1
0
1
0
0
1
1
0
1
1
1
0
1
0
1
1
0
1
1
1
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
1
0
1
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
1
1
1
1
1
0
1
0
0
1
1
1
0
1
0
1
0
1
1
0
1
1
1
0
1
1
1
1
1
1
1
0
1
0
1
1
1
0
1
0
1
0
1
1
1
0
1
1
1
0
1
1
0
1
1
1
0
1
0
1
(n-m+1)-bit Q
(n-m+1)-bit Q
n-bit
m-bit T
(m-1)-bit R
(2n-m+1)-bit QRS
Shift Register

## Slide 25: DIP2LED
module DIP2LED(Clk, DIP, LED, SEG);
input Clk;
input [7:0] DIP;
output [3:0] LED; // Hi-Enable 29, 30, 31, 32
output [7:0] SEG; // Low-Enable h, .., a
wire [15:0] BCD;
wire [11:0] bcd;
reg [13:0] FD;
// Frequency Divider
always@(posedge Clk) FD=FD+1;
wire Clk1kHz;
assign Clk1kHz = FD[13];
IU U1(Clk1kHz, DIP, OneShot);
OU U2(Clk1kHz, BCD, LED, SEG);
bin2bcd U3(Clk, OneShot, DIP, bcd);
assign BCD={4'b0, bcd};
endmodule

## Slide 26: High-Level Coding Flow
Problem or Idea
Pseudo Code
Verified by C-Code
Flow Chart
State Diagram
RTL Code

## Slide 27: Example: Prime Numbers
Problem or Idea
Pseudo Code
Verified by C-Code
Flow Chart
Counter/State Diagram
RTL Code
LEDs show the least prime number, 2, if a button is pressed for more than 2 seconds;
Next prime number is displayed if the button is loosen in 2 seconds.
Solution 1 shows the time-consuming approach without memory array;
Solution 2 uses primary array to speed up.
There will be 1253 prime numbers from 2 to 9973.

## Slide 28: Example: Prime Numbers
Problem or Idea
Pseudo Code
Verified by C-Code
Flow Chart
Counter/State Diagram
RTL Code
2 3 4 5 6 7 8 9 10 11 12 13 …
%2 %3 %4 %5 ….
If then ?? case ? ?

## Slide 29: Example: Prime Numbers
Problem or Idea
Pseudo Code
Verified by C-Code
Flow Chart
Counter/State Diagram
RTL Code
prime()
{
int m, n, p;
printf(“%d\n”, 2);
for(n=3; n<9999; n+=2){
p=1;
for(m=3;m*m<n;m+=2)
if(!(n%m)) {p=0; break;}
if(p) printf(“%d\n”, n);
}
}

## Slide 30: Example: Prime Numbers
Problem or Idea
Pseudo Code
Verified by C-Code
Flow Chart
CounterState Diagram
RTL Code
n<9999
n←n+2
m*m<n
p←1; m←3
LED←n
LED←2; n←3
m←m+2
n%m
p←0
p
N
Y
Y
N
N
Y
Y
N

## Slide 31: Example: Prime Numbers
Problem or Idea
Pseudo Code
Verified by C-Code
Flow Chart
CounterState Diagram
RTL Code
n<9999
n←n+2
m*m<n
p←1; m←3
LED←n
LED←2; n←3
m←m+2
n%m
p←0
p
N
Y
Y
N
N
Y
Y
N
Power
on
Rst
RESET:
PRIME:
NotPrime:
NEXTm:
NEXTn:
INIT:
Per-Clock-State is decided by (m, n, p, Meta-State)

## Slide 32: Example: Prime Numbers
Problem or Idea
Pseudo Code
Verified by C-Code
Flow Chart
CounterState Diagram
RTL Code

## Slide 33: Problem
module LCD_CTRL(clk,
reset, datain, cmd,
cmd_valid, dataout,
output_valid, busy);
clk
reset
datain
cmd
cmd_valid
dataout
output_valid
busy

## Slide 34: Meta-States
reg [1:0] PS, NS;
enum [1:0] PowerOn=0,
Init=1,
ZoomFit=2,
ZoomIn=3;
always@(posedge clk
or posedge reset)
if(reset)
PS=Init;
else
PS=NS;
PowerOn
Init
ZoomFit
ZoomIn
Load_data
Load_data
Load_data
Shift_up
Zoom_In
Shift_down
Shift_left
Shift_right
Power On
All=0
reset

## Slide 35: General 1-Dimension For-Do Loop
int i, Io, Is, If;
for(i=Io; i<If; i+=Is) Process;
reg [1:0] Loop1PS, Loop1NS;
enum [1:0] Init=2’b01, Next=2’b10;
reg [31:0] i;
wire [31:0] Io=0, Is=2, If=100;
always@(posedge Clk or posedge Rst)
begin
:
:
case(Loop1PS)
Init: begin
i=Io;
if(i<If) Loop1NS=Next;
else Loop1NS=Exit;
end
Next: begin
Process;
i = I + Is;
end
default:
endcase
:
:
:
end
always@(...) begin
Loop1PS=Loop1NS;
end
i<If
i←Io;
Process;
i←i+Is;
Y
N
Init:
Next:
Exit:
default:

## Slide 36: General 2-Dimension For-Do Loop
int i, Io, Is, If, j, Jo, Js, Jf;
for(i=Io; i<If; i+=Is)
for(j=Jo; j<Jf; j+=Js)
Process;
always@(...)
begin
:
case(Loop1PS)
Init: begin
i=Io;
if(i<If)
begin
Loop1NS=Next;
Loop2NS=Init;
else Loop1NS=Exit;
end
Next: begin
case(Loop2PS)
Init: ...
Next: begin
Process;
j = j+Js;
end
endcase
i = i+Is;
end
default:
endcase
:
end
reg [1:0] Loop1PS, Loop1NS;
reg [1:0] Loop2PS, Loop2NS;
enum [1:0] Init=1, Exit=2;
always@(...) begin
Loop1PS=Loop1NS;
Loop2PS=Loop1NS;
end
reg [31:0] i, j;
wire [31:0] Io=0, Is=2, If=100;
wire [31:0] Jo=0, Js=1, Jf=999;

## Slide 37: Typical 2-Dimension For-Do Loop
reg [1:0] LPS, LNS; //Loop States
enum [1:0] OutLoop=0, InitI=1,
InitJ=2, Next=3;
i < If
i←Io;
N
Y
InitI:
Exit:
LPS←InitI
j < Jf
j←Jo;
Process;
i←i+Is;
j←j+Js;
Y
N
InitJ:
Next:
always@(...)
case(LPS)
InitI:begin
i=Io;
if(i<If) LNS=InitJ;
else LNS=Exit;
end
InitJ:begin
j=Jo;
if(j<Jf) LNS=Next;
else LNS=InitI
Next: begin
case(Loop2PS)
Init: ...
Next: begin
Process;
j = j+Js;
end
endcase
i = i+Is;
end
default:
endcase

## Slide 38: DIP2LED
module DIP2LED(Clk, DIP, LED, SEG);
input Clk;
input [7:0] DIP;
output [3:0] LED; // Hi-Enable 29, 30, 31, 32
output [7:0] SEG; // Low-Enable h, .., a
wire [15:0] BCD;
wire [11:0] bcd;
reg [13:0] FD;
// Frequency Divider
always@(posedge Clk) FD=FD+1;
wire Clk1kHz;
assign Clk1kHz = FD[13];
IU U1(Clk1kHz, DIP, OneShot);
OU U2(Clk1kHz, BCD, LED, SEG);
bin2bcd U3(Clk, OneShot, DIP, bcd);
assign BCD={4'b0, bcd};
endmodule

## Slide 39: Steps to Design
Do you realize the functions to design?
Think about who needs this module? I/O? A/Synchronous?
What to be optimized? Area (Gate Count), Speed, or Easiness?
Parallel Sorter? Serial Sorter? What kind of algorithms?
Design Style: State-Oriented FSM? Algorithmic-State Machine (ASM)? Parallel Gate-Level Structure?

## Slide 40: Notes
Algorithm  ASM  FSM
Bidirectional  wire inout  reg
Combinational Circuits
Decoders: always@(input) case(input)
Events: dependency
Fixed and Floating Numeric
Gating Clock
Hierarchical
Initialization and power-on
Justify and just-make
Knowledge: well-known circuits, LFSR, DSP, ECC, Compression, IIR, FIR, FFT
Loops  procedural counter or spatial array
Memory and small buffers
Notes and Remarks
Open Cores
Preprocessing
Quality Check
Reuse Base
Signaling
Timing

## Slide 41: Algorithmic RTL Code
wire [15:0] F, G;
assign F = A * B + C >> 3;
assign G = C ? A+B : A-B;

## Slide 42: Algorithmic State Machine
A←0, B←100
while(B>A){
for(i=0; i<N; i++) {
if(A*B<C) …
}
}
Call Subroutine();
Draw state diagram using ASM-Mapping
Separate the FFs in ASM Chart
  Petri Net as is
  Counter or meta states
  Abstracted States for FSM

## Slide 43: Example: Prime Numbers
Store the first 100 prime numbers in RF
main()
{
int M[100];
int i, j, P, N;
for(i=0, N=2, P=1; i<100; P=1, N++) {
for(j=0; j<i; j++)
if(N%M[j]==0) {P=0; break;}
if(P) {M[i++]=N;
printf("%d ", N);}
}
}

## Slide 44: Flow Chart  State Diagram
i=0, N=2, P=1
i<100
j=0
j<i
N%M[j]
P
P=0
j++
M[i]=N, i++
P=1, N++
End
Y
N
Y
N
1
0
1
0
Init:
Wait4i:
Initj:
Wait4j:
Nextj:
Next:
Wait4P:
Store:
Divide:
End:

## Slide 45: Rules using inout
Left value inout can be used in assign format:
assign inoutWire = C ? regIn : z;
Since it’s continuous, its switching should be written in procedural format:
reg regIn, regOut;
always@(*) // or (posedge Clk)
begin
regIn <= In;
regOut <= inoutWire;
end
assign Out = inoutWire;

## Slide 46: Bi-directional inout
module A (inout_bus_a, en_a);
inout [7:0] inout_bus_a;
input en_a;
reg [7:0] inout_bus_a_reg;
assign inout_bus_a = (en_a) ? 'bz : inout_bus_a_reg;
always () begin
read_from_bus_data = inout_bus_a;
inout_bus_a_reg = write_to_bus_data;
end
Endmodule
module B (inout_bus_b, en_b);
inout [7:0] inout_bus_b;
input en_b;
reg [7:0] inout_bus_b_reg;
assign inout_bus_b = (en_b) ? inout_bus_b_reg : 'bz;
always () begin
read_from_bus_data = inout_bus_b;
inout_bus_b_reg = write_to_bus_data;
end
Endmodule
module top;
wire [7:0] inout_bus;
reg en_b; // this needs to be driven by top
A (inout_bus, en_b);
B (inout_bus, en_b);
endmodule

## Slide 47: Combinational Circuits
Gate Level: A set of gates (or module)
RTL Codes: assign wire = equation
ROM: always@()case()
Decoder: always()@case()
Constant: Vdd/GND
Multiplexer: out = c ? i1 : i0
Power of 2: 1<<n
Iterative logic array: parallel mul/div/mod

## Slide 48: Truth Table, Decoder, ROM
always@(IN)
case(IN)
4’b0000: OUT = 2’b01;
4’b0001: OUT = 2’b10;
4’b0010: OUT = 2’b10;
4’b0011: OUT = 2’b00;
:
4’b1111: OUT = 2’b11;
default: OUT = 2’b00;
endcase
always@(*)
case(IN);
4’b0000: OUT = 2’b01;
:
4’b1111: OUT = 2’b11;
default: OUT = 2’b00;
endcase

## Slide 49: Event Dependency
Considering all (e1, e2, ..) → (r1, r2, …)
  One-to-multiple: OK
  Multiple-to-one: (posedge e1 or posedge e2)
    Can be separated into multiple blocks of statements
  Level enables (inputs) and edge triggers cannot be merged together
  reg must be assigned to a wire for events

## Slide 50: 2’s Complements
Example when n=4, N = -2n-1~2n-1-1
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
overflow

## Slide 51: Fixed-Point Decimal
Maintain a notation for position computation
  For example, <5.3> can mean 5 bits of integer with 3 bits of decimal.  <i.d>
Fixed-Point Operations
  <a.b> + <c.d>  <max(a, c)+1.max(b, d)>  truncated
  <a.b> - <c.d>  <max(a, c).max(b, d)>  truncated
  <a.b> * <c.d>  <a+c.b+d>  truncated
  <a.b> / <c.d>  <a-c+1.b+c>  truncated
Floating-Point
  IEEE 754
  (-1) s x c x bq
  Sign, coefficient, base and exponent

## Slide 52: 2’s Complement Multiplier
Sign Extension
module cMul(A, B, P); // Fixed-Point 8.8 Complex Multiply
input [15:0] A[2], B[2];
output [15:0] P[2];
wire [31:0] Q[2], Ar, Ai, Br, Bi;
assign Ar={A[0][15]?8’hFF:8’h00, A[0]};//sign ext.
assign Ax={A[1][15]?8’hFF:8’h00, A[1]};
assign Br={B[0][15]?8’hFF:8’h00, B[0]};
assign Bi={B[1][15]?8’hFF:8’h00, B[1]};
assign Q[0]=Ar*Br-Ai*Bi;
assign Q[1]=Ar*Bi+Ai*Br;
assign P[0]=Q[0][23:8];
assign P[1]=Q[1][23:8];
endmodule

## Slide 53: Clock-Gating Cells for Synthesis
G
I
D Q
D Q
L
E
C
K
Label | Signal | 0 | 1 | Rule
C | Regular Clock | ↓ | ↑ | I = C⊕K
I | Inversion Type | Non-inverted | Inverted | 
K | Gated Clock | ↓ | ↑ | 
L | Latch Type | Low-level | High-level | L = ~C
G | Gate Type | OR | AND | G = E
E | Enable/Disable | Disable | Enable | 

## Slide 54: Hierarchical Design
Modularization:
  Try to separate the whole circuits into several modules
sensible
sensible
insensible
insensible
modularization
partitioning

## Slide 55: Initialization and Power-On
Only reminding for low-level raw-design
System Reset Circuit

## Slide 56: Justify
Check if 1-cycle error
Check if negative logics
Check if counting up from 0 or 1
Preparing a check list

## Slide 57: Knowledge of Well-Knowns
DSP
  Digital Filters: IIR, FIR
  Fourier Transform: FFT
  RNG using LFSR
Decoders
  Compressor/Decompressor, Haffman Codes
  ECC Decoders: Parity-Check, Hamming
  Address Decoder, Selector, Priority Encoder
  One-Hot, Thermal Codes
ALU

## Slide 58: Loops
Temporal (Time)  Physical Counter
  reg i;
  always@(posedge Clk) i = i + 1;
Spatial (Generate)  Array of modules
  integer i;
  (generate)
  for(i=1; i<=N; i=i+1) begin
  cell(i); …
  end
  (endgenerate)

## Slide 59: Memory
reg [w-1:0] M [0:(1<<a)-1];
SynMem  FF except Cost/Speed/Ports
ComMem  Gates (decoder)
Quartus II: MIF
ModelSim: $read/$write

## Slide 60: Notes and Comments
Taking advantage of // Notes
Write down the pin#
Note the versions

## Slide 61: Open Cores
Opencores.org
  8051, Z80, MIPS, etc.
  FFT, FIR, IIR, etc.

## Slide 62: Preprocessing
Taking advantage of Office Tools
  Excel
Taking advantage of Programming

## Slide 63: Quality Check
Symbols
  Inversion: bar, N, _
  Capital / lower case
Debug
  Break Point

## Slide 64: Reuse Database
Construct a circuit base

## Slide 65: State Abstraction
Catch the characteristics of the state flow
Note the initialization and termination
Partitioning the state diagram
Meta-states

## Slide 66: Timing
Delay Elements Asynchronous Machine

## Slide 67: Clock for Simulation
Initial Clk = 0;
always Clk = #10 ~Clk;
always Clk = #10 ~Clk;
Initial Clk = 0;
Note: Initialize in advance
Wrong!  Unknown
Frequency Divider by 2n
reg [n-1: 0] Q;
always@(posedge Clk) Q=Q+1;
assign Clk_div_2_pow_n = Q[n-1];
Frequency Divider by 2m<2n
reg R;
reg [n-1: 0] Q;
always@(posedge Clk)
if(Rst) begin Q=0; R=0; end
if(Q==m-1) begin Q=0; R = ~ R; end
assign Clk_div_2m = R;

## Slide 68: One-Shot
reg Q;
always@(posedge Clk)
if(Shot) Q<=1;
else Q<=P;
1-Period One-Shot
k-Period One-Shot
reg [n-1: 0] Q;
always@(posedge Clk) Q=Q+1;
assign Clk_div_2_pow_n = Q[n-1];

## Slide 69: Resettable Counter
reg [15:0] Q;
always@(posedge Clk)
if(Rst) Q=0;
else Q = Q + 1;
reg [15:0] Q;
always@(posedge Clk or posedge Rst)
if(Rst) Q=0;
else Q = Q + 1;
Synchronously Resettable
Asynchronously Resettable

## Slide 70: State-Abstract FSM
assign F = f(X1, X2, Q1, Q2);
always@(*) case(IN)...endcase
nand g1(D1, X1, Q1);
unit u1(X1, X2, Q1, Q2);
RTL Model
Behavioral Model
Gate-Level Model
Clk
NS
PS
always@(posedge Clk)
PS = NS;

## Slide 71: Algorithmic FSM
wire [15:0] F;
assign F = A * B + C >> 3;

## Slide 72: Counter-Based FSM
wire [15:0] F;
assign F = A * B + C >> 3;

## Slide 73: RAM
module M(W, A, D, Q);
parameter LW=8;
Parameter LA=10;
input W;
input [LA-1:0] A;
input [LW-1:0] D;
output [LW-1:0] Q;
reg [LW-1:0] Q;
reg [LW-1:0] RAM [0:1<<LA-1];
always@(W or A or D)
if(W) RAM[A] = D;
else Q = RAM[A];
endmodule

## Slide 74: ROM

## Slide 75: Stack

## Slide 76: Queue

## Slide 77: Edge Detector

## Slide 78: Pulse Shrinker

## Slide 79: Pulse Wider

## Slide 80: Clock Blender

## Slide 81: LFSR

## Slide 82: Johnson Counter

## Slide 86: Bidirectional Control

## Slide 87: Parallel Sorter

## Slide 88: Look-Up Table

## Slide 89: Hamming Codes

## Slide 90: Huffman Codes

## Slide 91: Sequence Detector

## Slide 92: Traffic Lights

## Slide 93: SAP3X5

## Slide 94: RF: Register Files

## Slide 95: Double Flip-Flops
Debouncer
Synchronizer

## Slide 96: Timer

## Slide 97: Bottom Events

## Slide 98: UART

## Slide 99: FF Conversions

## Slide 100: Divider

## Slide 101: Prime Number Generator
Coding in C
int U=10000, R=100;
for(p=2; p<U; p++){
Prime = 1;
for(i=0; i<N; i++)
if(p%M[i]==0){
Prime=0;
break;
}
if(Prime) {
if(TimeUp){
printf("%d,", p);
CountDown;
}
if(p<R) M[N++]=p;
}

## Slide 102: Prime Number Generator
State Diagram
int U=10000, R=100, N=0, M[100];
for(p=2; p<U; p++){
Prime = 1;
for(i=0; i<N; i++)
if(p%M[i]==0){
Prime=0;
break;
}
if(Prime) {
if(TimeUp){
printf("%d,", p);
CountDown;
}
if(p<R) M[N++]=p;
}

## Slide 103: ABCDEF for FSM
Algorithm: usually given by the contest problem.
Blocks: usually partitioned by the contest problem.
Coding: C programming for verification.
Diagram: mapping C program to state diagram.
Editing: by state (graph) or Verilog editor.
FSM typical style.

## Slide 104: Verilog Design for Fixed-Point Fast Fourier Transformers
Tsung-Chu Huang
Nat’l Changhua Univ. of Edu.
2015/08/27

## Slide 105: Outline
2’s Complement Fixed-Point in V2K
Basics of 2m-point FFT
Recursive Expansion
Synthesizer using generate-endgenerate
Synthesizer using C or matlab
Validation using C or matlab
Clocked-Latching and Pipeline

## Slide 106: Ring of 2’s Complements
Example when n=4, N = -2n-1~2n-1-1
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
overflow

## Slide 107: Shift of 2’s Complements
Shift Left:
  N << 1;  N=N*2;
  Eg. -3 ==11012 <<1 == -6 == 10102
  -7 == 10012 <<1 == -14 == 00102 == +2 (Overflow!)
Shift Right:
  N >> 1;  N=N/2;
  Eg. -4 ==11002 >>1 == -2 == 11102

## Slide 108: Fixed-Point Decimal
Maintain a notation for position computation
  For example, <5.3> can mean 5 bits of integer with 3 bits of decimal.  <i.d>
Fixed-Point Operations
  <a.b> + <c.d>  <max(a, c)+1.max(b, d)>  truncated
  <a.b> - <c.d>  <max(a, c).max(b, d)>  truncated
  <a.b> * <c.d>  <a+c.b+d>  truncated
  <a.b> / <c.d>  <a-c+1.b+c>  truncated
Floating-Point
  IEEE 754
  (-1) s x c x bq
  Sign, coefficient, base and exponent

## Slide 109: 2’s Complement Multiplier
Sufficient Condition to Skip Sign Extension
  Same and enough width without overflow!
module MUL88(A, B, P);
  input [15:0] A, B; //FP8.8
  output [23:0] P; //FP16.8
  wire [31:0] Ax, Bx, Px; //FP16.16
  assign Ax[31:16] = A[15]?16’hFF:16’h00;
  assign Ax[15:0] = A;
  assign Bx[31:16] = B[15]?16’hFF:16’h00;
  assign Bx[15:0] = B;
  assign Px = Ax * Bx;
  assign P = Px[31:8];
endmodule

## Slide 110: 2’s Complement Complex
Sign Extension
module cMul(A, B, P); // Fixed-Point 8.8 Complex Multiply
input [15:0] A[2], B[2];
output [15:0] P[2];
wire [31:0] Q[2], Ar, Ai, Br, Bi;
assign Ar={A[0][15]?8’hFF:8’h00, A[0]};//sign ext.
assign Ax={A[1][15]?8’hFF:8’h00, A[1]};
assign Br={B[0][15]?8’hFF:8’h00, B[0]};
assign Bi={B[1][15]?8’hFF:8’h00, B[1]};
assign Q[0]=Ar*Br-Ai*Bi;
assign Q[1]=Ar*Bi+Ai*Br;
assign P[0]=Q[0][23:8];
assign P[1]=Q[1][23:8];
endmodule

## Slide 111: FFT: Fast Fourier Transform
Spectrum (Optics)
Signature (Recognition)
Modulation, Filter (DSP)
Testing
etc.

## Slide 112: Complex Constant
Definition
wher
Lemma
The w constants can be generated by C or Excel

## Slide 113: 1-stage 2-point FFT
2-point FFT
+
+
+
x = a+jb
y = c+jd
X = (a+c)+j(b+d)
x-y = (a-c)+j(b-d)
Y= (x-y)w2

## Slide 114: 3-stage 8-point FFT
8-point FFT
000
001
010
011
100
101
110
111
000
100
010
110
001
101
011
111

## Slide 115: Recursion
N-point Decimation-in-frequency FFT
000
001
010
011
100
101
110
111
000
100
010
110
001
101
011
111
N/2-point FFT
N/2-point FFT

## Slide 116: Recursion
N-point Decimation-in-time FFT
000
001
010
011
100
101
110
111
000
100
010
110
001
101
011
111

## Slide 117: Recursion of Sorting Network
Batcher Bitonic Sorter
Parallel Sorter
Half-Cleaner

## Slide 118: Syntheses of Regular-Indexed Module
V2K using generate/endgenerate with integer indices
Generating text in EXCEL
Synthesizer by C
Synthesizer by matlab

## Slide 119: Catching the Regularity
Mathematical Induction (數學歸納法)
  Initial Condition
  Successive Relation
Exercise the initial cases
  N=1  FFT2
  N=2  FFT4
  N=3  FFT8
Providing more convenient assistances in your synthesizer

## Slide 120: generate Block of Verilog-2001
Example
module …
  input… output… reg… wire……;
  other blocks……;
  integer i, j;
  generate
  for(i=0; i<N; i=i+1) …
  for(j=0; j<M; j=j+1) …
  begin
  module_or_gate g1(array indexed with i, j);
  ……;
  end
  endgenerate
  other blocks;
endmodule

## Slide 121: Problems of generate Block
Variable-Type and Variable-Size Ports cannot be easily treated by generate blocks.
Difficult to maintain and extend.
Still need other shells or programs for system calls and linking.
Purpose-oriented: Use the proper tools
EXCEL
C
Matlab
C++
Verilog
SPICE

## Slide 122: Tutorials and Next Steps
Complex Fix-Point Operations
Parameter Generating
Preliminary Case Study: FFT2, FFT4, FFT8
Regularity Catching and Generalizaiton
Bench Signal Generating
Validation with Programming Tools
System Calls
Automation
Documentation: Report and Presentation
Rehearsal