## Slide 1
Hardware Description Language
-- Logic Design using Verilog
Tsung-Chu Huang
Dept. of Electronic Eng.
National Changhua University of Ed.
Email: tch@cc.ncue.edu.tw
2022/11/24

## Slide 2
Outline
Introduction to Physical Memory
  ROM, RAM, DRAM
Typical Memory Access Timing
Memory Simulation in Verilog HDL
Memory Synthesis for Chip Layout
Memory in FPGA/CPLD
  Routing Switch Control
  Reconfigurable RAM
Memory Synthesis in FPGA/CPLD
  Flipflop based
  RAM based
Tutorial: Simple Memory IO System

## Slide 3
Taxonomy
Introduction to Physical Memory
by Access Structure
  Random Access Memory (RAM)
  Serial Access Memory (SAM)
  Content Access Memory (CAM)
by Alterability
  RAM: R/W Memory, SRAM, DRAM, CCD
  ROM
  EPROM
  EEPROM
  Filed Alterable ROM, e.g., Flash
by Device: BJT, NMOS, CMOS, CCD

## Slide 4
Memory Design in General FPGA/CPLD
Basic Syntheses for Memory
M[7]
M[6]
M[5]
M[4]
M[3]
M[2]
M[1]
M[0]
15...0
reg [15:0] M[0:7];
M[A] = D;
D
A
Q = M[A];
Q
A

## Slide 5
Memory Design in General FPGA/CPLD
Single-Port RAM:
module single_port_ram(input [7:0] data, input [5:0] addr,
input we, clk,output [7:0] q);
// Declare the RAM variable
reg [7:0] ram[63:0];
// Variable to hold the registered read address
reg [5:0] addr_reg;
always @ (posedge clk)
begin
// Write
if (we)
ram[addr] <= data;
addr_reg <= addr;
end
// Continuous assignment implies read returns NEW data.
// This is the natural behavior of the TriMatrix memory
// blocks in Single Port mode.
assign q = ram[addr_reg];
endmodule;

## Slide 6
Use of Memory in FPGA/CPLD
Purposes
  Emulate the Real Memory
  Just Simulation
  Just Functional Usage
Resources of your FPGA/CPLD Chips
  Real Memory
    Compact, High Capacity
    Can emulate real memory in the same type
  Registers  emulating RAM
  Logic gates  emulating ROM

## Slide 7
Basic Static RAM (SRAM)
Word Line
Bit Line
Bit Line

## Slide 8
Basic SRAM Architecture
Memory Array
Y Decoder
Column Decoder
N
R
WL
BL
Control
Y Address Buffer
N
N
Column Address Buffer
M
M
M
SA

## Slide 9
Related Techniques of DRAM
EDO: Extended Data Output
  Fast Page Mode
BEDO: Burst EDO (4 addr. per burst)
  Burst Mode: 4 Addresses per burst
DDR: Double Data Rate Technique
SDRAM: Synchronous DRAM
RDRAM: RAMBus DRAM
VDRAM: Video RAM

## Slide 10
Historical Evolution of DRAM
Write Select
Read
Read Select
Write
Read
R/W Select
Write
Write Select
Read Select
Data
Data
R/W Select

## Slide 11
Historical Evolution of DRAM
Basic Planar and Trench DRAM Cells
Word
Bit
Planar Cell
Trench Cell
Word
Bit

## Slide 12
Basic ROM Architecture

## Slide 13
Typical Storage Hierarchy
Archive II
Archive I
Main Memory
L2 Cache
L1 Cache
Register
Optical disk
Magnetic disk
DRAM
SRAM
DRAM
SRAM
FF

## Slide 14
Basic Standards of Timing Diagrams
Basic I/O Signals
CS: Chip Select
Adr.: Address
WE: Write Enable
OE: Output Enable
Di: Data-input
Do: Data-output
RAS: Y Address Strobe
CAS: Column Address Strobe
Asynchronous Ports
Synchronous Ports
Adr
WE
In_Clock
Adr
WE

## Slide 15
Memory Simulation in Verilog HDL
Simulated by reg
  parameter WordLength=8, AddressBits;
  reg [WordLength-1:0] Mem[0:(1<<AddressBits)-1];
  reg [3:0] SmallMem[0:11]; //12 Nibbles
Only addressed word can be individually assigned.
  SmallMem[7] = 4’b1011;
  SmallMem[7][3]= 1’b0; //Wrong!
  SmallMem = AnotherBlock; //Wrong!
Simulated by Files in VerilogXL/Cadence
Defined by
  Using $readmemb(“text_file”, Mem); and $writememb(“text_file”, Mem) to do mass read/write.
  Using $displayb(Mem[1023]); to display

## Slide 16
Memory Synthesis for Chip Layout
Cell Base Layout:
  Survey the recent information from the CIC.
  Usually they support some memory cores with fixed sizes.
  Read the specification and request the simulation model and simulated module.
  Simulate your system embedding the memory module.
  The foundry will “paste” the real block to the hole in your layout.
Full Custom Layout:
  Layout the RAM Cell by yourself.
  Some foundries give suggested circuits.

## Slide 17
Memory In FPGA/CPLD
The basic memory for FPGA/CPLD is to record the switch states for routes
CLB
For an ideal example:
An NxN ideal crossbar switch needs N2 bits of memory.
Frequent-used states are minimized and stored in fewer bits of memory.
EAB
Embedded Array Block implementing logic or RAM in Altera/FLEX10K device. 1 EAB consists of 8 EAB Cells. 1 Cell can implement 256 bits.
Flipflops are usually synthesized as a RAM bit if without RAM

## Slide 18
MegaWizard in Altera’s Tools (1)
Tools → MegaWizard Plug-In Manager
  LPM: Library of Parametered Modules
    Decoders
    IO Ports
    LPM_RAM
  Mega Functions
  SOPC Builters

## Slide 19
MegaWizard in Altera’s Tools (2)
Select Device, HDL, Function and Object file

## Slide 20
MegaWizard in Altera’s Tools (3)
Select Size Parameters

## Slide 21
MegaWizard in Altera’s Tools (4)
Select mif (Memory Initial File).

## Slide 22
Sample of MIF
A sample can be get by indexing mif.
DEPTH = 32; % Memory depth and width are required %
WIDTH = 14; % Enter a decimal number %
ADDRESS_RADIX = HEX; % Address and value radixes are required %
DATA_RADIX = HEX; % Enter BIN, DEC, HEX, OCT, or UNS; %
% unless otherwise specified, radixes=HEX%
-- Specify values for addresses, which can be single or range
CONTENT
BEGIN
[0..F] : 3FFF; % Range from 0 to F = 3FFF %
6 : F; % Single address--Address 6 = F %
8 : F E 5; % Range starting from %
END;

## Slide 23
Example 1
Timer-base ASM with RAM Output
Output 6 successive BCDs to a 7-seg. LED cyclically.
DEPTH = 6; % 6 words %
WIDTH = 4; % 1 word = 1 nibble %
ADDRESS_RADIX = HEX; % Address and value radixes are required %
DATA_RADIX = HEX; % Enter BIN, DEC, HEX, OCT, or UNS; %
% unless otherwise specified, radixes=HEX%
-- Specify values for addresses, which can be single or range
CONTENT
BEGIN
0 : 1 7 8 9 0 6;
END;