## Slide 1: Hardware Description Language Case Study of HDL CPU SAP444 & Assembler
Tsung-Chu Huang
IC-TestLab NCUE, Taiwan
2022/12/29

## Slide 2: Outline
CPU Models
ISA Model
  5 Categories of Op Types
  Instruction Formats
  Addressing Modes
  Instruction Cycles
Case Study 1: SAP3X5
Case Study 2: SAP444
Register Transfer Language/Level
Memory
  Hierarchy & Simulation
  Mnemonics & Timing
Assembler
Practice & Timing Closure

## Slide 3: 3 Major CPU Models
Von Neumann (5U)
Harvard Model
Datapath Model
MU
IU
OU
CU
ALU
Sequencer
x
+
shift
Two Major Flows
  Control Flow Computers
  Data Flow Computers

## Slide 4: MIPS: Hybrid with Harvard + Datapath

## Slide 5: 3 Categories of Parallel Computers
Pipeline Computers:
  Expiration in Time-Space Diagram
  Multiple-pipelines multiple instruction forwarding for superscalar computers
Array Processors:
  Processors X N + Control
Multiprocessor Systems:
  P1+P2+…+Control
A
B
C
A
B
C
A
B
C
Time
Space

## Slide 6: Instruction Set Architecture (ISA)
Model View: an abstract model of a computer
Classified by Complexity:
  RISC: Reduced Instruction Set Computers
  CISC: Complex Instruction Set Computers
  (VLIW: Very-Long-Instruction-Word Computers)
5 Instruction Categories (Types)
  ALU-related Instructions:
    ADD/SUB, MUL/DIV, SHL/SHR, RLC/RRC, AND/OR/NOT
  BUS-related Instructions:
    MOV R1, R2; LDA/STA
  CU-related Instructions:
    Jmp, JNC, JNZ, branch, Call, return
  Data I/O related Instructions
    IN, OUT
  Environmental/System related Instructions
    INT, HLT, sleep, mode
      (Note: a little modified from textbooks for convenience of mnemonics)

## Slide 7: Instruction Format
OP Code: operation code
  m bits can encode instructions
  If one code is used to extend x bits:
Categorized by #operands - #implied_opernads
  0. no operand, or implied to A, C, or special register
  single operand, or with implied opernand
  two operands
  VLIW: Very Long Instruction Word
OP1
Ext
OP2
OP1
OP Code
Operand
OP1
Destination
Source
OP1
Opd1
Opd2
Opd3
Opd4

## Slide 8: Addressing Modes
Immediate Data
  ADD R1, #03FA
Direct Address Mode
  ADD R1, 03FA
Indirect Address Mode
  ADD R1, @R2
Indexing Mode
  LDA R1, X
Register Mode
  ADD R1, R2

## Slide 9: Instruction Cycles

## Slide 10: Case Study 1: SAP3X5
My undergraduate work in NTUEE in 1985

## Slide 11: Instruction Set of SAP3X5
000 00000 NOP ; (no operation),↓
000 00001 NOT A ; A←~A,↓
000 00010 SHL A ; A[n-2:0]←A[n-1:1], A[n-1]←A[0] ,↓
000 00011 SHR A ; A[n-1:1]←A[n-2:0], A[0]←A[n-1] ,↓
000 00100 IN A ; A←KBD,↓
000 00101 OUT A ; LED←A,↓
000 00110 CLR A ; A←0,↓
000 00111 CLR C ; C←0,↓
000 01000 INC A ; A←A+1,↓
000 01001 DEC A ; A←A-1,↓
000 01010 RET ; PC←STK
000 11111 HLT ; (halt)
001 aaaaa STA aaaaa ; M[a]←A,↓
010 aaaaa AND aaaaa ; A←A&M[a],↓
011 aaaaa ADC aaaaa ; A←A+M[a]+C,↓
100 aaaaa JC aaaaa ; ↓,C=1:PC←a
101 aaaaa JNZ aaaaa ; ↓,Z=0:PC←a
110 aaaaa CALL aaaaa ; STK←PC+1, ADR←a
111 aaaaa LDA aaaaa ; A←M[a],↓

## Slide 12: Assembly Code Example of SAP3X5
BEGIN LDA ONE 00000:111 01111
STA I 00001:001 10000
LOOP LDA SUM 00010:111 01110
ADC I 00011:
STA SUM 00100:
LDA I 00101:
INC A 00110:
STA I 00111:
NOT A 01000:
ADD TWENTY 01001:
JNZ LOOP 01010:
LDA SUM 01011: 111 01110
OUT A 01100:
STOP HLT 01101:
SUM DB 0 01110: 000 00000
ONE DB 1 01111: 000 00001
I DB 10000: ??? ?????
TWENTY DB 20 10001: 000 10100

## Slide 13: Abstracts of Computer Architecture
(source: web)

## Slide 14: Case Study 2: SAP444
A
C
MU
ALU
PC
STK
Z
INA/OUT
LDA/STA
RF
0
11
0
7
0
15
Morse

## Slide 15: Instruction Format and Instruction Set
Code
########
LDI #Opd
0000
Code
RRRR
NOT Ri
RRC Ri
RLC Ri
INC Ri
DEC Ri
CLR Ri
Code
Rd
Rs
AND Rd, Rs
LOR Rd, Rs
ADD Rd, Rs
SUB Rd, Rs
ADC Rd, Rs
SBC Rd, Rs
XOR Rd, Rs
MOV Rd, Rs
Code
aaaaaaaa
JMP addr
JNC addr
JNZ addr
CAL addr
LDA addr
STA addr
0000
0000
Code
ALU
Bus
Ctrl
DIO
Env/sys
HLT
INA
OUT
NOP
CLC
SEC
SWP
RET
implied mode
register mode
register mode
immediate mode
direct mode

## Slide 16: Simple Memory Management
Instruction & Data share the same RAM
MU
11 10 9 8 7 6 5 4 3 2 1 0
00
01
02
FF
Instruction Code
Data Code
Declared a byte:
Label DB (initial value)
PC is reset to 0

## Slide 17: Structural Synthesis: Efficient but Glue
Control of MUX is decoded first.

## Slide 18: Behavioral Style Synthesis: Simple but Inefficient
always@(posedge Clk)
case(PS)
case(OP1)
case(OP2)
case(OP3)
code1: A = A + R1;
code2:
code3: A = A << 1;
code4:
endcase
endcase
endcase
endcase
A
A
instruction cycle = t-1
instruction cycle = t
+
*
*
*
*
+
0 1
0 1
0 1
instruction cycle = t-1
instruction cycle = t
Decoder
Last &
Complex
ALU not sharable

## Slide 19: Instruction Cycles
Fetch
(Virtual) Decode
Execution
(and Practical Decode)
LOAD
INA/HALT

## Slide 20: RTL
Register-Transfer Concepts
  Register-Transfer Language for describing Instructions of a CPU
  Register-Transfer Level in VLSI Synthesis and
Register Transfer Language
  Examples:
  NOP ; PC ← PC + 1
  ADD R1, R2 ; R1 ← R1 + R2, PC ← PC + 1
  JMP F01A ; PC ← F01A
  CAL F01A ; STK ← PC + 1, PC ← F01A
  RET ; PC ← STK

## Slide 21: Hierarchy and Simulation of Memory
Register
0.1ns
Cache
1ns
Main Memory
10ns
Bit Area
Bit Price
Bit Power
Speed
module memory(
output [7:0] data_out,
input [7:0] address,
input [7:0] data_in,
input write_enable,
input clk
);
reg [7:0] memory [0:255];
always @(posedge clk) begin
if (write_enable) begin
memory[address] <= data_in;
end
end
assign data_out = memory[address];
endmodule
$setuphold( ……);

## Slide 22: Basic Timing of Memory
CS: Chip Select
Adr.: Address
WE: Write Enable
OE: Output Enable
Di: Data-input
Do: Data-output
RAS: Y Address Strobe
CAS: Column Address Strobe
Synchronous Ports
Adr
WE
In_Clock
Asynchronous Ports
Adr
WE

## Slide 23: RAM Synthesized by MegaWizard
-- RAM256D.mif for SAP444 in Cyclone III/DE0
WIDTH=12;
DEPTH=256;
ADDRESS_RADIX=HEX;
DATA_RADIX=HEX;
CONTENT BEGIN
[00..FF] : 000; -- test2.asm
0 : 000;
1 : F11;
2 : C00;
3 : 911;
4 : B50;
… …
1C : 000;
1D : 006;
1E : 00F;
1F : 010;
END;
Loader : Quartus II

## Slide 24: Simple Assembler for SAP444
-- RAM256D.mif for SAP444 in Cyclone III/DE0
WIDTH=12;
DEPTH=256;
ADDRESS_RADIX=HEX;
DATA_RADIX=HEX;
CONTENT BEGIN
[00..FF] : 000; -- test2.asm
0 : 000;
1 : F11;
2 : C00;
3 : 911;
4 : B50;
… …
1C : 000;
1D : 006;
1E : 00F;
1F : 010;
END;
BEGIN NOP
CAL SHOW
JMP BEGIN
L1 LDI 17
STA 80
…
…
NOP
RET
HLT
NOT
Assembler
(by C, Python,
etc.
or manually)
Source Code: Assembly Code
Object Code: Machine Code

## Slide 25: Timing Closure
Power Consumption
Technology Mapping
A iterative process to optimize
timing of an IC circuit by adjusting
non-functional factors including
power and technology mapping.
Timing

## Slide 26: Practice and Implementation on Cyclone III
ROM Reading
RAM Writing and Reading
Coding SAP444 in Verilog
Coding Assembler in C
Coding Assembly Programs and Testing

## Slide 27: A Simplified MIPS Processor in Verilog

## Slide 28: Instruction Cycles

## Slide 29: Data Memory
module DM(MemRead, MemWrite, ABUS, DIN, DATABUS);
  MemWrite: Nothing happens if 0. If 1, the memory at location ABUS will be written with DIN.
  ABUS: At any moment, the data at location ABUS will appear at DATABUS.
  MemRead: Not used.

## Slide 30: Data Memory
Address bus: 8 bits.
Data bus: 32 bits. Each memory location holds 32 bits.

## Slide 31: Data Memory
Init the contents in data memory with any value you like:
initial
begin
for (i=0; i <= DM_ADDR_MAX_m1; i = i + 1)
ram[i] = i*10 + 1;
end

## Slide 32: Instruction Memory
module IM(CSB,WRB,ABUS,DATABUS);
  CSB: chip select. If 0, selected. If 1, not selected.
  WRB: Not used.
  ABUS: Address bus. At any moment, if chip is selected, the data at location ABUS will appear at DATABUS.

## Slide 33: Instruction Memory
Address bus: 8 bits.
Data bus: 32 bits. Each memory location holds 32 bits.

## Slide 34: Instruction Memory
The most straightforward way of loading a program:
ram[0] = 32'b00100000000000000000000000000000; // addi $0, $0, 0
ram[1] = 32'b00100000001000010000000000000001; // addi $1, $1, 1
ram[2] = 32'b00100000010000100000000000000010; // addi $2, $2, 2
ram[3] = 32'b00100000011000110000000000000011; // addi $3, $3, 3
ram[4] = 32'b00000000000000000000000000000000; // nop
ram[5] = 32'b00000000000000000000000000000000; // nop
ram[6] = 32'b00000000000000000000000000000000; // nop
ram[7] = 32'b00000000000000000000000000000000; // nop
ram[8] = 32'b00000000000000000000000000000000; // nop
ram[9] = 32'b00000000000000000000000000000000; // nop

## Slide 35: Get The Next PC
module getNextPC (PCSrc, currPC, offset, out);
parameter MIPS_PC_WIDTH_m1 = 7;
input PCSrc;
input [MIPS_PC_WIDTH_m1:0] offset;
input [MIPS_PC_WIDTH_m1:0] currPC;
output reg [MIPS_PC_WIDTH_m1:0] out;
always @(PCSrc, currPC, offset)
if (PCSrc == 0)
out <= currPC + 1;
else
out <= currPC + 1 + offset;
endmodule

## Slide 36: PC
module MIPSPC(clk, newPC, PC);
Just an 8-bit D-flip-flop.

## Slide 37: Register File
module MIPSREG(clk, RegWrite, ReadAddr1, ReadAddr2, WriteAddr, ReadData1, ReadData2, WriteData);
  Just as what specified in the book.
  RegWrite: If 0, disabling write. If 1, register WriteAddr register WriteAddr will be overwritten with WriteData.
  At any time, ReadData1 is the content of reg ReadAddr1, and ReadData2 is the content of reg ReadAddr2.

## Slide 38: ALU
module MIPSALU (ALUctl, A, B, ALUOut, Zero);
input [3:0] ALUctl;
input [31:0] A,B;
output reg [31:0] ALUOut;
output Zero;
assign Zero = (ALUOut==0); //Zero is true if ALUOut is 0; goes anywhere
always @(ALUctl, A, B) //reevaluate if these change
case (ALUctl)
0: ALUOut <= A & B;
1: ALUOut <= A | B;
2: ALUOut <= A + B;
6: ALUOut <= A - B;
7: ALUOut <= A < B ? 1:0;
12: ALUOut <= ~(A | B); // result is nor
default: ALUOut <= 0; //default to 0, should not happen;
endcase
endmodule

## Slide 39: Sign Extension
module SignExtend (in, out);
input [15:0] in;
output [31:0] out;
assign out[15:0] = in[15:0];
assign out[31:16] = in[15];
endmodule

## Slide 40: Two-to-one Selector
module STwoToOne32 (sel, in0, in1, out);
input sel;
input [31:0] in0, in1;
output reg [31:0] out;
always @(sel, in0, in1)
if (sel == 0)
out <= in0;
else
out <= in1;
endmodule

## Slide 41: Control
module MIPSCtrl (instr, RegDst, ALUSrc, MemToReg, RegWrite, MemWrite, MemRead, branch, ALUCtrl);
  Take the 32-bit instruction, generate the control signals.

## Slide 42: Data Path Setup According to

## Slide 43: Supported instructions
add, sub, addi, lw, sw, beq.

## Slide 44: Stepping through the program
The clock is set to be 200 time units. Run 200 every time.
Check the values of the wires in the waveform
Check the content of the registers and data memories in the memory windows.

## Slide 45: The waveform after two instructions
00100000000000000000000000000000; // addi $0, $0, 0
00100000001000010000000000000001; // addi $1, $1, 1

## Slide 46: Supporting a new instruction
With the current data path, can we support a new instruction?
lwr $rs, $rt, $rd
What it does is to read from data memory at $rs-$rt, and write it to $rd
Suppose its opcode is 000001.

## Slide 47: Supporting a new instruction
else if (instr[31:26] == 6'b000001) //lwr
begin
RegDst <= 1;
ALUSrc <= 0;
MemToReg <= 1;
RegWrite <= 1;
MemRead <= 1;
MemWrite <= 0;
branch <= 0;
ALUCtrl <= 4'b0110;
end