## Slide 1: Residue Codes for CORDIC and Neural Network
Tsung-Chu Huang
2019/04/06
VTTF@NCHU

## Slide 2: Outline
Introduction
  Why Residue? Why Neural Network?
  Modulo-based Codes:
    AN Codes
    Residue Number System
    Residue Codes
Previous Work
Proposed Techniques
  Low-cost & Fast Design of Logistic Function
  Design Rules for optimizing checking/cost
  Low-cost BRC for Conjugate Residue Codes
  Hybrid RNSC Based Neural Network for Self-Healing and Acceleration
Evaluations
Conclusions

## Slide 3: Introduction
Significance of Neural Network
PFLOPS Computation
  Acceleration
  Reliability
Fused Multiply-Adder
GPU or Vector Processors

## Slide 4: Arithmetic Operations in NN
Floating-Point Numbers can be easily represented by Fixed-Point Numbers with an Exponent.
Fixed-Point Numbers are isomorphic to 2’s Complement Integers.
Operations: Addition/Subtraction/Multiplication/Logistic
[1] J. Bouvrie. Notes on Convolutional Neural Networks. May 2014. http://people.csail.mit.edu/jvb/papers/cnn_tutorial.pdf.

## Slide 5: Introduction to CORDIC
Combinational Circuit without Buffer Registers
Adders with Buffer Registers
  Area reduction
  Detection Rate

## Slide 6: Digit Error (Fault) Model
L-digit Radix-r number system:
  , where
) digit Errors include L single errors.
The single error at the k-th digit:
Arithmetic Weight
  ,
  where , , and
  , i.e.,
Arithmetic Distance btw integers :
Example:
309
-) 190
= 299
= 119

## Slide 7: Symbol Table and Definitions
Symb | Definition | Example
 | prime numbers | ={2, 3, 5, 7, 11, 13, 17…}
, | positive integers | ={1, 2, …}
 | non-negative integers | ={0, 1, 2, …}
 | non-negative integers | ={0, 1, 2, …, }
 | 1’s complement with L bits | ={, …,, 1, …,
 | 2’s complement with L bits | ={, …, -1,, 1, …,
 | residue (class) of modulo | , i.e., 17-3 (mod m)
 | remainder, residue in a range | 
 | -bit 1’s complement repr. | ==
 | -bit 2’s complement repr. | ==
 | weight of | =
 | arithmetic distance btw & | =
Symb | Definition | Example
 | prime numbers | ={2, 3, 5, 7, 11, 13, 17…}
 | positive integers | ={1, 2, …}
 | non-negative integers | ={0, 1, 2, …}
 | non-negative integers | 
 | 1’s complement with L bits | 
 | 2’s complement with L bits | 
 | remainder, residue in a range | 

## Slide 8: Philosophy
RNS
Commutative
Closure
Associative
Identity
Inverse
Closure
Associative
Identity
Inverse
Commutative
Group
Distributive
Field
Commutative Ring
Ring
linear space
multiplicative space
CORDIC

## Slide 9: CRT: Chinese Residue Theorem
Given where . Find
CRT Algorithm: let , (in about 473)
Example:
  [Ans]
  We have
  modular multiplicative inverse can be solved in advance by
    Extended Euclidean Algorithm:  Reverse the steps to
    Euler Theorem: (mod )

## Slide 10: Garner’s Classification
Diamond conjectured the form for arithmetic should be an+b in 1955 [2].
Garner classified residue-related codes into
  Nonseparate codes:
  Separate codes:
  Include RNS
  ( )m means (mod m)
[2] J. M. Diamond, “Checking codes for digital computers,” IRE Correspondence, vol. 43, pp.487-488, Apr. 1955.
[3] H. L. Garner, "The residue number system," IRE Trans. Electronic Computers. vol. EC-8, pp.140-147, June 1959.
[4] H. L. Garner, "Error codes for arithmetic operations," IEEE Trans. Electronic Computers, vol. EC-15, pp. 763-770, Oct. 1966.

## Slide 11: Brown’s AN Codes for Adders
Brown proved ranges for SED and SEC in 1960[5].
AN Code
SED:
SEC: , and
Example: 71n Codes for r=2, b=0, L=35
  d(a = 71)3 with minimum error can have 483,939,977 integers. The redundancy is only 6.15 bits.
  Assume arithmetic operating result an=7,132 is with single bit error, we have error = 7,132 % 71 = 32 = and the corrected result will be 7,100/71 = 100.
[5] D. T. Brown, "Error detecting and correcting binary codes for arithmetic operations," IRE Trans. Electronic Computers, vol. EC-9, pp. 333-337, September 1960.
[6] W. W. Peterson, Error-Correcting Codes. New York: Wiley, and Cambridge, Mass.: M.I.T. Press, 1961

## Slide 12: Mandelbaum-Barrows Codes
A cyclic AN codes
Let radix , bound B=,
is prime, , and
, can represented
as and split into s
segments , then
If s=2, the residue
generator will be
[7] D. Mandelbaum, "Arithmetic codes with large distance," IEEE Trans. Information Theory, vol. IT-13, pp. 237-242, April 1967.
[8] Massey, J. L. and Garcia, O. N.: Error-correcting codes in computer arithmetic. In: Advances in Information Systems Science, Vol. 4, Ch. 5. (Edited by J. T. Ton). New York: Plenum Press, 1972.
p
B-1=ap=2L-1
/p
(mod 2L-1)
Residue
Codes
Checksum
Codes

## Slide 13: Residue Generators
Residue-to-Binary Converter (R2B, RBC, RG)
Light Modulus:
For CORDIC, light-weight multiplier
is called fine number.
Heavy Modulus:
  but the division is more complicate.
  Barrett Reduction Algorithm
  Basically an L-bit integer is precomputed.
  Then physical implementation of is easier.
[9] P. Barrett, “Implementing the Rivest Shamir and Adleman public key encryption algorithm on a standard digital signal processor,” Lecture Notes in Computer Science, Springer. (263)311–323, 1987.

## Slide 14: Burst Error Correction
k-Burst Errors:
  Eg. carry generating error for a series of contagious propagations
  Error ,
  were
Henderson Codes:
  detects k-burst errors
[10] D. S. Henderson, "Residue class error checking codes," Proc. 16th Natl. Meeting of the Association for Computing Machinery, Los Angeles, Calif., September 1961.
[11] R. T. Chien, "On linear residue codes for burst-error correction," in IEEE Transactions on Information Theory, vol. 10, no. 2, pp. 127-133, April 1964.

## Slide 15: Checksum vs. Residue Codes
Usas demoed pros/residue codes in inversion.
Aviz proposed 2D and cmp'd 2DxInvx(XS, Res)
Bose detailed 2D Residue Codes.
[12] Alan M. Usas, "Checksum Versus Residue Codes For Multiple Error Detection", IEEE Computer Society, Digest of Papers on the Eighth Annual International Conference on Fault-Tolerant Computing, p.224 (1978).
[13] T.-C. Huang. A Low-Power Dependable Berger Code for Fully Asymmetric Communication. IEEE Communications Letters, vol. 12, no. 10, pp.773-775, Oct. 2008.
[14] A. Avizienis and C. S. Raghavendra, "Applications for arithmetic error codes in large, high-performance computers," 1983 IEEE 6th Symposium on Computer Arithmetic, Aarhus, Denmark, 1983, pp. 169-173.
[15] B. Bose. 2-Dimensional Arithmetic Residue Check Codes. Comput. Math. Applic. Vol. 13, No. 5/6, pp. 547-554, 1987.
Checksum/Residue
Inversion
Dimensions
?

## Slide 16: Rao’s Biresidue Codes
Rao[16] proposed separate residue codes for shift() in
Tuazon proposed as a number system.
Double separate residues (Biresidues)[18] were proposed.
  Single Bit Error Correctable for
[16] T. R. N. Rao, "Error-checking logic for arithmetic-type operations of a processor," IEEE Trans. Computers, vol. C-17, pp.845-849, Sep. 1968.
[17] J. O. Tuazon. Residue number system in computer arithmetic. Dissertation, Iowa State U., 1969.
[18] T. R. N. Rao, “Biresidue Error-Correcting Codes for Computer Arithmetic,” Computers, IEEE Transactions on, vol. C-19, pp. 398–402, May 1970.
[19] D. K. Banerji, "On the Use of Residue Arithmetic for Computation," in IEEE Transactions on Computers, vol. C-23, no. 12, pp. 1315-1317, Dec. 1974.

## Slide 17: Conjugate-Type Biresidues
First proposed in [20] in Residue Number System (RNS).
  Moduli almost cover numbers.
  Since block codes are used in encryption, L-bit 0 will represent number .
  Diminished-1 Issue: number 0 will be constraint by other modulus.
Lai proposed RNS for Encryption [20].
Advantages of taking conjugate residue codes
  Product is still a light number.
  can be decomposed to nested primes.
Disadvantages
  Only 5 Fermat numbers.
[20] M. A. Soderstrand, W. K. Jenkins, G. A. Jullien, and F. J. Taylor. Residue Number System Arithmetic: Modern Applications in Digital Signal Processing. IEEE Press, New York, 1986.
[21] X. Lai and J. L.Massey. A proposal for a new block encryption standard. In Advances in Cryptology – EUROCRYPT’90, pages 389–404, Berlin, Germany: SpringerVerlag, 1990.

## Slide 18: 2’s Complement Residue Generators
Moduli for
, taking advantage of
is represented in , so as .
, if ,
Sign-extended and
If ,
In summary,
For modulo , if ,
In summary,
Note
  may appears as .
  needs bits.

## Slide 19: RNS for DSP/Encry with only
[22] Z. Wang et al, "An algorithm for multiplication modulo ," Proceedings of the 39th Midwest Symposium on Circuits and Systems, Ames, IA, USA, 1996, pp. 1301-1304 vol.3.
[23] A. Skavantzos et al, "New efficient RNS-to-weighted decoders for conjugate-pair-moduli residue number systems," 33th Asilomar Conference on Signals, Systems, and Computers, 1999.
[24] A. Skavantzos and M. Abdallah, "Implementation issues of the two-level residue number system with pairs of conjugate moduli," in IEEE Trans. Signal Processing, vol. 47, no. 3, pp. 826-838, March 1999.
[25] R. Zimmermann, "Efficient VLSI implementation of modulo addition and multiplication," Proceedings 14th IEEE Symposium on Computer Arithmetic (Cat. No.99CB36336), Adelaide, SA, Australia, 1999, pp. 158-167.
[26] J.-C. Bajard, and L. Imbert, "A full RNS implementation of RSA", IEEE Trans. Comput., vol. 53, no 6, pp. 769–774, June 2004.
[27] W. Hong, R. Modugu and M. Choi, "Efficient Online Self-Checking Modulo 2^n+1 Multiplier Design," in IEEE Transactions on Computers, vol. 60, no. 9, pp. 1354-1365, Sept. 2011.
ALU with only
Memory
CU
BRC
RBC

## Slide 20: RNS for Neural Network
[28] H. Nakahara and T. Sasao. "A deep convolutional neural network based on nested residue number system," 25th Int'l Conf. on Field Programmable Logic and Applications (FPL), London, 2015, pp.1-6.
[29] N. I. Chervyakov et al, "Increasing of convolutional neural network performance using residue number system," Int'l Multi-Conf. on Engineering, Computer and Information Sciences (SIBIRCON), Novosibirsk, 2017, pp. 135-140.
[30] S. Salamat, M. Imani, S. Gupta and T. Rosing, "RNSnet: In-Memory Neural Network Acceleration Using Residue Number System," 2018 IEEE International Conference on Rebooting Computing (ICRC), McLean, VA, USA, 2018, pp. 1-12.
[31] K. Phalakarn and A. Surarerks, "Alternative Redundant Residue Number System Construction with Redundant Residue Representations," 3rd Int'l Conf. on Computer and Communication Systems (ICCCS), Nagoya, 2018, pp. 457-461.
Modular
Multiplier
Residue
Adder
Residue
Generator
Binary
Residue
Converter
Residue
Binary
Converter
No residue-related technique applied in the activation function in the literature so far.
(Assume separated to s segments)

## Slide 21: Target Issues & Proposed Solutions
Nonlinear Operations
  Speedup & Cost-down for precise neural network:
  Magnitude Comparison inc. in softmax, max-pooling
  Right-Shifts in CORDIC and Sigmoid Activation Functions
BRC
Heavy RBC
  CRT Algorithm
  Modular Multiplicative Inverse
    Euler Theorem
    Extended Euclidean Theorem
    LUT
Optimized Moduli Set
 (1) Low-cost & Fast Design of Logistic Function
 (2) Design Rules for optimizing checking/cost
 (4) Hybrid RNSC NN Architecture
 (3) Low-cost BRC for Conjugate Residue Codes

## Slide 22: Low-Cost & Fast S. Activation Functions
Arithmetic for calculating
Taylor Series (1712)
Remez Algorithm (1934)
CORDIC (1956)
>1971
[32] J. E. Volder. Binary Computation Algorithms for Coordinate Ro-tation and Function Generation, Convair, Aeroelectronics group, IAR-1.148, 1956.
[33] NetLib Project. Freely Distributable C Math Library Supporting IEEE 754. http://www.netlib.org/fdlibm/, 2004.
[34] GNU. C Math Library. May 2018. https://code.woboq.org/us-erspace/glibc/sysdeps/ieee754/dbl-64/e_exp.c.html.
[35] J.S. Walther. A Unified Algorithm for Elementary Functions. in Proc. Spring Joint Computation Conference, 1971, pp.379-385.
[36] Quinapalus Inc. Calculate exp() and log() without Multiplications. https://www.quinapalus.com/efunc.html, 2018.
(1)

## Slide 23
y = logistic(x) =
Columbus's egg!
[37] T.-C. Huang et al. “Low-Cost and Fast Design of Precise Activation Functions in Neural Network” ICCE-TW2019, May 2019.
Low-Cost & Fast S. Activation Functions
// CORDIC for exp(x)
y = 1;
If (x>0) {
for (i=M; i>=0; i--) if((t = x +ln(1<<2i))>=0)
{x = t; y =2i;}
for(i=1; i<=N; i++) if((t = x – ln(1+2-i))>=0)
{x = t; y -= y i;} } }
else {
for (i=M; i>=0; i--) if((t = x – ln(1<<2i))>=0)
{x = t; y =2i;}
for(i=1; i<=N; i++) if((t = x – ln(1+2-i))>=0)
{x = t; y += y i;} } } }
← Proposed in ICCE-TW2019
← Conventional
(1)

## Slide 24: Considerations for Moduli Selection
Motivation: to promote checking rate and to cost down
Observation & Considerations:
  Light-Weight () Moduli make generating and checking easy.
  BRC: Light-Weight Moduli
  RBC: Light-Weight LCM of Moduli
  Conjugate formula: , , eq. can potentially reduce the hardware cost and/or promote the detection rate.
(2)

## Slide 25: Considerations for Moduli Selection
Observation & Considerations:
  When only is considered, should be 0 for SEC.
  E.g. 2, 3, 5, 7, 13, 17, 19, … (note 11 not)
  Fermat numbers. so far. (Eular defuted k=5)
  However has been shown with few factors, and few repetitive prime factors.
  A modulus with no repetitive prime factor can have the same detection rate.
  A 2’s complement integer can be cast as non-negative integer , all distinct except
  (, , ) is a 2L+2 bit number system, where and are , and is a zero flag implemented by a NOR gate.
  (, , , ) can correct single bit-errors, multiple faults at the same generators in a range, and self-checking with low aliasing rate from about to .
  Modulo- generators can share the same adders in time.
(2)

## Slide 26: Design Rules for optimizing checking/cost
Basic Rules
  Residue to nonlinear operations must be reserved or checking prior to RBC, otherwise upstream coverage will be lost.
  To check the nonlinear operations and to utilized the reserved residue, the residues should be encoded into the downstream linear binary operator.
Right Shifting:
  Not recommended because k-bit truncated errors.
  Right Shifting is usually combined with accumulator like .
For nonlinear operators with only pure RNS inputs
  RBC and Checking first
  Binary Operation
  Residue Operation
(2)
redundant
shiftable
remained or abandoned

## Slide 27: Right-Shifter and Adder
Independent Arithmetic for Left Shifting:
Shifted-Message Borrowed for Right Shifting:
  Although bits can be still self-shifted with discarded bits, when , all residue will be discarded.
  The last stage and the shifter are still under monitoring for checking.
RG
(2)

## Slide 28: Low-Cost BRC for Conjugate Residues
Radix 𝒓=𝟐, #segments=s=2, bound , ,
Let
𝒄𝒂𝒏 𝒔𝒉𝒂𝒓𝒆 𝒕𝒉𝒆 𝒂𝒅𝒅𝒆𝒓𝒔 𝒂𝒍𝒍 𝒕𝒚𝒑𝒆𝒔 𝒍𝒊𝒌𝒆 𝑪𝑺𝑨 𝒐𝒓 𝑪𝑳𝑨
A L-bit HF-based incrementer is designed for cyclically adding their carry.
Note that the longest critical-path for -bit adders is .
Theorem: the critical-path distance
  Proof:
  Let be the lowest generated carry, therefore we can have and its sum bit will be 0, that will kill the carry propagation through of the incrementer. QED.
(3)
FA
FA
FA
FA
FA
FA
FA
C
FA
HA
HA
HA
HA
HA
HA
HA
HA
0

## Slide 29: Proposed BRC for Reidue System
(3)

## Slide 30: Proposed RBC for 4-Reidue System
(3)
Note: are constant numbers
BRC

## Slide 31: Heuristics for Searching Optimized Moduli
Weight & Coprime-Weight of Composite Numbers
  Examples:
Given a typical NN, length of fixed-point numbers , activation (ReLU or tanh) and cost function:
  To balance operations, modulus sizes should be about in L bits.
  To have high speedup and area reduction, .
  Since RBC will dominate, when k moduli are chosen, binary numbers can be converted for checking. So there are few choices for , say , , , and .
  Self-Checking: . are selected.
  MMR correction: and is a good choice.
  Note that with minimized total weight.
  Weights: are selected.
(4)

## Slide 32: Consideration: Checking Schemes
Owing to that cost of RBC >> cost of BRC,
  Checking : check BRC() with
  Checking that can convert k binary numbers by subsets:
    Only Checking:
      Convert only one RBC(subset of ) = ,
      check BRC(𝑛) with other |𝑛|_(𝑚_𝑖 )
    Correction by Modular Redundancy
      Convert more than 4 , select the equal ones.
(4)

## Slide 33
S
RBC
tanh
CHK
BRC
BRC
BRC
BRC
BRC
S
RBC
tanh
CHK
S
RBC
tanh
CHK
S
RBC
tanh
CHK
S
RBC
tanh
CHK
Binary Number System
Binary Number System
Residue Number System
Hybrid Residue Number System for NN
(4)

## Slide 34
Impact-Relaxing Self-Healing Approach
(4)
0
1
AVG
S
RBC
tanh
CHK
upstream
soft error
downstream
soft error
Error

## Slide 35: Comparison
 | [28] | [29] | [30] | [31] | Ours
NN | CNN | CNN | DNN | CNN | NN784-16-10
RNS | 12 moduli | RNS | RNS | RRNS | {}
A. Overhead | ++ ??? | NA | NA | NA | - 58%
Power | NA | NA | ~ 50% | NA | NA
Accelerate | 6.8X | 37.4% | 35% | NA | + 147%
Activation | skipped unchecked | softmax unchecked | Taylor unchecked ReLU, checked | skipped unchecked | tanh, softmax, … checked
Checking | partial | partial | full / partial | partial | full
Self-healing | none | none | none | none | downstream branch
Majority | none | none | none | none | MMR
 | [28] | [29] | [30] | [31] | Ours
NN | CNN | CNN | DNN | CNN | NN784-16-10
RNS | 12 moduli | RNS | RNS | RRNS | 
A. Overhead | ++ ??? | NA | NA | NA | - 58%
Power | NA | NA | ~ 50% | NA | NA
Accelerate | 6.8X | 37.4% | 35% | NA | + 147%
Activation | skipped unchecked | softmax unchecked | Taylor unchecked ReLU, checked | skipped unchecked | tanh, softmax, … checked
Checking | partial | partial | full / partial | partial | full
Self-healing | none | none | none | none | downstream branch
Majority | none | none | none | none | MMR
[28] H. Nakahara and T. Sasao. "A deep convolutional neural network based on nested residue number system," 25th Int'l Conf. on Field Programmable Logic and Applications (FPL), London, 2015, pp.1-6.
[29] N. I. Chervyakov et al, "Increasing of convolutional neural network performance using residue number system," Int'l Multi-Conf. on Engineering, Computer and Information Sciences (SIBIRCON), Novosibirsk, 2017, pp. 135-140.
[30] S. Salamat, M. Imani, S. Gupta and T. Rosing, "RNSnet: In-Memory Neural Network Acceleration Using Residue Number System," 2018 IEEE International Conference on Rebooting Computing (ICRC), McLean, VA, USA, 2018, pp. 1-12.
[31] K. Phalakarn and A. Surarerks, "Alternative Redundant Residue Number System Construction with Redundant Residue Representations," 3rd Int'l Conf. on Computer and Communication Systems (ICCCS), Nagoya, 2018, pp. 457-461.

## Slide 36: Conclusions
We analyzed the cause/effect and pros/cons of the AN/RNS/Residues Codes
We proposed
  Low-cost & Fast Design of Logistic Function: 2/3 area & time saved.
  Design Rules for optimizing checking/cost
  Low-cost BRC/RBC for Light-Weight Residue Codes
  Hybrid RNSC Based Neural Network for Self-Healing and Acceleration
Future Work:
  Analysis and Synthesis Automation.
  RNS/VPA for High-Precision Application