## Slide 1: Data Flow Scheduling and High Level Synthesis
Tsung-Chu Huang
2020/11/28
TestLab, NCUE

## Slide 2: Outline
Introduction
  Why Residue? Why Neural Network?
  Modulo-based Codes:
    AN Codes
    Residue Number System
    Residue Codes
Previous Work
Proposed Techniques
  Low-cost & Fast Design of Logistic Function
  Design Rules for optimizing checking/cost
  Low-cost BRC for Conjugate Residue Codes
  Hybrid RNSC Based Neural Network for Self-Healing and Acceleration
Evaluations
Conclusions

## Slide 3: High Level Synthesis (HLS)
The process of converting a high-level description of a design to a netlist
  Input:
    High-level languages (e.g., C)
    Behavioral hardware description languages (e.g., VHDL)
    Structural HDLs (e.g., VHDL)
    State diagrams / logic networks
  Tools:
    Parser
    Library of modules
  Constraints:
    Area constraints (e.g., # modules of a certain type)
    Delay constraints (e.g., set of operations should finish in l clock cycles)
  Output:
    Operation scheduling (time) and binding (resource)
    Control generation and detailed interconnections

## Slide 4: High-Level Synthesis Compilation Flow
Lex
Parse
Compilation front-end
Behavioral Optimization
Intermediate form
Arch synth
Logic synth
Lib Binding
HLS backend
x = a + b  c + d
+
+

a
b
c
d
+
+

a
d
b
c

## Slide 5: Behavioral Optimization
Techniques used in software compilation
  Expression tree height reduction
  Constant and variable propagation
  Common sub-expression elimination:
  (e.g., x = (a+b)*(c+d) + c+d+e  g = c+d; x = (a+b)*g + g+e
  Dead-code elimination
  Operator strength/complexity reduction (e.g., *4  << 2)
Typical Hardware transformations
  Conditional expansion
    If (c) then x=A else x=B  If c not computable at t, but A, B are, then to reduce latency, compute A and B in parallel, then comp. x=(C)?A:B
  Loop expansion
    Instead of three iterations of a loop, replicate the loop body three times—this eliminates fsm control (simplifying this) and sometimes allows for more parallelism (when no inter-iteration dependency)
A
B
x
c

## Slide 6: Architectural Synthesis
Deals with “computational” behavioral descriptions
  Behavior as sequencing graph (aka dependency graph, or data flow graph DFG)
  Hardware resources as library elements
  Constraints on operation timing
  Constraints on hardware resource availability
  Other Costs: Storage as registers, data transfer using wires
Objective
  Generate a synchronous, single-phase clock circuit
  Might have multiple feasible solutions (explore tradeoff)
  Satisfy constraints, minimize objective:
    Maximize performance subject to area constraint
    Minimize area subject to performance constraints

## Slide 7: Schedule in Temporal Domain
Scheduling and binding can be done in different orders or together
Schedule:
  Mapping of operations to time slots (cycles)
  A scheduled sequencing graph is a labeled graph
+
NOP






+
<
-
-
NOP
1
2
3
4
+
NOP






+
<
-
-
NOP
1
2
3
4
Notes: In the left schedule, how many multipliers do we need? How many ALU’s?
What about the schedule on the right?

## Slide 8: Operation Types & Binding
For each operation, define its type.
For each resource, define a resource type, and a delay (in terms of # cycles)
b is a function that maps an operation to a resource type that can implement it
  b : V  {1, 2, ..., nres}.
More general case:
  A resource type may implement more than one operation type (e.g., ALU)
Resource binding:
  Map each operation to a resource with the same type
  Might have multiple options (different speed/power types)—module selection

## Slide 9: Schedule in Spatial Domain (Binding)
Resource sharing
  More than one operation bound to same resource
  Operations have to be serialized
  Can be represented using hyperedges (define vertex partition)
+
NOP






+
<
-
-
NOP
1
2
3
4
2 adders &
4 multipliers

## Slide 10: Scheduling and Binding
 Resource dominated
 Control dominated
Resource constraints:
  Number of resource instances of each type {ak : k=1, 2, ..., nres}.
Scheduling:
  Labeled vertices, e.g., f (v3)=1.
Binding:
  Hyperedges (or vertex partitions) b (v2)=adder1.
Cost:
  Number of resources  area
  Registers, steering logic (Muxes, Demuxes, busses), wiring, control unit
  Power (leakage plus dynamic)
Delay:
  Start time of the “sink” node
  Might be affected by steering logic and schedule (control logic): resource-dominated vs. ctrl-dominated

## Slide 11: Architectural Optimization
Optimization in view of design space flexibility
A multi-criteria optimization problem:
  Determine schedule f and binding b.
  Under area A, power P, latency l and cycle time t objectives
Traditional Goals:
  Min area: solve for minimal binding/resources
  Min latency: solve for minimum l scheduling
Order of scheduling and binding?
  Apply either one (scheduling, binding) first
  Do both together!

## Slide 12: Other Considerations: How Is the Datapath Implemented?
Assuming the following schedule and binding
Wires between modules?
Input selection
(mux’ing)?
How does binding / scheduling affect congestion?
How does binding / scheduling affect steering logic?
+






+
<
-
-
1
2
3
4
2 adders & 2 multipliers
Will this cause routing congestion?

## Slide 13: Min Latency Unconstrained Scheduling
Simplest case: no constraints, find min latency
Given set of vertices V, delays D and a partial order > on operations E, find an integer labeling of operations f: V  Z+ Such that:
  ti = f(vi).
  ti  tj + dj  (vj, vi)  E.
  l = tn – t0 is minimum.
Solvable optimally in polynomial time
Bounds on latency for resource constrained problems
ASAP algorithm used: topological order
ALAP algorithm also solves the problem optimally and polynomially

## Slide 14: ASAP Schedules
  Schedule v0 at t0=1 /* Note: delay d0 of v0 = 0*/.
  While (vn not scheduled)
    Select vi with all scheduled predecessors
    Schedule vi at ti = ASAP(vi) = max {tj+dj}, vj being a predecessor of vi (boundary/initial case t0=1): .
  Return tn.
2 adders &
4 multipliers
+
NOP






+
<
-
-
NOP
1
2
3
4
v0
vn
Sub-optimal in res. because of “jamming-up” effect

## Slide 15: ALAP Schedules
  Schedule vn at tn=l+1 (l is the latency constraint).
  While (v0 not scheduled)
    Select vi with all scheduled successors
    Schedule vi at ti = ALAP(vi) = min {tj} -di, vj being a successor of vi (boundary/initial case tn=l+1).
+
NOP






+
<
-
-
NOP
1
2
3
4
3 adders &
2 multipliers
v0
vn
Sub-optimal in res. because of “jamming-down” effect

## Slide 16: Resource Constraint Scheduling
Constrained scheduling
  General case NP-complete
  Minimize latency given constraints on area or the resources (ML-RCS)
  Minimize resources subject to bound on latency (MR-LCS)
Exact solution methods
  ILP: Integer Linear Programming
  Hu’s heuristic algorithm for identical processors/ALUs
Heuristics
  List scheduling
  Force-directed scheduling

## Slide 17: ILP Formulation of ML-RCS
Use binary decision variables
  i = 0, 1, ..., n
  l = 1, 2, ..., l’+1 l’ given upper-bound on latency
  xil = 1 if operation i starts at step l, 0 otherwise.
Set of linear inequalities (constraints), and an objective function (min latency)
Observations
  ti = start time of op i.
  is op vi (still) executing at step l?
?
Notes: - Make sure that you understand the

## Slide 18: Start Time vs. Execution Time
For each operation vi , only one start time
If di=1, then the following questions are the same:
  Does operation vi start at step l?
  Is operation vi running at step l?
But if di>1, then the two questions should be formulated as:
  Does operation vi start at step l?
    Does xil = 1 hold?
  Is operation vi running at step l?
    Does the following hold?
?

## Slide 19: Operation vi Still Running at Step l ?
Is v9 running at step 6?
  Is x9,6 + x9,5 + x9,4 = 1 ?
Note:
  Only one (if any) of the above three cases can happen
  To meet resource constraints, we have to ask the same question for ALL steps, and ALL operations of that type
v9
4
5
6
x9,4=1
v9
4
5
6
x9,5=1
v9
4
5
6
x9,6=1

## Slide 20: Operation vi Still Running at Step l ?
Is vi running at step l ?
  Is xi,l + xi,l-1 + ... + xi,l-di+1 = 1 ?
vi
l
l-1
l-di+1
...
xi,l-di+1=1
vi
l
l-1
l-di+1
...
xi,l-1=1
vi
l
l-1
l-di+1
...
xi,l=1
. . .

## Slide 21: ILP Formulation of ML-RCS (cont.)
Constraints:
  Unique start times:
  Sequencing (dependency) relations must be satisfied
  Resource constraints
Objective: min cTt.
  t =start times vector, c =cost weight (e.g., [0 0 ... 1])
  When c =[0 0 ... 1], cTt =
Notes: How can we graphically depict a resource constraint inequality?
How will the resource constraint inequality change if all operations have unit delay?
What does it mean to set c=[1 1...1]?
  What will cTt look like?
  What schedule do we get?

## Slide 22: ILP Example
Assume l = 4
First, perform ASAP and ALAP
  (we can write the ILP without ASAP and ALAP, but using ASAP and ALAP will simplify the inequalities)
+
NOP






+
<
-
-
NOP
1
2
3
4
+
NOP






+
<
-
-
NOP
1
2
3
4
v2
v1
v3
v4
v5
vn
v6
v7
v8
v9
v10
v11
v2
v1
v3
v4
v5
vn
v6
v7
v8
v9
v10
v11

## Slide 23: ILP Example: Unique Start Times Constraint
Without using ASAP and ALAP values:
Using ASAP and ALAP:

## Slide 24: ILP Example: Dependency Constraints
Using ASAP and ALAP, the non-trivial inequalities are: (assuming unit delay for + and *)

## Slide 25: ILP Example: Resource Constraints
Resource constraints (assuming 2 adders and 2 multipliers)
Objective:
  Since l=4 and sink has no mobility, any feasible solution is optimum, but we can use the following anyway:

## Slide 26: ILP Formulation of MR-LCS
Dual problem to ML-RCS
Objective:
  Goal is to optimize total resource usage, a.
  Objective function is cTa , where entries in c are respective area costs of resources
Constraints:
  Same as ML-RCS constraints, plus:
  Latency constraint added:
  Note: unknown ak appears in constraints.

## Slide 27: Hu’s Algorithm
Simple case of the scheduling problem
  Operations of unit delay
  Operations (and resources) of the same type
Hu’s algorithm
  Greedy
  Polynomial AND optimal
  Computes lower bound on number of resources for a given latency OR: computes lower bound on latency subject to resource constraints
Basic idea:
  Label operations based on their distances from the sink
  Try to schedule nodes with higher labels first (i.e., most “critical” operations have priority)

## Slide 28: Hu’s Algorithm (ML-RCS prob. w/ all opers the same)
  HU (G(V,E), a) { // a is the # of available resources
  Label the vertices // label = length (i.e., delay) of longest path starting from the vertex
  l = 1
  repeat {
  U = unscheduled vertices in V whose predecessors have been scheduled (or have no predecessors)
  Select S  U such that |S|  a and labels in S are maximal /* a is the upper bound on # res. */
  Schedule the S operations at step l by setting ti=l, i: vi  S.
  l = l + 1
  } until vn is scheduled.
  }

## Slide 29: Hu’s Algorithm: Example
a = 3
(a)
(b)
(c)
(d)
Distance
from sink
Node label

## Slide 30: Hu’s Algorithm
[©Dutt]
Why is Hu’s optimal for all operations of the same type?
First note: In our earlier heuristic of breaking ties, the situation of two competing operations u1, u2 w/ the same label (distance to sink) having sibling output times to the most-critical children that affect the availability of their children w1, w2 differently will never occur, as all opers w/ higher labels than w1, w2 will be scheduled before either of w1, w2 (by the algorithm + all opers being the same type, this is also possible w/o wasting resource/FU execute cycles), making it possible to schedule w1, w2 at the same cc based on both the algorithm (note that w1, w2 also have the same label) and availability of resources (any of which w1, w2 can be scheduled on, as they are all of the same type—this may not be the case if w1, w2 are of different types , as then it is possible for an FU for one to be available when w1, w2 are, but not for the other).
We can prove by induction on the label of two nodes u1, u2 that if only one FU is available, scheduling either on it will result in the same solution in terms of the final latency (the induction step for label l = k is shown in the figure below). This argument can then be extended by a double induction on the number of nodes that have the same label and a triple induction on the number FUs available for them.

## Slide 31: Hu’s Algorithm
[©Dutt]
k
k
k-1
k-1
0
>=k
>=k
u1
u2
w2
w1
y
x
sink
We prove only the tied label part: Given only one FU (in
general, a limited number) we will get the same latency irrespective of which node we schedule first.
Proof Outline: Assume true for node labels < k (easy to prove base case, dist=1)
One FU avail for u1 and u2, both being avail @ time ti (which is latency so far).
There exists at least one child w1 of u1 and w2 of u2 w/ labels k-1.
If after scheduling u1 @ ti, w1 becomes available at tj > ti along w/an FU for it, then w2 will also become available along with an FU for it @ tj. This is because the same set of opers have to be scheduled on the same FU before w1, w2 can be available w/ an FU for them, are exactly the same.
Further, if u2 instead of u1 is scheduled at ti, the situation wrt availability of w1, w2 along w/ an FU available for them will also be at the same time tj as above as again, exactly the same set of opers will need to be scheduled as in the above case before w1 and w2 are available along with an FU for them.
If only one FU is available for w1, w2 (both have label k-1) at tj in either of the above cases, we will be optimal irrespective of whether we schedule w1 or w2 on it, according to the induction hypothesis for labels <= k-1

## Slide 32: List Scheduling
Greedy algorithm for ML-RCS and MR-LCS
  Extended Hu-type scheduling
  Does NOT guarantee optimum solution
Similar to Hu’s algorithm
  Operation selection decided by criticality
  O(n log n ) time complexity
More general input
  Resource constraints on different resource types

## Slide 33: What makes the general problem more difficult? (added by Shantanu Dutt)
Analysis for ML-RCS problem. Resources: 1 + (1 cc) , 1 X (2 cc), 1 div (3 cc) (“a” is now a vector (1, 1, 1), where each elt. corresponds to the # of avail. res. of each type
(b) Better scheduling w/ lookahead of resource-based earliest schedule time (REST) for successors given current sched. & binding, and res. avail. in the future. In a “competitive” (e.g., tie-breaking) situation, can schedule an oper. u later if it is not going to affect any *critical* successor’s sched. time (both top-level +’s have the same label: sched. + pred. of div first as divider avail in cc 2, whereas a mult. is unavail. for X succ. of competing +  REST of this X is later (3) than REST of the div. (2))
Ans. Different res. types w/ diff. delays  not all of them may be used or avail. together in each cc (unlike in Hu’s case—assuming enough available nodes)  when res’s avail and how efficintly they are use [min. idling] depends on sched. decisions  more room for better optimization techniques (larger opt. space)
6
1 (cc)
+
+
X
div
+
X
X
+
div
5
4
2
5
4
1
4
3
2 (cc)
nop
5 (cc)
6 (cc)
9 (cc)
L = 8 cc
(a) Hu-type scheduling
Distance
label
3 (cc)
+
+
X
div
+
X
X
+
div
5
4
2
5
4
1
4
3
nop
6
1 (cc)
2 (cc)
3 (cc)
5 (cc)
8 (cc)
L = 7 cc
Sched. time

## Slide 34: A lookahead heuristic for ML-RCS scheduling (added by Shantanu Dutt)
REST determination: Begin
If u is an i/p node (no parent other than V0), then rest(u) = 1.
For k = 2 to d /* d is the last level */ do
For each node w of type r in level k do
  connect w to ar nodes of the same type as w of level < k and w/ the largest values of rest, where ar is the # of res. of type r. If there are no such nodes, connect to dummy oper. node of type r (rest of dummy node = 1, delay = 0). these are w’s resource parent nodes.
  rest(w) = max{min{rest of the res. parent node u of w + d(u)}, asap(w)}, where (d(u)=delay of u).
  e-rest(w) = rest(w) /* defn. below*/
For k = d to 1 do
For each node w of type r in level k do
  update the effective rest, e-rest of each u that is a dfg parent of w, as max{rest(u), min over all children w’s (e-rest(w)) – d(u))}, and if the rest changes, propagate up to u’s dfg parents and so on.
End for
End for
End
New heuristic: Schedule nodes w/ highest path-distance label breaking ties in favor of those w/ a lower (i.e., earlier) e-rest.
Note that the rest values are used to determine initial e-rest that are then updated based on e-rest of children nodes.
Analysis for ML-RCS problem. Resources: 1 + (1 cc) , 1 X (2 cc), 1 div (3 cc) (“a” is now a vector (1, 1, 1), where each elt. corresponds to the # of avail. res. of each type
6
+
+
X
div
+
X
X
+
div
5
4
2
5
4
1
4
3
2 (cc)
nop
Longest
path
label
1  2
1
1
3
div
2
3  4
5
4  5
5
Res. dependency arcs (blue)
dummy
oper.
node
REST w/
update ro E-REST
Fig. 2: The REST concept also takes care of other non-res. based scheduling priority by propagating the asap of children w up to parents u as rest(u) = asap(w) – d(u). Here d(u) = 2 for all nodes
Fig. 1: Example of the REST & E-REST (in red italics)
computation & resulting scheduling
u
w
asap, rest =3,
path length = 7
asap, rest = 4
asap,
e-rest = 6
e-rest:6-2 = 4
Exploit the gap by delaying sched. of u to after c if there is a tie in path length w/ u & other opers @ c, and res. are limited—it does not help latency min. to sched. u at c
u
v
rest(u) = i,
path length
label = p,
current cc for sched. = c < j – d(u)
rest (v)= j
(cannot be
sched.
before j)
gap =
j – (c+d(u))
Fig. 3: Exploiting the REST gap
v
asap,
e-rest = 5
asap,
rest=3
asap,
rest = 3,
path
length
= 7
Give priority to scheduling v over u when there is competition between them for a resource—it does not help improve latency by scheduling u first, but helps by scheduling v first due to the lower rest value for u

## Slide 35: List Scheduling Algorithm: ML-RCS
  LIST_L (G(V,E), a) { // a is a vector of avail. res. of each type
  Compute the ALAP times tL w.r.t. an upper bound latency L. /* alap times “inverse” of but correlated to max-path-delay or length label */
  l = 1 // the current cc
  repeat {
  for each resource type k {
  Ul,k = available vertices in V.
  Tl,k = operations in progress.
  Compute the slacks { si = tiL - l,  vi Ul,k }.
  /* Note slack also is inv. prop. to length label */
  Select minimal slack Sk  Ul,k such that
  |Sk| + |Tl,k|  ak /* break ties arbitrarily */
  Schedule the Sk operations at step l
  }
  l = l + 1
  } until vn is scheduled.
  } // Note: Does not do lookahead using e-rest as in the prev. example. Can do so for a better ML-RCS algorithm, i.e., choose opers to schedule w/minimal e-rest rather than minimal slack.

## Slide 36: List Scheduling Example
Resource constraints: 3 X’s (2 cc), 1 + (1 cc). Avail. opers ar shown by rectangles
CC 4
CC 5
CC 6
(d) CC 4-6
*
(c) CC 3
*
(a) CC 1
*
(b) CC 2
*

## Slide 37: List Scheduling Algorithm: MR-LCS
  LIST_R (G(V,E), l) { // l is the latency constraint
  a = 1 // vector a has 1 res. of each type
  l = 1 // the current cc
  Compute the ALAP times tL w.r.t. l. /* alap times “inverse”of but correlated to max path delay/length label */
  if t0L < 0
  return (not feasible)
  repeat {
  for each resource type k {
  Ul,k = available vertices in V.
  Compute the slacks { si = tiL - l,  vi Ul,k }.
  Schedule operations with zero slack, update a
  Schedule additional Sk  Ul,k w/ minimal slack
  under current avail. in a /* break ties arbitrarily */
  }
  l = l + 1
  } until vn is scheduled.
  }

## Slide 38: List Scheduling Example
Latency constraint: 7cc’s; Start w/ 1 + (1 cc); 1 X (2 cc’s)
nop
alap= 8
7
7
7
6/5
5/4
6
5
4
2/1
2/1
3/2
nop
Alap= 8
7
7
7/5
6
5/3
6
5
4
2
2/0
3/1
1
1
1
1
2
2
6
a = (1, 1)
a = (1, 2)
alap
slack
+1cc
+1cc
CC 1
CC 2
+
X
nop
Alap= 8
7
7
7
5/2
6
5
4
2
2
3/0
1
1
2
2
a = (1, 2)
CC 3
nop
Alap= 8
7
7
7
5/1
6
5
4/0
2
2
3
1
1
2
2
a = (1, 2)
CC 4
: Scheduled
: Running
: Done
L
E
G
E
N
D
+1cc

## Slide 39: List Scheduling Example
Latency constraints: 7cc’s; Start w/ 1 + (1 cc); 1 X (2 cc’s)
nop
Alap= 8
7
7
7
5/1
6
5
4/0
2
2
3
1
1
2
2
a = (1, 2)
CC 4
: Scheduled
: Running
: Done
L
E
G
E
N
D
nop
Alap= 8
7
7
7
5/0
6
5/0
4
2
2
3
1
1
2
2
a = (1, 3)
CC 5
+1cc
nop
Alap= 8
7
7
7
5/0
6/0
5/0
4
2
2
3
1
1
2
2
a = (1, 3)
CC 6
nop
Alap= 8
7/0
7/0
7
5/0
6/0
5/0
4
2
2
3
1
1
2
2
a = (2, 3)
CC 7
+1cc
+1cc

## Slide 40: Backtracking List Scheduling Algorithm: MR-LCS
[©Dutt]
Fan-in
tree of u
u
w
u
Just sched. node u & v w/ additional res. (+2 mults)
move pred. w
up by 2 cc’s
move u up
by 2 cc’s
v
w
+ 2 mults
+ 1 mult
if w is oper.
OR
+1 mult & +1 add if w is “+” oper
w
u
v
Idea:
Backtrack an individual oper. whenever it is scheduled on a new FU to improve usage of new FU (allocate the new FU earlier)
In above ex, backtrack u, v separately up to their asap’s from scheduled cc that results in no extra FU allocation. Note that this may lead to extra allocation of other FU types.
Issue is also how much to backtrack u? Try all possibilities from (current cc -1) to asap(u)?
  Sometimes results in scheduling u at an earlier time on an existing FU. This can occur at the expense of increasing count of some other FU type (type of a parent or some ancestor), and we do if the total cost of other increased FUs < cost of a single FU of u’s type
  Other times, it cannot decrease # of FUs of u’s type, but increases utilization of the new FU as it is assigned earlier at the time the u could be backtracked to. This new FU can be re-used for another oper. in the current or future cc and can decrease # of FUs needed (of u’s type) later. If we cannot determine if u’s BT is going to decrease the # of FUs of u’s type, this BT should only be done of no new FU of another type needs to be allocated due to u’s BT.
Take the best of the best solns for backtracking u, v, and original soln. w/o backtracking, breaking ties in favor of the BT solution (as FU’s will be less idle  there can be advantages in later cc’s)

## Slide 41: Backtracking List Scheduling Algorithm: MR-LCS
  LIST_R_BT (G(V,E), l’) {
  a = 1, l = 1
  Compute the ALAP times tL.
  if t0L < 0
  return (not feasible)
  repeat {
  for each resource type k {
  Ul,k = available vertices in V.
  Compute the slacks { si = tiL - l,  vi Ul,k }.
  Schedule operations with 0 slack, upd. a
  if a(k) is increased by an amount m > 0 {
  for each oper just scheduled {
  Backtrack along its fan-in tree to re-schedule itself its max-arrival time
  pred. as earlier as possible w/o increasing overall cost;
  Mark this oper. if CD = cost(res. k) - added cost of extra res. of
  other types needed for this >= 0;
  }
  Let S = the marked opers that have the highest m CDs
  for each oper in S in order of decreasing CDs {
  re-scheduled its fan-in tree as determined by above backtracking;
  /* may need to resolve conflicts w/ previous backtrackings */
  update a
  }
  } /* if */
  Schedule additional Sk  Ul,k w/ minimal slack under a constraints
  } /* for */
  l = l + 1
  } until vn is scheduled.
  }
[©Dutt]
Fan-in
tree of u
u
w
u
Just sched. node u & v w/ additional res. (+2 mults)
move pred. w
up by 2 cc’s
move u up
by 2 cc’s
v
w
+ 2 mults
+ 1 mult
if w is oper.
OR
+1 mult & +1 add if w is “+” op
w
u
v

## Slide 42: List Scheduling w/ Backtrack
Latency constraints: 7cc’s; Start w/ 1 + (1 cc); 1 X (2 cc’s)
nop
alap= 8
7
7
7
6/5
5/4
6
5
4
2/1
2/1
3/2
nop
Alap= 8
7
7
7/5
6
5/3
6
5
4
2
2/0
3/1
1
1
1
1
2
2
6
a = (1, 1)
a = (1, 2)
alap
slack
+1cc
-1cc (BT)
CC 1
CC 2
+
X
nop
Alap= 8
7
7
7
5/4
6
5
4
2/1
2/1
3/2
1
1
2
2 1
a = (1, 2)
CC 1
nop
Alap= 8
7
7
7
5/3
6
5
4/2
2
2
3/1
1
1
2
1
a = (1, 2)
CC 2
: Scheduled
: Running
: Done
L
E
G
E
N
D
+1cc
Sched cc
Schedule oper.
earlier in cc 1 via BT

## Slide 43: List Scheduling w/ Backtrack
Latency constraints: 7cc’s; Start w/ 1 + (1 cc); 1 X (2 cc’s)
: Scheduled
: Running
: Done
L
E
G
E
N
D
nop
Alap= 8
7
7
7
5/2
6
5
4/1
2
2
3/0
1
1
2
1
a = (1, 2)
CC 3
3
3
nop
Alap= 8
7
7
7
5/0
6/1
5/0
4
2
2
3
1
1
2
1
a = (1, 2)
CC 5
3
3
5
5
5
+2cc
nop
Alap= 8
7
7
7
5
6
5
4
2
2
3/0
1
1
2
1
a = (1, 2)
CC 6
3
3
5
5
5
+1cc
nop
Alap= 8
7/0
7/0
7
5
6
5
4
2
2
3
1
1
2
1
a = (2, 2)
CC 7
3
3
5
5
5
7
7
Note: No 3’rd X FU needed here unlike in the non-BT method.
@ 3
@ 5
@ 5
@ 3
@ 3
@ 5
@ 7
sched. time

## Slide 44: List Scheduling w/ Backtrack
Latency constraints: 7cc’s; Start w/ 1 + (1 cc); 1 X (2 cc’s)
: Scheduled
: Running
: Done
L
E
G
E
N
D
nop
Alap= 8
7/0
7/0
7
5
6
5
4
2
2
3
1
1
2
1
a = (2, 2)
CC 7
3
3
5
5
5
7
7
Backtracking from either of the 2 scheduled +/- nodes to try to schedule either 1 cc earlier (in order to reduce # of +’s), results in 1 extra X needed, resulting in a = (1,3) which is more expensive. So this (a = (2,2)) is the best soln. we can obtain using targeted backtracking
However, if X and + opers were interchanged in the dfg the above BT will result in a less expensive solution
X
more mults needed for
both these BTs
pred. sched.
asap time; can’t
be moved up
@ 3
@ 5

## Slide 45: List Scheduling w/ Backtrack
Latency constraints: 7cc’s; Start w/ 1 + (1 cc); 1 X (2 cc’s)
: Scheduled
: Running
: Done
L
E
G
E
N
D
Assuming + is more expensive than X (or subst. all +/-/> opers by
“div”; which is more expensive than X).
nop
Alap= 8
7/0
7/0
7
5
6
5
4
2
2
3
1
1
2
1
a = (2, 2)
CC 7
3
3
5
5
5->4
7
7 -> 6
Max overlapping
X opers
Backtrack along right + oper:
1 extra X needed; a = (1,3). Note that left – oper cannot be backtracked as its – parent is already scheduled at its asap and cannot thus be backtracked.

## Slide 46: Force-Directed Scheduling
Developed by Paulin and Knight [DAC87]
Similar to list scheduling (LS)
  Can handle ML-RCS and MR-LCS
  For ML-RCS, schedules opers step-by-step, but not necessarily in order of increasing cc’s (from 1 to last), as in the LS algorithms.
  BUT, selection of the operations tries to find the globally best set of operations
Difference with list scheduling in selecting operations
  Select operations with least force
  Consider the effect on the type distribution
  Consider the effect on successor nodes and their type distributions
Idea:
  Find the mobility mi = tiL – tiS of operations
  Look at the operation type probability distributions
  Try to flatten the operation type distributions: minimize the max probabilistic resource usage at every step of scheduling
ALAP time
ASAP time

## Slide 47: Force-Directed Scheduling
Rationale:
  Reward uniform distribution of operations across schedule steps
Force
  Used as a priority function
  Related to concurrency – sort operations for least force
  Mechanical analogy: Force = constant x displacement
    Constant = operation-type distribution value (DG value for that operation tpe and cc)
    Displacement = change in probability
Definition: operation probability density
  pi ( l ) = Pr { vi starts at step l }.
  Assume uniform distribution:

## Slide 48: Force-Directed Scheduling: Definitions
Operation-type distribution (gives probabilistic avg. # of FUs needed in cc l)
Operation probabilities over control steps:
Distribution graph of type k over all steps:
  qk ( l ) can be thought of as expected or average operator cost for implementing operations of type k at step l.
….
….

## Slide 49: Force-Directed Scheduling
Control/Time steps l for type-k FUs/opers
qk(l).
Control/Time steps l for type-k FUs/opers
qk(l)
(a) A very non-uniform ave. “occupancy rates” qk(l). of diff. time steps for type-k opers.  more congestion in time step  more FUs needed to solve the problem in a given time (bad for MR-LCS). Note how this alleviates the jamming effects is asap, alap as well as list scheduling for MR-LCS. It also means that for a given res. constraint, the congested time steps will need to be “spread out” into more time steps  more the peak pr congestion on a time step being spread out, more the time for opers to complete (bad for ML-RCS)
(b) A more uniform ave. “occupancy rates” qk(l). of diff. time steps for type-k opers. that alleviates both of the problems stated for a highly non-uniform distribution
The main idea of FD scheduling is to schedule in a way that gradually transforms a highly non-uniform time-step occupancy rate distribution to a more uniform one. This is accomplished by scheduling opers in time slots (within their mobility range) that has the least force (max. reduction of non-uniformity) for them and their child/successor opers.

## Slide 50: Example: MR-LCS, l = 4
+
NOP






+
<
-
-
NOP
1
2
3
4
2.83
2.33
.83
0
1
2
1.66
0.33
Note: Too approx. If prec. constr. taken into account, should be 1/3 + 1/3 = 0.66
With prec. constr. should be
1 + 1/3 + 1/3 = 1.66

## Slide 51: Forces
Self-force
  Sum of forces to other steps
  Self-force for operation vi in step l
  Force(l) =
  dlm = 1 when l = m, and 0 otherwise
  dlm – pi(m) is the change in the prob. contribution of vi to qk(m)
  qk(m) is the “weight” of the change
Successor/Predecessor-force
  Related to scheduling of the successor/predecessor operations
  For example, delaying an operation may cause the delay of its successors (shrinking of their mobility ranges [MRs] and mobilities and thus increase in qk values in their new MRs)
  Similar formulation: S over all affected k’s, m’s qk(m)*Dqk(m)

## Slide 52: Example: operation v6
Multiply
Add
v6 can be scheduled in the first two steps
  p(1) = p(2) = 0.5, p(3) = p(4) = 0.0
Distribution: q(1) = 2.8, q(2) = 2.3
Assign v6 to step 1
  Variation in probability of step 1: 1 – 0.5 = 0.5
  Variation in probability of step 2: 0 – 0.5 = -0.5
Self-force: 2.8 x 0.5 - 2.3 x 0.5 = 0.25
No change in successors’ MRs and no predecessors, so p/s forces = 0
qmult(l)
qadd(l)
l
l

## Slide 53: Example: operation v6
Multiply
Add
Assign v6 step 2
  Variation in probability: 0 – 0.5 = -0.5
  Variation in probability: 1 – 0.5 = 0.5
Self-force: 2.8 x -0.5 + 2.3 x 0.5 = -0.25

## Slide 54: Example: operation v6
Multiply
Add
Successor-force
  Operation v7 assigned to step 3
  2.3(0 – 0.5) + 0.8(1 – 0.5) = -.75
Total-force = -1
Conclusion
  Least force is for step 2
  Assigning v6 to step 2 reduces concurrency, force, but
  increases utilization

## Slide 55: FD Scheduling – An example (another view)
Calculate the force with the operation x’ in control-step 1. DG(i) here is the same as qk(i).
DG(1) = 2.833 ; DG(3) = 0.833
DG(2) = 2.333 ; DG(4) = 0
Poor utilization
= Diff. in DG(i) of sched. time step j from the average DG(j) over the MR of the current oper. v. Note the denominator 2 above will in general be replaced by m+1, where m is the mobility range of v
Assigning to a time j step w/ DG(j) > avg. DG (i.e., +ve force) skews the non-uniform distribution even more—not desirable
Manipulation of previous force eqn. gives us:

## Slide 56: FD Scheduling – An example (another view)
Calculate the force with the operation x’ in control-step 2. (succ. oper. x’’ must be pushed to control-step 3)
DG(1) = 2.833 DG(3) = 0.833
DG(2) = 2.333 DG(4) = 0
Good utilization
Direct force (calculated as before)
Indirect force (on x’’ in control-step 3)

## Slide 57: FD Scheduling
By repeatedly assigning operations to various
control-steps and calculating the force associated
with the choice, several force values will be available.
The Force-directed scheduling algorithm chooses
the assignment with the lowest force value, which
also balances the concurrency of operations most
efficiently.

## Slide 58: Force Directed Scheduling Algorithm
/* i.e., mobility ranges */
in the time step

## Slide 59: Conclusion
ILP – optimal, but exponential worst case runtime
Hu’s
  Optimal and polynomial
  Only works in restricted cases
List scheduling
  Extension to Hu’s for general case
  Greedy (fast) but suboptimal
  REST parameter incorporation can make LS much better for both ML-RCS and MR-LCS
Force directed
  More complicated than list scheduling algorithm
  Take into account more global view of the scheduling options
  Globally greedy (locally greedy—greedy within each cc)
  Complexity?
  Note again: MR-LCS and ML-RCS are NP-hard
  Still suboptimal—why?

## Slide 60: To Probe Further...
Linear programming
  http://www.cs.sunysb.edu/~algorith/files/linear-programming.shtml
Linear programming tools
  http://www-unix.mcs.anl.gov/otc/Guide/faq/linear-programming-faq.html
Automatic compilation of pipelined designs
  T. Maruyama and T. Hoshino, “A C to HDL Compiler for Pipeline Processing on FPGAs”, IEEE Symposium on FPGAs for Custom Computing Machines (FCCM), pp. 101-110, 2001.