## Slide 1: Pynq System Installation
Tsung-Chu Huang (黃宗柱)
Electronics Eng., NCUE
TestLab, NCUE
2022/1/8

## Slide 2: Outline
Installation of Xilinx PYNQ System
Pynq-z1/2 Setup
USB-COM Installation
  for Zynq-7020 (FPGA) Bitstream Programming
    Using ISE or SDK
  for A9 + Pynq (Embedded System) Bitstream Downloading
    Terminal for Linux with Kernel Python/C
    Vivado (+SDK) Bitstream Downloading library
RJ45-CAT5e-RJ45 Ethernet Installation
  Desktop of Ubuntu 18.04 (Heavy)
  Jupyter Lab (Light) with File Upload/Download
  Terminal
SAMBA (SMB)
  FTP through File Manager in Windows

## Slide 3: Installation of Xilinx PYNQ System
download files
https://drive.google.com/drive/folders/1EZG40mE2-NDZH9r5QzjHjP5nreGNSJvw?usp=sharing
  Image file:
    https://digilent.com/reference/programmable-logic/pynq-z1/start
    http://www.e-elements.com.tw/products/fpga_system/xup_pynq/pynq-z2/
  Image writer:
    https://sourceforge.net/projects/win32diskimager
Steps:
  For Formatted SD
    Unzip the image
    Write to a blank MicroSD (>8G, looked as a FAT32 USB HD) using
  For Unformatted SD with the same partition
    Click SD in File Manager, Format to FAT32 in Content
  For SD with wrong partition:
    Enter DOS by cmd, > DISKPART
      help
      list disk (e.g., disk 4)
      select disk 4
      clear
      create partition primary
      format fs=fat32
      exit

## Slide 4: Pynq-z1/2 Setup
Configure PuTTY Terminal in PC:
SD  JTAG
Boot from SD,
or program from JATAG
Power from USB/REGulator
Insert microSD
Connect microUSB
Turn On
Open Device Manager
Check COM#
Turn off/on and PuTTY to browse Booting:
Activating Ethernet
DCHP Server
> uname –a
SAMBA
> who
ttyPS0  COM4 connected
xilinx@pynq:~$ ifconfig
eth0: flags=4099<UP,BROADCAST,MULTICAST> mtu 1500
. . . .
eth0:1: flags=4099<UP,BROADCAST,MULTICAST> mtu 1500
inet 192.168.2.99 netmask 255.255.255.0 broadcast
COM PuTTY
Check iNet IPv4

## Slide 5: Review on Typical Settings
Booted from SD
SD
Micro-USB
RJ45
COM
LAN
Power On
Power
source:
USB

## Slide 6: Connect the Internet for File Transfer
RALink WiFi RT5370
RJ45
USB
RJ45
Manual
switch
USB-RJ45 LAN
USB Hub
③
②
①
④

## Slide 7: High-Level Embedded System Design
SW
Python
C++
Verilog
PC
FPGA
HW
HW
FPGA
Pynq
PC
HLS
SDK
IPI
Vivado